COS Prelaunch Calibration Data

| Date: | March 13, 2008 |
| --- | --- |
| Document Number: | COS-01-0008 |
| Revision: | Revision A |
| Contract No.: | NAS5-98043 |
| CDRL No.: | AV-04 |

| Prepared By: | Dr. Erik Wilkinson |  | 5/14/04 |
| --- | --- | --- | --- |
|  | Dr. E. Wilkinson, COS Project Scientist, CU |  | Date |
| Reviewed By: | Dr. Dennis Ebbets |  | 5/14/04 |
|  | Dr. D. Ebbets, COS Calibration Scientist, BATC |  | Date |
| Reviewed By: | Dr. Ken Brownsberger |  | 5/14/04 |
|  | Dr. K. Brownsberger, COS Experiment Manager, CU |  | Date |
| Approved By: | Dr. James Green |  | 5/3/04 |
|  | Prof. J. C. Green, COS Principal Investigator, CU |  | Date |
| Approved By: | Tom LaJeunesse |  | 5/14/04 |
|  | Mr. Tom LaJeunesse, COS Program Manager, BATC |  | Date |

Center for Astrophysics & Space Astronomy

University of Colorado

Campus Box 593

Boulder, Colorado 80309

| REVISIONS |
| --- |
| Letter | ECO No. | Description | Check | Approved | Date |
| - |  | Initial Release |  | EW | 5/14/04 |
| A | COS-090 | Incorporates results from 2006 thermal vacuum tests. |  | CSF |  |
| Original Release |  | THE UNIVERSITY OF COLORADO |
| Name | Date | At Boulder |
| Drawn: E. Wilkinson | 4-12-04 | The Center for Astrophysics and Space Astronomy |
| Reviewed: |  |  |
| Approved: |  | COS Prelaunch Calibration Data |
|  |  | Size | Code Indent No. | Document No. | Rev |
|  |  | A |  | COS-01-0008 | A |
|  |  | Scale: N/A |  |  |

TABLE OF CONTENTS

1.	Introduction	4

2.	Controlling Documents	4

3.	COS Reference Files	5

4.	Relevant Calibration Information	6

4.1	2003 Thermal vacuum test configuration	6

4.2	2006 Thermal Vacuum Test configuration	10

5.	Instrument Performance	15

5.1	Wavelength solutions and ranges	15

5.1.1	CEI Requirements	15

5.1.2	Description	15

5.1.3	Results from 2003 Appendix B Tests	16

5.1.4	Results of 2006 measurements	21

5.2	Spectral Resolution	22

5.2.1	CEI Requirements	22

5.2.2	Description	22

5.2.3	2003 Results - FUV	24

5.2.4	2003 Results ( NUV	28

5.2.5	2006 Test Results	29

5.2.6	BOA Spectral Resolution	34

5.2.6.1	Description	35

5.2.6.2	2003 Results	35

5.2.6.3	Results of 2006 Tests	43

5.3	Spatial Resolution	45

5.3.1	CEI Requirements	45

5.3.2	Description	45

5.3.3	FUV spatial resolution	46

5.3.3.1	2003 Results	46

5.3.4	NUV spatial resolution	48

5.3.4.1	2003 Results	48

5.3.5	2006 Test Results	50

5.4	Sensitivity	51

5.4.1	CEI Requirements	51

5.4.2	Description	51

5.4.3	2003 Results – 1st Order Efficiencies	57

5.4.4	2003 Results – 2nd Order Efficiencies	61

5.4.4.1	Results for G225M:	63

5.4.4.2	Results for G285M and G230L:	63

5.4.4.3	Conclusions:	63

5.4.5	2003 Results – 1st Order Efficiencies w/ FUV Detector QE Grid Off	63

5.4.6	2006 Sensitivity Measurements	66

5.5	Bright Object aperture transmission	73

5.5.1	CEI Requirement	73

5.5.2	2003 Test Description & Data Reduction	73

5.5.3	FUV Channel	74

5.5.3.1	2003 Results	75

5.5.4	NUV Channel	75

5.5.4.1	2003 Results	76

5.5.5	2006 Test Results	79

5.5.5.1	FUV	80

5.5.5.2	NUV	81

5.6	signal to noise	82

5.6.1	CEI Requirements	82

5.6.2	FUV Channel	82

2003 FUV Flat Field Analysis	83

5.6.2.1	83

5.6.2.2	2006 FUV Flat Field Analysis	89

5.6.3	NUV Channel	95

5.6.3.1	2003 Results	96

5.6.3.2	2006 Results	101

5.6.3.2	102

5.7	Field of View	102

5.7.1	CEI Requirements	102

5.7.2	Description	102

5.7.3	2003 Results	103

5.8	Stray and Scattered Light	106

5.8.1	Requirements	106

5.8.2	FUV	106

5.8.2.1	Analysis	107

5.8.2.2	Results	107

5.8.3	NUV	109

5.8.3.1	Analysis	109

5.8.3.2	Results	110

5.9	Image stability & Drift CompensAtion	112

5.9.1	CEI Requirements	112

5.9.2	Description	112

5.9.3	Results	115

5.9.4	Recommendations	126

5.9.5	2006 Tag-flash Verification Testing	127

5.10	NUV Imaging Capability	127

5.10.1	CEI Requirements	127

5.10.2	Description	127

5.10.3	2003 Results	128

5.10.4	2006 Results	129

5.11	FUV/NUV Background Rates	130

5.11.1	2003 FUV Background Results	130

5.11.1.1	2006 FUV Background Results	133

5.11.2	NUV Background	135

5.11.2.1	2006 NUV Background Results	136

5.12	Calibration Subsystem	136

5.12.1	CEI Requirements	136

5.12.2	Description	136

5.12.3	Wavelength Calibration Lamp Count Rates	136

5.12.4	Flat Field Lamp Count Rates	138

5.13	Operational Parameters	140

5.13.1	FUV	140

5.13.1.1	Nominal Stim Locations	140

5.13.1.2	Geometric Distortion Map	141

5.13.1.3	Location of Spectra	141

5.13.2	NUV	141

5.13.2.1	Location of Spectra	141

5.13.3	Target Acquisition	142

6.	Appendix	142

6.1	2003 Calibration Planning	142

6.2	2006 Calibration planning	145

6.3	Target Acquisition Data	148

# Introduction

This document presents the final results of the ground calibration of the Cosmic Origins Spectrograph (COS).  The data were acquired as part of the formal thermal vacuum testing of COS where the testing procedures were documented in Appendices A, B, and C of the thermal vacuum procedure.  Data taken as part of Appendix A were largely intended to gather data and experience necessary to facilitate more extensive testing during Appendix B and to identify early on any potential performance issues.  Appendix B was a thorough test of all instrument performance characteristics conducted in 2003.  In the summer of 2006, the COS electronics boards were removed from the instrument and modified to replace the power converters with more robust components and to correct for minor workmanship issues. Appendix C was a repeat of several key calibration tests, undertaken in late 2006 to verify continued nominal performance of the instrument after the modification and reinstallation of the electronics boards.  The exposure list for all the data acquired during Appendices A,B, and C are available as COS-03-0091 (exposurelist_A_master.xls), COS-03-0092 (exposurelist_B_master.xls), and COS03-0093 (exposurelist_C_master.xls) from the controlled documents archive of the COS instrument development team.

This document is organized in the following manner.  Section 2 lists relevant documents that provide a complete description of the COS instrument, how it works, how to operate it, and how to reduce the data.  Section 3 lists the COS reference files delivered to the Space Telescope Science Institute for use in the COS data reduction pipeline. Section 4 describes the calibration systems used to calibrate COS and Section 5 presents the various calibration results.  Section 5 is organized in a similar fashion to the top-level controlling document for COS, the Contract End Item Specification.  Finally, Section 6 consists of a variety of appendices that contain calibration planning and exposure logs for Appendix A as well as final results for the target acquisition testing conducted in 2003.

# Controlling Documents

This document is the third publication in a triumvirate that provide a complete top-level description of COS instrument.  The other two documents are…

Cosmic Origins Spectrograph (COS) Science Operations Requirements Document

(CDRL OP-01; CU/CASA document COS-01-0001)

COS Calibration Requirements & Procedures

(CDRL AV-03; CU/CASA document COS-01-0003)

Also worth examining is the top-level controlling document for COS:

Hubble Space Telescope Cosmic Origins Spectrograph Contract End Item Specification	 (GSFC document STE-63).

# COS Reference Files

The data acquired during science calibration tests in 2003 and 2006 were used to generate reference files to initially populate the COS data reduction pipeline, the software package provided to general observers by the Space Telescope Science Institute (STScI) for COS data calibration.  The reference files, listed in Table 4.1-1, were delivered to STScI in 2007. This document describes the tests undertaken in 2003 and 2006 and the subsequent data analysis and characterization of the instrument properties. A description of the creation of the files is provided in COS-03-0090, “Generating the COS Reference Files.

Table 4.1-1: COS Reference Files

| Title | IDT filename | STScI filename | Description |
| --- | --- | --- | --- |
| Flat Field | nuv_flat.fits | s5n1735al_flat.fits | The flat field reference file is an image with pixel-to-pixel flat; the large-scale fluctuations in sensitivity are accounted for in the photometric correction table. |
| Geometric Distortion | FUV02_GEOCORR.fits | nb61015el_geo.fits | The geometric distortion reference file is used to correct for the intrinsic nonlinearity (INL) of the FUV detector. |
| Detector Deadtime | fuv02_dead.fits nuv_dead.fits | s5n1734pl_dead.fits s5n17358l_dead.fits | The deadtime reference frame table gives the livetime factor for various values of the observed global count rate. |
| Data Quality | fuv_bpix.fits nuv_bpix.fits | s5n1734sl_bpix.fits s5n17357l_bpix.fits | The data quality initialization table gives the locations of rectangular regions that cover portions of the detector that are known to be less than optimal. |
| Baseline Reference Frame | ref_brf.fits | nan1523nl_brf.fits | The baseline reference frame table gives the “actual” location of each of the two electronic stims, for each FUV segment. These are necessary to perform the thermal correction. |
| Pulse Height Thresholds | fuv_pha.fits | s5n17352l_pha.fits | The pulse height parameters reference table gives thresholds for checking FUV data based on pulse height filtering for TIME-TAG data and PHA distribution verification for ACCUM data. |
| 1-D Extraction | fuv_1dx_2003.fits fuv_1dx_2006.fits nuv_1dx_2003.fits nuv_1dx_2006.fits | s5n1734ql_1dx.fits s5n1734rl_1dx.fits s5n17355l_1dx.fits s5n17356l_1dx.fits | The 1-D extraction parameters table gives the location of the spectrum to be extracted from a 2-D image. |
| Calibration Lamp Templates | fuv_lamp.fits nuv_lamp.fits | s5n17351l_lamp.fits s5n1735bl_lamp.fits | The template cal lamp spectra table contains template wavecal spectra, to be compared with observed wavecal spectra. |
| Photometric Sensitivity | fuv_phot.fits nuv_phot.fits | s5n17353l_phot.fits s5n1735cl_phot.fits | The photometric sensitivity reference table gives the instrumental sensitivity at each element of a 1-D extracted spectrum. |
| Dispersion Solutions | fuv_disp.fits nuv_disp.fits | s5n17350l_disp.fits s5n17359l_disp.fits | The dispersion relation table gives a set of polynomial coefficients for computing wavelength from pixel number. |
| Wavelength Calibration Parameters | fuv_wcp.fits nuv_wcp.fits | s5n17354l_wcp.fits s5n1735dl_wcp.fits | The wavecal parameters reference table gives parameters that are relevant to wavecal processing (pixels per FPPOS position, number of pixels per resolution element, etc.). |

# Relevant Calibration Information

# 2003 Thermal vacuum test configuration

In 2003 (Appendices A and B), COS Thermal-Vacuum Testing and Science Calibration took place in the large “Rambo” vacuum chamber located in Ball’s FT1 environmental test facility. The photograph in Figure 4.1-1 gives an idea of its size, while Figure 4.1-2 shows the high level arrangement of the equipment. COS was inside the vacuum chamber, inside its thermal balance fixture, and sitting on a vibration isolated table. The Reflective Aberration Simulator for CALibration (RASCAL) sent an image to the COS entrance aperture that reproduced the aberration content of a point source (single or multiple) as seen by HST. The Calibration Delivery System (CDS) delivered light with the desired spectral content and intensity to RASCAL. CDS consisted of two sections – an external platform outside the vacuum chamber and a set of relay optics inside the chamber that illuminated the RASCAL input pinholes.

The layout of the external platform is shown in Figure 4.1-3. There were two channels. One included an Acton VM-504 vacuum UV monochromator, which isolated a wavelength region approximately 10 Å in width, centered on any wavelength in the COS range 1150 Å <  < 3200 Å.  The second channel bypassed the monochromator and allowed the entire spectral content of its lamp to reach COS. This was known as the ‘lamp-only channel’. A manually operated flat turning mirror selected the desired channel and fed a collimating mirror. The collimated beam passed through a 10 cm long absorption cell and six filter wheels in series. A manually operated shutter blocked all light when inserted. A MgF2 window separated CDS from RAMBO, allowing each to respond to its own system of vacuum pumps.

An IST Pt-Ne hollow cathode lamp illuminated the input slit of the monochromator, and was the only source used on this channel. On the lamp-only channel we used a Pt-Ne lamp, a D2 hollow cathode lamp, and a Vici-Condyne Kr continuum lamp for the various experiments. Swapping lamps took about half an hour. The absorption cell was filled with CO for FUV tests, and O2 for NUV measurements. The pressure could be set to any value between about a milli-Torr and one atmosphere. The cell was removed when not in use. Each filter wheel contained one open position and two filters. Neutral density filters ranging from ND 0.3 to ND 3.0 could be used individually or in series, providing a large range of discrete steps of attenuation. A CaF long-pass filter blocked the Ly  emission line for certain experiments, and a fused silica long-pass filter blocked all FUV light shortward of about 1650 Å when NUV measurements were under way. Bandpass filters centered at 122, 145, 157, 185, 220 and 280 nm allowed restriction of the spectral content to the wavelength regions of the COS gratings. In general these were only used during setup, and not during the COS exposures.

The movement of the grating turret in the monochromator was controlled by a Labview program running on the RASCAL computer. All other equipment on the CDS external platform, including the monochromator slit widths, was operated manually. The lamps were connected to their power supplies and operated manually. As a matter of safe practice the RASCAL PMT was inserted into the light path during the setup phase for each test. The lamp intensity and selection of filters were made to produce a count rate on the PMT that would ensure adequate but safe levels of illumination for COS. The expected hardware configuration and target event rates were documented in the calibration planning documents and procedures.

The external platform also contained an alignment camera that viewed the RASCAL entrance apertures. It was only used during the pre-test setup to guide the alignment of the relay optics to RASCAL.

The RASCAL entrance aperture accommodates four different pinholes and one fully open position. A 10m diameter circular pinhole simulated a point source, and a 100m circular aperture produced a slightly extended image for efficiency measurements. These were used during all phases of the calibration program. A 4m pinhole was in place during Appendix A, but was not used. A pair of 10m holes separated by the equivalent of 1 arc second were used to verify spatial resolution. For the Appendix B tests these were replaced by a linear array of 7 pinholes (10(m pinholes equally spaced at 1" in the cross-dispersion direction) and a 2D array of pinholes (10m pinholes on a 100m x 338 [disp x cross-dispersion] grid) needed for FUV geometrical distortion measurements. The aperture selection was made from the menu on the RASCAL computer.

The alignment of the RASCAL powered optics to produce the required aberration content and focus was performed by the cognizant GSFC optical scientists prior to the COS calibration. Adjusting RASCAL image quality was not part of the CU/Ball calibration effort.

The output beam of RASCAL could be steered in tip and tilt via commands from its computer menu. Similarly the CsTe PMT could be inserted into and extracted from the optical beam with this program. The PMT was operated with a separate Labview program running on the same computer. The calibration and use of the PMT are described elsewhere in this report.

Figure 4.1-1: The RAMBO chamber where the COS calibration activity was conducted in 2003.

Figure 4.1-2 : Overall layout of the test setup used during the 2003 COS calibration and thermal vacuum test.

Figure 4.1-3 : The Calibration Delivery Sub-system (CDS) used during COS calibration in 2003 to inject monochromatic or polychromatic light into the RAMBO chamber where the RASCAL instrument formatted the input light into an aberrated beam for use by COS.

## 2006 Thermal Vacuum Test configuration

The 2006 Thermal Vacuum Testing and Science Calibration (Appendix C) took place in the Space Environment Simulator (SES) at the Goddard Space Flight Center.  The configuration of the chamber required that COS, RASCAL, and the CDS all reside on the same vibration isolated table in the SES vacuum chamber (see Figure 4.2-1 and Figure 4.2-2).  As with the previous setup, the CDS fed light to the RASCAL Relay Optics which in turn fed light through one of 5 selectable pinholes or pinhole arrays and into RASCAL.  RASCAL recreates the HST aberrations and feeds light at the appropriate beam speed into the science instrument.  RASCAL is equipped with a NIST traceable photomultiplier tube which is placed in the calibration beam path after the last reflection for photometric calibration.

A new vacuum compatible CDS was developed with all the capabilities of the previous version except for the absorption cell and the Kr lamp.  The layout of the calibration setup is shown in Figure 4.2-3 and the CDS is illustrated in Figure 4.2-4. The vacuum CDS consisted of a remotely selectable lamp array feeding a vacuum compatible monochromator system.  This was followed by a two bank filter wheel and a fold mirror.  The final element before the relay optics was a MgF2 wedge polarization scrambler with a 25mm clear aperture.  The CDS was also fitted with a remotely operated shutter, an alignment camera, a deployable beam splitter for the camera, and a heated cover for stray light suppression and thermal control.

The lamp array consisted of two non-flight IST hollow cathode Pt/Ne lamps and two non-flight IST Deuterium lamps, as well as a Hureas Pt/Cr/Ne hollow cathode lamp (unused) and a LED alignment lamp.  Lamps were heat sunk and mounted on a lamp select translation stage.  The monochromator system consisted of a McPherson 234/302 scanning monochromator system (a 0.2 meter corrected holographic grating monochromator fed by a model 615B condenser and in turn feeding a 30mm collimator).  The filter mechanism consisted of two nine position wheels (the available filters are listed in Table 4.2-1).   All CDS controls were concentrated in a single control rack near the RASCAL control station, and the CDS configuration could be automatically logged during science calibration.

RASCAL is described in the previous section, and was used in the same configuration as is described for appendix B testing (three circular pinholes; 1mm (‘open’), 100µm, 10µm, and two arrays; a 1x7 (cross dispersion) and a 7x7 array of 10µm pinholes).

Table 4.2-1:  Calibration Delivery System Filter Array

| Position | Filter Wheel 1 | Filter Wheel 2 |
| --- | --- | --- |
| 1 | Open | Open |
| 2 | F122 | CaF2 |
| 3 | F145 | ND 0.3 |
| 4 | F157 | ND 0.5 |
| 5 | F185 + Fused Silica | ND 1.0 |
| 6 | F220 + Fused Silica | ND 2.0 |
| 7 | F280 + Fused Silica | ND 3.0 |
| 8 | ND 0.5 | Fused Silica |
| 9 | Open | Open |

Figure 4.2-1  COS Thermal Vacuum 2006 calibration test configuration – COS and all optical GSE are installed in the Space Environment Simulator (SES) vacuum chamber at Goddard Space Flight Center.  COS is supported in the thermal balance fixture (TBF) in the ‘diamond’ configuration, and the CDS is to the left of COS under the CDS thermal enclosure.  All components are mounted on a two piece support plate which is in turn mounted to the circular vibration isolated table.

Figure 4.2-2:  COS Thermal Vacuum 2006 calibration test configuration showing CDS (far left), the relay optics and RASCAL with COS above and behind.

Figure 4.2-3:  COS Thermal Vacuum 2006 calibration test configuration.  The CDS, relay Optics, RASCAL and COS/TBF were mounted on the vibration isolated table in the GSFC SES chamber. The base plates for CDS and COS/RASCAL were bolted together. The Relay Optics were hard mounted to the COS base plate, while the CDS, RASCAL and COS/TBF were placed on kinematic mounts.  The light path from the calibration lamps through the COS entrance aperture is shown.  Illustration is not to scale.

Figure 4.2-4: Vacuum compatible calibration delivery system (CDS) layout. Not to scale.

# Instrument Performance

## Wavelength solutions and ranges

### CEI Requirements

Tables 4.1 and 4.2 of the CEI list the specific requirements on wavelength coverage.

### Description

The wavelength solutions for the NUV and FUV channels are presented below.  The wavelength solutions presented were derived using the wavelength calibration spectra. Subsequently, the offsets () between the wavelength calibration spectra and the science spectra were measured.  This offset must be applied to the y-intercept of the wavelength calibration solution to get the correct wavelength solution for the science spectrum.

Tests:	1160 - CDS Pt-Ne spectra G185M

1170 - CDS Pt-Ne spectra G225M

1180 - CDS Pt-Ne spectra G285M

1190 - CDS Pt-Ne spectra G230L

1110 - FUV CDS Pt-Ne Group 1

1120 - FUV CDS Pt-Ne Group 2

### Results from 2003 Appendix B Tests

The tables below present the NUV and FUV wavelength solutions and bandpass values for each wavelength setting and channel.  The file names listed and the wavelength solutions given (aside from the (λ term) correspond to the internal PtNe calibration exposures . For Table 5.1-1 and Table 5.1-2, λ (min), λ (cen) and λ (max) correspond to the minimum, central and maximum observable wavelengths for that setting, based on the pixel values for the active detector region limits for each segment after thermal and geometric correction.  Note that the λ (min) and λ (cen) columns are reversed in Table 5.1-2 relative to Table 5.1-1. These values are approximate wavelengths and may be different in flight due to the final location of the aperture and to repeatability errors within OSM1 and OSM2.

For the FUV channels the wavelengths are computed using

λ = a0 (+(λ) + a1 * x + a2 *x 2

where x is in pixels.  A first order fit is sufficient for G130M and G160M, so the a2 values are set to zero for these gratings.

For the NUV channels the wavelengths are computed using

λ = a0 (+(λ) + a1 *y + a2 *y 2

where y is in pixels.  The (λ term is added if the wavelength solution is to be applied to science data as opposed to wavelength calibration spectra.

Table 5.1-1  : FUV Wavelength Solutions

| Channel | File | Seg. | c |  (min) |  (cen) |  (max) | a0 | a1 | a2 |  (Å) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| G130M | CSIL03286093403a | A | 1291 | 1283.70 | 1353.80 | 1423.90 | 1435.483 | -0.0099656 | 0 | 0.433 |
|  |  | B |  | 1130.77 | 1201.52 | 1272.25 | 1282.227 | -0.0099643 | 0 | 0.413 |
| G130M | CSIL03286095158 | A | 1300 | 1293.89 | 1364.00 | 1434.10 | 1445.679 | -0.0099656 | 0 | 0.433 |
|  |  | B |  | 1140.97 | 1211.72 | 1282.45 | 1292.429 | -0.0099645 | 0 | 0.413 |
| G130M | CSIL03286021646 | A | 1309 | 1303.83 | 1373.94 | 1444.04 | 1455.619 | -0.0099656 | 0 | 0.433 |
|  |  | B |  | 1150.93 | 1221.68 | 1292.42 | 1302.392 | -0.0099645 | 0 | 0.413 |
| G130M | CSIL03286100953 | A | 1318 | 1313.21 | 1383.32 | 1453.42 | 1464.999 | -0.0099656 | 0 | 0.433 |
|  |  | B |  | 1160.31 | 1231.05 | 1301.78 | 1311.756 | -0.0099638 | 0 | 0.413 |
| G130M | CSIL03286102748 | A | 1327 | 1322.97 | 1393.08 | 1463.18 | 1474.759 | -0.0099656 | 0 | 0.433 |
|  |  | B |  | 1170.09 | 1240.83 | 1311.56 | 1321.535 | -0.0099617 | 0 | 0.413 |
| G160M | CSIL03286080403 | A | 1577 | 1576.67 | 1662.50 | 1748.33 | 1762.780 | -0.012244 | 0 | 0.529 |
|  |  | B |  | 1388.50 | 1472.29 | 1560.08 | 1574.523 | -0.012238 | 0 | 0.513 |
| G160M | CSIL03286082058 | A | 1589 | 1588.51 | 1674.37 | 1760.18 | 1774.628 | -0.012242 | 0 | 0.529 |
|  |  | B |  | 1400.40 | 1486.17 | 1571.94 | 1586.375 | -0.012235 | 0 | 0.513 |
| G160M | CSIL03286034546 | A | 1600 | 1600.06 | 1685.85 | 1771.64 | 1786.080 | -0.012238 | 0 | 0.529 |
|  |  | B |  | 1411.87 | 1497.66 | 1583.45 | 1597.891 | -0.012238 | 0 | 0.513 |
| G160M | CSIL03286083753 | A | 1611 | 1612.17 | 1697.95 | 1783.72 | 1798.162 | -0.012236 | 0 | 0.529 |
|  |  | B |  | 1423.98 | 1509.77 | 1595.56 | 1609.997 | -0.012238 | 0 | 0.513 |
| G160M | CSIL03286085448 | A | 1623 | 1624.31 | 1710.10 | 1795.89 | 1810.330 | -0.012238 | 0 | 0.529 |
|  |  | B |  | 1436.10 | 1521.94 | 1607.72 | 1622.162 | -0.012237 | 0 | 0.513 |
| G140L | CSIL03286120659 | A | 1105 | 1120.64 | 1686.82 | 2256.13 | 2336.657 | -0.08047 | 3.114e-08 | 3.411 |
| G140L | CSIL03286051016 | A | 1230 | 1260.89 | 1827.55 | 2396.78 | 2477.245 | -0.08041 | 2.548e-08 | 3.411 |

a Exposure names from the thermal vacuum tests are automatically generated and indicate the date and time of the file creation; e.g., CSIL03286093403 indicates that the file was written in year [20]03, day  286, hour 09, minute 34, second 03 (UT time).

Table 5.1-2 : NUV Wavelength Solutions

| Channel | File | Stripe | c |  (cen) |  (min) |  (max) | a0 | a1 | a2 |  (Å) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | a |  | 1795.67 | 1776.49 | 1814.69 | 1814.695 | -0.03711 | -2.23E-07 | 0.561 |
| G185M | CSIL03265222615 | b | 1900 | 1898.72 | 1880.04 | 1917.25 | 1917.247 | -0.03613 | -2.36E-07 | 0.470 |
|  |  | c |  | 2003.61 | 1985.83 | 2021.57 | 2021.569 | -0.03491 | -3.22E-07 | 0.391 |
|  |  | a |  | 1712.47 | 1693.12 | 1731.68 | 1731.678 | -0.03748 | -2.06E-07 | 0.699 |
| G185M | CSIL03266010953 | b | 1817 | 1816.56 | 1797.67 | 1835.30 | 1835.300 | -0.03655 | -2.21E-07 | 0.593 |
|  |  | c |  | 1922.71 | 1904.39 | 1940.86 | 1940.861 | -0.0354 | -2.47E-07 | 0.521 |
|  |  | a |  | 1747.25 | 1728.00 | 1766.39 | 1766.392 | -0.03738 | -1.48E-07 | 0.659 |
| G185M | CSIL03266012647 | b | 1850 | 1850.92 | 1832.13 | 1869.57 | 1869.567 | -0.03638 | -2.13E-07 | 0.567 |
|  |  | c |  | 1956.57 | 1938.34 | 1974.63 | 1974.629 | -0.03522 | -2.47E-07 | 0.486 |
|  |  | a |  | 1778.94 | 1759.78 | 1798.04 | 1798.044 | -0.03723 | -1.67E-07 | 0.602 |
| G185M | CSIL03266014341 | b | 1882 | 1882.21 | 1863.53 | 1900.81 | 1900.816 | -0.03623 | -2.09E-07 | 0.517 |
|  |  | c |  | 1987.39 | 1969.28 | 2005.39 | 2005.387 | -0.03502 | -2.72E-07 | 0.431 |
|  |  | a |  | 1818.03 | 1798.97 | 1837.05 | 1837.045 | -0.03705 | -1.73E-07 | 0.583 |
| G185M | CSIL03266020035 | b | 1921 | 1920.8 | 1902.2 | 1939.3 | 1939.298 | -0.03599 | -2.69E-07 | 0.505 |
|  |  | c |  | 2025.39 | 2007.38 | 2043.29 | 2043.285 | -0.03482 | -2.74E-07 | 0.419 |
|  |  | a |  | 1850.53 | 1831.51 | 1869.48 | 1869.484 | -0.03690 | -2.12E-07 | 0.522 |
| G185M | CSIL03266021729 | b | 1953 | 1952.88 | 1934.35 | 1971.28 | 1971.284 | -0.03579 | -3.09E-07 | 0.448 |
|  |  | c |  | 2056.95 | 2039.06 | 2074.77 | 2074.770 | -0.03468 | -2.22E-07 | 0.361 |
|  |  | a |  | 1884.67 | 1865.74 | 1903.52 | 1903.524 | -0.03672 | -2.07E-07 | 0.546 |
| G185M | CSIL03266023423 | b | 1986 | 1986.54 | 1968.13 | 2004.81 | 2004.879 | -0.03568 | -2.37E-07 | 0.438 |
|  |  | c |  | 2090.1 | 2072.29 | 2107.8 | 2107.804 | -0.03444 | -2.73E-07 | 0.370 |
|  |  | a |  | 1682.93 | 1663.56 | 1702.21 | 1702.212 | -0.03755 | -2.25E-07 | 0.790 |
| G185M | CSIL03266025117 | b | 1786 | 1787.37 | 1768.46 | 1806.21 | 1806.207 | -0.03667 | -2.22E-07 | 0.674 |
|  |  | c |  | 1893.92 | 1875.57 | 1912.2 | 1912.198 | -0.03558 | -2.20E-07 | 0.578 |
|  |  | a |  | 1730.75 | 1711.46 | 1749.91 | 1749.914 | -0.03741 | -1.79E-07 | 0.676 |
| G185M | CSIL03266030811 | b | 1835 | 1834.62 | 1815.77 | 1853.30 | 1853.302 | -0.03644 | -2.36E-07 | 0.602 |
|  |  | c |  | 1940.51 | 1922.24 | 1958.61 | 1958.609 | -0.03529 | -2.56E-07 | 0.504 |
|  |  | a |  | 1760.29 | 1741.07 | 1779.39 | 1779.391 | -0.03728 | -1.72E-07 | 0.630 |
| G185M | CSIL03266032505 | b | 1864 | 1863.82 | 1845.06 | 1882.41 | 1882.408 | -0.03626 | -2.43E-07 | 0.549 |
|  |  | c |  | 1969.25 | 1951.06 | 1987.27 | 1987.274 | -0.03513 | -2.64E-07 | 0.446 |
|  |  | a |  | 1788.3 | 1796.16 | 1807.34 | 1807.343 | -0.03707 | -2.53E-07 | 0.588 |
| G185M | CSIL03266034159 | b | 1890 | 1891.45 | 1872.77 | 1910.02 | 1910.019 | -0.03613 | -2.76E-07 | 0.471 |
|  |  | c |  | 1996.48 | 1978.4 | 2014.47 | 2014.473 | -0.03502 | -2.36E-07 | 0.352 |
|  |  | a |  | 1810.58 | 1791.5 | 1829.61 | 1829.612 | -0.03707 | -1.83E-07 | 0.515 |
| G185M | CSIL03266035853 | b | 1913 | 1913.45 | 1894.85 | 1931.98 | 1931.979 | -0.03610 | -1.86E-07 | 0.419 |
|  |  | c |  | 2018.15 | 2000.14 | 2036.08 | 2036.082 | -0.03491 | -2.22E-07 | 0.309 |
|  |  | a |  | 1838.15 | 1819.1 | 1857.1 | 1857.099 | -0.03689 | -2.44E-07 | 0.495 |
| G185M | CSIL03266041547 | b | 1941 | 1940.64 | 1922.11 | 1959.12 | 1959.121 | -0.03601 | -1.61E-07 | 0.377 |
|  |  | c |  | 2044.92 | 2026.98 | 2062.77 | 2062.767 | -0.03473 | -2.49E-07 | 0.311 |
|  |  | a |  | 1868.57 | 1849.62 | 1887.47 | 1887.469 | -0.03681 | -1.84E-07 | 0.455 |
| G185M | CSIL03266043241 | b | 1971 | 1970.68 | 1952.2 | 1989.04 | 1989.035 | -0.03570 | -2.96E-07 | 0.366 |
|  |  | c |  | 2074.48 | 2056.61 | 2092.23 | 2092.234 | -0.03453 | -2.86E-07 | 0.281 |
|  |  | a |  | 1909.63 | 1890.79 | 1928.47 | 1928.471 | -0.03677 | -6.42E-08 | 0.408 |
| G185M | CSIL03266044935 | b | 2010 | 2011.17 | 1992.82 | 2029.46 | 2029.459 | -0.03560 | -2.12E-07 | 0.348 |
|  |  | c |  | 2114.32 | 2096.59 | 2131.96 | 2131.96 | -0.03432 | -2.50E-07 | 0.279 |

| Channel | File | Stripe | c |  (cen) |  (min) |  (max) | a0 | a1 | a2 |  (Å) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | a |  | 2087.85 | 2069.39 | 2106.15 | 2106.1463 | -0.035691 | -2.36E-07 | 0.241 |
| G225M | CSIL03266121900 | b | 2186 | 2186.78 | 2168.89 | 2204.51 | 2204.5096 | -0.034568 | -2.48E-07 | 0.106 |
|  |  | c |  | 2286.92 | 2269.70 | 2303.97 | 2303.9665 | -0.033232 | -2.60E-07 | 0.033 |
|  |  | a |  | 2119.01 | 2100.67 | 2137.23 | 2137.2289 | -0.035557 | -1.78E-07 | 0.204 |
| G225M | CSIL03266103736 | b | 2217 | 2217.45 | 2199.66 | 2235.08 | 2235.0776 | -0.034363 | -2.57E-07 | 0.090 |
|  |  | c |  | 2317.02 | 2299.89 | 2333.97 | 2333.9691 | -0.033016 | -2.90E-07 | -0.007 |
|  |  | a |  | 2136.31 | 2117.99 | 2154.49 | 2154.4911 | -0.035473 | -2.08E-07 | 0.146 |
| G225M | CSIL03266075357 | b | 2233 | 2234.47 | 2216.73 | 2252.05 | 2252.0485 | -0.034265 | -2.52E-07 | 0.061 |
|  |  | c |  | 2333.73 | 2316.66 | 2350.62 | 2350.6155 | -0.032895 | -2.90E-07 | -0.079 |
|  |  | a |  | 2153.21 | 2134.94 | 2171.31 | 2171.3134 | -0.035313 | -2.38E-07 | 0.119 |
| G225M | CSIL03266105430 | b | 2250 | 2251.09 | 2233.40 | 2268.62 | 2268.6245 | -0.034214 | -2.13E-07 | 0.050 |
|  |  | c |  | 2350.03 | 2333.00 | 2366.84 | 2366.8427 | -0.032714 | -3.56E-07 | -0.027 |
|  |  | a |  | 2171.97 | 2153.76 | 2190.05 | 2190.0491 | -0.035279 | -1.89E-07 | 0.149 |
| G225M | CSIL03266123554 | b | 2268 | 2269.56 | 2251.92 | 2287.01 | 2287.0108 | -0.034006 | -2.87E-07 | 0.043 |
|  |  | c |  | 2368.15 | 2351.20 | 2384.91 | 2384.9140 | -0.032664 | -2.89E-07 | -0.059 |
|  |  | a |  | 2187.55 | 2169.35 | 2205.58 | 2205.5757 | -0.035141 | -2.64E-07 | 0.101 |
| G225M | CSIL03266111124 | b | 2283 | 2284.86 | 2267.29 | 2302.28 | 2302.2787 | -0.033956 | -2.41E-07 | 0.035 |
|  |  | c |  | 2383.16 | 2366.26 | 2399.88 | 2399.8832 | -0.032586 | -2.79E-07 | -0.055 |
|  |  | a |  | 2208.37 | 2190.25 | 2226.33 | 2226.3299 | -0.035025 | -2.42E-07 | 0.089 |
| G225M | CSIL03266125248 | b | 2306 | 2305.34 | 2287.82 | 2322.68 | 2322.6808 | -0.033803 | -2.72E-07 | 0.002 |
|  |  | c |  | 2403.23 | 2386.41 | 2419.87 | 2419.8699 | -0.032411 | -2.87E-07 | -0.108 |
|  |  | a |  | 2228.74 | 2210.70 | 2246.66 | 2246.6594 | -0.034979 | -1.71E-07 | 0.093 |
| G225M | CSIL03266112818 | b | 2325 | 2325.38 | 2307.91 | 2342.64 | 2342.6425 | -0.033616 | -3.26E-07 | -0.048 |
|  |  | c |  | 2422.87 | 2406.12 | 2439.43 | 2439.4329 | -0.032252 | -3.06E-07 | -0.095 |
|  |  | a |  | 2242.21 | 2224.21 | 2260.05 | 2260.0539 | -0.034780 | -2.56E-07 | 0.059 |
| G225M | CSIL03266130942 | b | 2339 | 2338.60 | 2321.20 | 2355.91 | 2355.9071 | -0.033828 | -9.20E-08 | -0.030 |
|  |  | c |  | 2435.85 | 2419.15 | 2452.37 | 2452.3653 | -0.032172 | -2.93E-07 | -0.119 |
|  |  | a |  | 2262.78 | 2244.83 | 2280.58 | 2280.5788 | -0.034731 | -2.09E-07 | 0.043 |
| G225M | CSIL03266114512 | b | 2357 | 2358.82 | 2341.48 | 2375.98 | 2375.9796 | -0.033426 | -2.94E-07 | -0.054 |
|  |  | c |  | 2455.65 | 2439.03 | 2472.09 | 2472.0909 | -0.032033 | -2.81E-07 | -0.158 |
|  |  | a |  | 2278.28 | 2260.37 | 2296.02 | 2296.0209 | -0.034597 | -2.49E-07 | 0.023 |
| G225M | CSIL03266100434 | b | 2373 | 2374.04 | 2356.75 | 2391.15 | 2391.1522 | -0.033352 | -2.74E-07 | -0.049 |
|  |  | c |  | 2470.56 | 2453.96 | 2486.95 | 2486.9514 | -0.031912 | -3.31E-07 | -0.173 |
|  |  | a |  | 2295.54 | 2277.70 | 2313.24 | 2313.2361 | -0.034533 | -1.95E-07 | -0.009 |
| G225M | CSIL03266120206 | b | 2390 | 2391.00 | 2373.75 | 2408.05 | 2408.0460 | -0.033180 | -3.37E-07 | -0.100 |
|  |  | c |  | 2487.18 | 2470.66 | 2503.49 | 2503.4944 | -0.031770 | -3.23E-07 | -0.191 |
|  |  | a |  | 2316.09 | 2298.31 | 2333.72 | 2333.7245 | -0.034402 | -2.13E-07 | -0.028 |
| G225M | CSIL03266132636 | b | 2410 | 2411.19 | 2394.00 | 2428.15 | 2428.1539 | -0.033012 | -3.63E-07 | -0.090 |
|  |  | c |  | 2506.93 | 2490.51 | 2523.19 | 2523.1907 | -0.031682 | -2.61E-07 | -0.212 |

| Channel | File | Stripe | c |  (cen) |  (min) |  (max) | a0 | a1 | a2 |  (Å) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | a |  | 2498.34 | 2476.19 | 2520.33 | 2520.334 | -0.04286 | -2.83E-07 | 0.281 |
| G285M | CSIL03266212736 | b | 2617 | 2617.21 | 2595.74 | 2638.53 | 2638.530 | -0.04154 | -2.85E-07 | 0.213 |
|  |  | c |  | 2737.53 | 2716.86 | 2758.04 | 2758.042 | -0.03995 | -3.00E-07 | 0.057 |
|  |  | a |  | 2519.60 | 2497.50 | 2541.54 | 2541.537 | -0.04275 | -2.89E-07 | 0.222 |
| G285M | CSIL03266145158 | b | 2637 | 2638.13 | 2616.70 | 2659.37 | 2659.367 | -0.04133 | -3.69E-07 | 0.129 |
|  |  | c |  | 2758.07 | 2737.47 | 2778.50 | 2778.497 | -0.03975 | -3.49E-07 | 0.014 |
|  |  | a |  | 2538.93 | 2516.90 | 2560.81 | 2560.811 | -0.04265 | -2.63E-07 | 0.220 |
| G285M | CSIL03266214430 | b | 2657 | 2657.16 | 2635.81 | 2678.37 | 2678.369 | -0.04134 | -2.57E-07 | 0.116 |
|  |  | c |  | 2776.74 | 2756.20 | 2797.11 | 2797.113 | -0.03967 | -3.17E-07 | 0.011 |
|  |  | a |  | 2558.02 | 2536.03 | 2579.85 | 2579.846 | -0.04253 | -2.97E-07 | 0.266 |
| G285M | CSIL03266200306 | b | 2676 | 2675.94 | 2654.64 | 2697.04 | 2697.042 | -0.04108 | -3.60E-07 | 0.151 |
|  |  | c |  | 2795.18 | 2774.71 | 2815.49 | 2815.493 | -0.03956 | -2.94E-07 | 0.065 |
|  |  | a |  | 2578.44 | 2556.56 | 2600.25 | 2600.247 | -0.04256 | -1.36E-07 | 0.167 |
| G285M | CSIL03266155716 | b | 2695 | 2696.05 | 2674.82 | 2717.12 | 2717.120 | -0.04105 | -2.97E-07 | 0.055 |
|  |  | c |  | 2814.91 | 2794.50 | 2835.14 | 2835.138 | -0.03935 | -3.60E-07 | -0.027 |
|  |  | a |  | 2593.01 | 2571.12 | 2614.75 | 2614.746 | -0.04236 | -2.78E-07 | 0.216 |
| G285M | CSIL03266202000 | b | 2709 | 2710.37 | 2689.15 | 2731.38 | 2731.380 | -0.04087 | -4.01E-07 | 0.105 |
|  |  | c |  | 2828.96 | 2808.59 | 2849.14 | 2849.141 | -0.03928 | -3.47E-07 | 0.000 |
|  |  | a |  | 2601.00 | 2579.13 | 2622.71 | 2622.706 | -0.04229 | -3.01E-07 | 0.147 |
| G285M | CSIL03266170234 | b | 2719 | 2718.23 | 2697.04 | 2739.20 | 2739.196 | -0.04079 | -4.02E-07 | 0.064 |
|  |  | c |  | 2836.66 | 2816.31 | 2856.81 | 2856.806 | -0.03920 | -3.81E-07 | -0.072 |
|  |  | a |  | 2622.00 | 2600.21 | 2643.66 | 2643.657 | -0.04222 | -2.50E-07 | 0.172 |
| G285M | CSIL03266220124 | b | 2739 | 2738.87 | 2717.77 | 2759.80 | 2759.798 | -0.04074 | -3.30E-07 | 0.031 |
|  |  | c |  | 2856.91 | 2836.67 | 2877.04 | 2877.042 | -0.03926 | -2.03E-07 | -0.002 |
|  |  | a |  | 2736.60 | 2715.14 | 2757.91 | 2757.911 | -0.04153 | -2.73E-07 | -0.005 |
| G285M | CSIL03266221818 | b | 2850 | 2851.50 | 2830.79 | 2872.07 | 2872.065 | -0.04006 | -2.81E-07 | -0.132 |
|  |  | c |  | 2967.29 | 2947.43 | 2986.96 | 2986.963 | -0.03826 | -3.76E-07 | -0.236 |
|  |  | a |  | 2840.02 | 2818.90 | 2861.00 | 2861.002 | -0.04088 | -2.67E-07 | -0.130 |
| G285M | CSIL03266180752 | b | 2952 | 2953.04 | 2932.72 | 2973.23 | 2973.232 | -0.03934 | -2.52E-07 | -0.202 |
|  |  | c |  | 3066.69 | 3047.22 | 3085.98 | 3085.983 | -0.03753 | -3.51E-07 | -0.332 |
|  |  | a |  | 2866.53 | 2845.52 | 2887.44 | 2887.435 | -0.04078 | -1.89E-07 | -0.075 |
| G285M | CSIL03266203654 | b | 2979 | 2979.06 | 2958.76 | 2999.14 | 2999.138 | -0.03905 | -4.13E-07 | -0.230 |
|  |  | c |  | 3092.14 | 3072.77 | 3111.31 | 3111.305 | -0.03726 | -4.08E-07 | -0.310 |
|  |  | a |  | 2884.75 | 2863.77 | 2905.55 | 2905.554 | -0.04049 | -3.49E-07 | -0.141 |
| G285M | CSIL03266223512 | b | 2996 | 2996.91 | 2976.72 | 3016.95 | 3016.946 | -0.03902 | -2.97E-07 | -0.243 |
|  |  | c |  | 3109.62 | 3090.31 | 3128.73 | 3128.734 | -0.03718 | -3.70E-07 | -0.382 |
|  |  | a |  | 2906.44 | 2885.52 | 2927.20 | 2927.196 | -0.04042 | -3.13E-07 | -0.170 |
| G285M | CSIL03266205348 | b | 3018 | 3018.19 | 2998.06 | 3038.14 | 3038.135 | -0.03881 | -3.50E-07 | -0.232 |
|  |  | c |  | 3130.41 | 3111.20 | 3149.45 | 3149.445 | -0.03703 | -3.47E-07 | -0.337 |
|  |  | a |  | 2923.99 | 2903.18 | 2944.70 | 2944.698 | -0.04037 | -2.11E-07 | -0.172 |
| G285M | CSIL03266225206 | b | 3035 | 3035.41 | 3015.37 | 3055.30 | 3055.301 | -0.03875 | -2.82E-07 | -0.280 |
|  |  | c |  | 3147.23 | 3128.21 | 3166.22 | 3166.221 | -0.03711 | -4.42E-08 | -0.422 |
|  |  | a |  | 2947.63 | 2926.85 | 2968.23 | 2968.228 | -0.04010 | -3.34E-07 | -0.284 |
| G285M | CSIL03266211042 | b | 3057 | 3058.57 | 3038.59 | 3078.38 | 3078.376 | -0.03856 | -3.19E-07 | -0.361 |
|  |  | c |  | 3169.89 | 3150.80 | 3188.70 | 3188.696 | -0.03647 | -5.60E-07 | -0.479 |
|  |  | a |  | 2965.13 | 2944.43 | 2985.66 | 2985.655 | -0.03994 | -3.53E-07 | -0.254 |
| G285M | CSIL03266191310 | b | 3074 | 3075.73 | 3055.81 | 3095.44 | 3095.437 | -0.03834 | -3.91E-07 | -0.371 |
|  |  | c |  | 3186.64 | 3167.63 | 3205.43 | 3205.429 | -0.03652 | -4.24E-07 | -0.423 |
|  |  | a |  | 2984.08 | 2963.45 | 3004.57 | 3004.567 | -0.03992 | -2.69E-07 | -0.233 |
| G285M | CSIL03266230900 | b | 3094 | 3094.30 | 3074.47 | 3113.91 | 3113.910 | -0.03815 | -3.93E-07 | -0.367 |
|  |  | c |  | 3204.80 | 3185.83 | 3223.47 | 3223.473 | -0.03623 | -5.54E-07 | -0.446 |

| Channel | File | Stripe | c |  (cen) |  (min) |  (max) | a0 | a1 | a2 |  (Å) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | a |  | 1539.56 | 1343.61 | 1738.14 | 1739.14 | -0.39334 | 6.92E-06 | 20.06 |
| G230L | CSIL03267064458 | b | 2635 | 2630.13 | 2430.46 | 2828.98 | 2828.98 | -0.38869 | -8.43E-07 | 19.30 |
|  |  | c |  | 1883.88 | 1784.68 | 1982.66 | 1982.66 | -0.19311 | -4.06E-07 | 8.51a |
|  |  | a |  | 1852.23 | 1652.14 | 2051.69 | 2051.69 | -0.39009 | -4.58E-07 | 19.32 |
| G230L | CSIL03267091836 | b | 2950 | 2942.43 | 2742.98 | 3141.13 | 3141.13 | -0.38850 | -6.80E-07 | 18.17 |
|  |  | c |  | 2039.71 | 1940.50 | 2138.18 | 2138.18 | -0.19215 | -1.05E-06 | 8.18a |
|  |  | a |  | 1911.58 | 1711.55 | 2110.82 | 2110.82 | -0.38950 | -7.63E-07 | 19.06 |
| G230L | CSIL03267074616 | b | 3000 | 3001.69 | 2802.13 | 3200.20 | 3200.20 | -0.38784 | -1.25E-06 | 18.95 |
|  |  | c |  | 2069.68 | 1972.95 | 2168.29 | 2168.29 | -0.19498 | 3.95E-06 | 5.75a |
|  |  | a |  | 2279.03 | 2079.17 | 2478.33 | 2478.33 | -0.38985 | -3.23E-07 | 18.99 |
| G230L | CSIL03267084734 | b | 3360 | 3368.69 | 3169.24 | 3566.85 | 3566.85 | -0.38692 | -1.71E-06 | 18.18 |
|  |  | c |  | 2252.22 | 2153.36 | 2350.83 | 2350.83 | -0.19294 | -8.50E-08 | 8.25a |

a Second-order light.

### Results of 2006 measurements

The measurements of the wavelength solutions for all of the COS spectroscopic modes were repeated in Appendix C.  The relevant test numbers are given below.  Between 2003 and 2006, the ‘tag-flash’ observing mode was implemented to correct for spectral drifts in the data caused by motions of the OSM1 and OSM2 mechanisms (see Section 5.9).  When tag-flash is used, the internal PtNe wavelength calibration lamp is exposed periodically during a science exposure.   The Appendix C observations used tag-flash, eliminating the need for the separate internal wavecal exposures that were obtained in the 2003 tests.  Accordingly, the tests listed below are equivalent to their 2003 complements (e.g., Tests 1160 and 1161 are paired) in execution, except for the removal of separate internal wavecals and the use of tag-flash during the external exposures.

Tests:	1161 - CDS Pt-Ne spectra G185M

1171 - CDS Pt-Ne spectra G225M

1181 - CDS Pt-Ne spectra G285M

1191 - CDS Pt-Ne spectra G230L

1111 - FUV CDS Pt-Ne Group 1

1121 - FUV CDS Pt-Ne Group 2

There were only minor changes in the wavelength solutions between the 2003 and 2006 measurements.  The spectral dispersions remained the same for all of the gratings.  The zero points of the science and calibration stripes changed slightly: about 0.5 Å for G130M and G160M, and 4.7 Å for G140L in the FUV modes, for example, and 0.85 Å and 2 Å for G225M on the NUV side.  The change in the zero points of the science frames is most likely attributable to a different placement of the COS aperture block relative to RASCAL in the two test setups, except for the larger offset in G225M, which is the result of a change in the flight software commanding for the central wavelength of the grating between 2003 and 2006.

## Spectral Resolution

### CEI Requirements

Section 4.2.2 and Table 4-4 of the CEI present the spectral resolution requirements for COS.  In short, the G130M, G160M, G225M, and G285M channels shall support a spectral resolution () > 20,000, the G185M shall support R > 16,000, and the G140L and G230L shall support R>2000.  The spectral resolution must also be achieved over 80% of the usable bandpass.

### Description

The resolutions of the FUV channels were computed using drift corrected exposures with exposure times of 6500 seconds to give accurate representations of the expected instrument resolution.  In addition, for the FUV spectra care was taken to extract only those lines identified as narrow and isolated, to remove the potential for naturally broad or multiple lines to appear as degraded resolution.

For the NUV channels the large number of wavelength settings made collecting long exposures and drift correcting all the data impractical, so short exposures were used to measure the spectral resolution. Also, the sheer number of lines and wavelength settings for the NUV channel made it inefficient to hand-select isolated, narrow emission lines, so all the emission lines were measured.  This means there appear to be a certain number of lines that do not meet the spectral resolution requirements.  It is highly likely that these lines do not reflect poor resolution and should be ignored.  Finally, the G185M and G225M resolutions were measured at GN2 to minimize a thermal distortion between the COS thermal balance fixture and RAS/Cal.  Thus some of the shortest lines in the G185M channel were not measured, as the GN2 blocked those lines.

Tests:	2300 – FUV Grating Stability

1155 – G185M NUV Pt-Ne Spectra in GN2

1156 – G225M NUV Pt-Ne Spectra in GN2

1180 – G285M NUV Spectra of Pt-Ne Lamp

1190 – G230L NUV Spectra of Pt-Ne Lamp

Relevant Exposures:

Table 5.2-1: Exposure list for 2003 Spectral Resolution Measurements

| File | Channel/C | Comments |
| --- | --- | --- |
| CSIL03285043406 | G130M/1309 | texp=6500 |
| CSIL03285081037 | G160M/1600 | texp=6500 |
| CSIL03285101309 | G140L/1240 | texp=6500 |
| CSIL03295043202 | G185M/2010 | GN2 environment |
| CSIL03295044431 | G185M/1986 | " |
| CSIL03295045701 | G185M/1971 | " |
| CSIL03295050931 | G185M/1953 | " |
| CSIL03295052200 | G185M/1941 | " |
| CSIL03295053429 | G185M/1921 | " |
| CSIL03295054700 | G185M/1913 | " |
| CSIL03295055931 | G185M/1900 | " |
| CSIL03295061201 | G185M/1890 | " |
| CSIL03295062431 | G185M/1882 | " |
| CSIL03295063700 | G185M/1864 | " |
| CSIL03295064931 | G185M/1850 | " |
| CSIL03295070201 | G185M/1835 | " |
| CSIL03295071430 | G185M/1817 | " |
| CSIL03295072700 | G185M/1786 | " |
| CSIL03295073831 | G225M/2410 | " |
| CSIL03295074601 | G225M/2390 | " |
| CSIL03295075331 | G225M/2373 | " |
| CSIL03295080100 | G225M/2357 | " |
| CSIL03295080831 | G225M/2339 | " |
| CSIL03295081600 | G225M/2325 | " |
| CSIL03295082331 | G225M/2306 | " |
| CSIL03295083101 | G225M/2283 | " |
| CSIL03295083830 | G225M/2268 | " |
| CSIL03295084600 | G225M/2250 | " |
| CSIL03295085330 | G225M/2233 | " |
| CSIL03295090100 | G225M/2217 | " |
| CSIL03295090831 | G225M/2186 | " |
| CSIL03266144527 | G285M/2637 | Vacuum environment |
| CSIL03266155045 | G285M/2695 | " |
| CSIL03266165603 | G285M/2719 | " |
| CSIL03266180121 | G285M/2952 | " |
| CSIL03266190639 | G285M/3074 | " |
| CSIL03266193941 | G285M/2637 | " |
| CSIL03266195635 | G285M/2676 | " |
| CSIL03266201329 | G285M/2709 | " |
| CSIL03266203023 | G285M/2979 | " |
| CSIL03266204717 | G285M/3018 | " |
| CSIL03266210411 | G285M/3057 | " |
| CSIL03266212105 | G285M/2617 | " |
| CSIL03266213759 | G285M/2657 | " |
| CSIL03266215453 | G285M/2739 | " |
| CSIL03266221147 | G285M/2850 | " |
| CSIL03266222841 | G285M/2996 | " |
| CSIL03266224535 | G285M/3035 | " |
| CSIL03266230229 | G285M/3094 | " |
| CSIL03267063927 | G230L/2635 | " |
| CSIL03267074045 | G230L/3000 | " |
| CSIL03267084203 | G230L/3360 | " |
| CSIL03267091305 | G230L/2950 | " |

### 2003 Results - FUV

Figures 4.2-1, 4.2-2, and 4.2-3 show the spectral resolution for the G130M, G160M, and G140L channels respectively.  Tables 4.2-1 and 4.2-2 list the wavelengths and measured resolutions in tabular form.  The G130M channel does exceed 20,000 over the central portions of the bandpass, but fails to meet the 80% criteria.  The G160M just meets the requirement and the G140L easily meets the spectral resolution requirements.

Figure 5.2-1 : G130M spectral resolution.  The red dots are the measured spectral resolution BEFORE correcting for mechanism drift.  The green dots are the same data AFTER correcting for drift.  The black dots show the spectral resolution measured from a short 100 second exposure.

Figure 5.2-2: G160M spectral resolution.  In this case the red dots are the spectral resolution as measured from a texp = 6500 exposure.  The black dots are for a 100 second exposure spectrum.  No drift correction was required for this data set as there was essentially no drift.

Figure 5.2-3: G140L spectral resolution. The red dots are the measured spectral resolution BEFORE correcting for mechanism drift.  The green dots are the same data AFTER correcting for drift.  The black dots show the spectral resolution measured from a short 100 second exposure.

Table 5.2-2: Wavelength and Measured Spectral Resolutions for G130M and G160M

| G130M-A |  | G130M-B |  | G160M-A |  | G160M-B |
| --- | --- | --- | --- | --- | --- | --- |
| Å | R () |  | Å | R () |  | Å | R () |  | Å | R () |
| 1436.34 | 13987.45 |  | 1286.47 | 11077.47 |  | 1410.14 | 14316.14 |  | 1602.77 | 19103.34 |
| 1435.15 | 22099.85 |  | 1283.69 | 23519.16 |  | 1413.67 | 13349.1 |  | 1605.35 | 18537.53 |
| 1429.53 | 19796.81 |  | 1282.64 | 16833.88 |  | 1417.83 | 14601.75 |  | 1604.74 | 22957.65 |
| 1428.6 | 18774.01 |  | 1275.51 | 19028.68 |  | 1418.38 | 17171.67 |  | 1606.26 | 20332.41 |
| 1417.84 | 18511.48 |  | 1274.63 | 15512.14 |  | 1420.56 | 14407.3 |  | 1610.13 | 15926.11 |
| 1413.69 | 24988.89 |  | 1271.81 | 20695.52 |  | 1421.54 | 16415.01 |  | 1613.98 | 18319.86 |
| 1409.05 | 21146.65 |  | 1266.91 | 21024.81 |  | 1428.57 | 16767.25 |  | 1614.41 | 19687.93 |
| 1389.89 | 25053.41 |  | 1265.74 | 20365.71 |  | 1429.52 | 17079.09 |  | 1620.68 | 19959.11 |
| 1383.29 | 23986.98 |  | 1259.53 | 19247.95 |  | 1432.92 | 16489.3 |  | 1621.65 | 16927.45 |
| 1380.52 | 22355.84 |  | 1257.23 | 18084.29 |  | 1435.13 | 15481.45 |  | 1630.51 | 17996.8 |
| 1379.02 | 25927.98 |  | 1256.57 | 18231.42 |  | 1436.32 | 18250.57 |  | 1631.1 | 17652.6 |
| 1378.07 | 23855.24 |  | 1248.63 | 19588.24 |  | 1446.28 | 18807.28 |  | 1634.23 | 17497.11 |
| 1374.95 | 22705.05 |  | 1245.69 | 20107.58 |  | 1447.8 | 19485.87 |  | 1636.15 | 17669.01 |
| 1373.23 | 23250.27 |  | 1244.84 | 20692.67 |  | 1454.28 | 18862.26 |  | 1644.46 | 17797.19 |
| 1369.42 | 23303.7 |  | 1244.37 | 21356.79 |  | 1461.08 | 21144.43 |  | 1652.12 | 19857.21 |
| 1364.17 | 19236.6 |  | 1237.5 | 21797.78 |  | 1461.49 | 21429.47 |  | 1654.27 | 22086.38 |
| 1355.76 | 21814.14 |  | 1236.09 | 18064.82 |  | 1462.67 | 20091.62 |  | 1659.47 | 21220.84 |
| 1353.02 | 22716.67 |  | 1235.12 | 19107.55 |  | 1464.14 | 18509.99 |  | 1669.23 | 24692.75 |
| 1348.88 | 20803.39 |  | 1234.58 | 21784.54 |  | 1475.64 | 22290.63 |  | 1676.02 | 23473.67 |
| 1348.32 | 20699.3 |  | 1232.9 | 21016.1 |  | 1482.83 | 22777.73 |  | 1677.85 | 24674.27 |
| 1347.02 | 22729.85 |  | 1229.05 | 22436.04 |  | 1494.72 | 23138.08 |  | 1679.19 | 25365.41 |
| 1340.21 | 19643.62 |  | 1220.82 | 19643.02 |  | 1498.12 | 22393.42 |  | 1680.88 | 22087.78 |
| 1337.94 | 18605.42 |  | 1219.53 | 20930.45 |  | 1499.38 | 22213.04 |  | 1681.69 | 25364.86 |
| 1327.49 | 17331.93 |  | 1217.82 | 17954.67 |  | 1505.24 | 21783.5 |  | 1684.58 | 23139.84 |
| 1325.16 | 19798.86 |  | 1217.52 | 20205.19 |  | 1506.29 | 23138.09 |  | 1686.25 | 21985.01 |
| 1323.36 | 16882.77 |  | 1216.14 | 18528.5 |  | 1507.63 | 19554.21 |  | 1688.36 | 23065.03 |
| 1322.91 | 18840.03 |  | 1215.27 | 18800.54 |  | 1509.3 | 21842.26 |  | 1692.15 | 24666.91 |
| 1320.26 | 17603.71 |  | 1213.25 | 20929.93 |  | 1524.73 | 21844.27 |  | 1696.29 | 23141.75 |
| 1315.62 | 17449.19 |  | 1208.23 | 20807.53 |  | 1528.29 | 22310.8 |  | 1698.49 | 25388.49 |
| 1309.58 | 20322.1 |  | 1207.68 | 21014.32 |  | 1530.2 | 23433.38 |  | 1707.08 | 24111.3 |
|  |  |  | 1203.78 | 16833.11 |  | 1534.9 | 24957.72 |  | 1712.66 | 24054.21 |
|  |  |  | 1201.32 | 21423.57 |  | 1540.5 | 20761.46 |  | 1713.83 | 23704.43 |
|  |  |  | 1200.84 | 19077 |  | 1541.83 | 22026.14 |  | 1714.47 | 22150.78 |
|  |  |  | 1198.81 | 20365.82 |  | 1542.71 | 21249.45 |  | 1723.14 | 20489.18 |
|  |  |  | 1196.59 | 17667.55 |  | 1546.83 | 21909.77 |  | 1727.67 | 20518.64 |
|  |  |  | 1193.48 | 18322.21 |  | 1552.32 | 20697.6 |  | 1737.18 | 20129.55 |
|  |  |  | 1192.3 | 21150.04 |  | 1554.93 | 22276.94 |  | 1737.59 | 21061.7 |
|  |  |  | 1189.34 | 21950.72 |  | 1559.4 | 22865.1 |  | 1744.43 | 17035.45 |
|  |  |  | 1188.73 | 21199.01 |  | 1561.55 | 22024.68 |  | 1746.45 | 21246.35 |
|  |  |  | 1186.26 | 18905.08 |  | 1566.73 | 19657.84 |  | 1753.83 | 18403.25 |
|  |  |  | 1182.4 | 18179.99 |  | 1568.89 | 21550.69 |  | 1758.12 | 16824.12 |
|  |  |  | 1181.15 | 16289.71 |  | 1573.18 | 22002.52 |  | 1764.6 | 107597.57 |
|  |  |  | 1180.77 | 17008.71 |  | 1573.83 | 19896.71 |  | 1766.02 | 17983.91 |
|  |  |  | 1180.29 | 17075.38 |  | 1574.31 | 22426.07 |  | 1767.15 | 17410.34 |
|  |  |  | 1179 | 17255.67 |  | 1579.45 | 19993.04 |  | 1776.57 | 19206.16 |
|  |  |  | 1178.47 | 11749.81 |  | 1581.41 | 15973.84 |  | 1777.08 | 17560.08 |
|  |  |  | 1177.02 | 16527.96 |  |  |  |  |  |  |
|  |  |  | 1176.45 | 16180.43 |  |  |  |  |  |  |
|  |  |  | 1175.19 | 14424.29 |  |  |  |  |  |  |
|  |  |  | 1169.8 | 15807.51 |  |  |  |  |  |  |
|  |  |  | 1166.9 | 14755.56 |  |  |  |  |  |  |
|  |  |  | 1152.45 | 17939.24 |  |  |  |  |  |  |

Table 5.2-3: Wavelength and Measured Spectral Resolution for G140L

| Å | R () | Å | R () | Å | R () | Å | R () |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 2049.52 | 4050.98 | 1826.44 | 3833.79 | 1669.68 | 3846.19 | 1429.98 | 2392.47 |
| 2036.56 | 4734.84 | 1813.11 | 4360.98 | 1644.97 | 3566.37 | 1410.52 | 2622.51 |
| 2032.59 | 3582.43 | 1803.26 | 4200.22 | 1636.79 | 4077.77 | 1404.34 | 1846.62 |
| 1988.78 | 4065.58 | 1794.45 | 4366.37 | 1634.74 | 3800.65 | 1390.36 | 2701.26 |
| 1979.47 | 4715.86 | 1789.48 | 4939.32 | 1631.61 | 2156.77 | 1382.49 | 2711.17 |
| 1971.18 | 3933.36 | 1786.98 | 4774.67 | 1622.2 | 2488.16 | 1379.5 | 2910.27 |
| 1962.84 | 4939.16 | 1782.21 | 4951.97 | 1594.68 | 2507.33 | 1373.76 | 2550.39 |
| 1949.54 | 5220.15 | 1777.52 | 3847.1 | 1588.2 | 3402.09 | 1356.18 | 2895.18 |
| 1944.25 | 4237.22 | 1767.64 | 4605.18 | 1581.96 | 3276.69 | 1349.17 | 1334.4 |
| 1939.76 | 3404.45 | 1765.14 | 4058.64 | 1574.93 | 2795.47 | 1340.45 | 1607.43 |
| 1937.28 | 4732.3 | 1758.69 | 2614.32 | 1567.22 | 2283.64 | 1338.15 | 2250.85 |
| 1934.18 | 4398.89 | 1754.35 | 4789.63 | 1555.47 | 3629.81 | 1330.39 | 2568.8 |
| 1916.12 | 5065.72 | 1745.03 | 4753.83 | 1552.87 | 3040.55 | 1327.73 | 2195.01 |
| 1911.73 | 5118.91 | 1736.42 | 4659.44 | 1547.38 | 3981.66 | 1323.32 | 1552.71 |
| 1907.56 | 4714.85 | 1728.24 | 3981.1 | 1535.42 | 2702.37 | 1320.43 | 1996 |
| 1895.31 | 2411.24 | 1723.66 | 4311.34 | 1528.92 | 3367.21 | 1315.78 | 1986.57 |
| 1889.69 | 4409.74 | 1718.56 | 5043.54 | 1525.32 | 2246.1 | 1313.16 | 2266.61 |
| 1883.24 | 5400.34 | 1707.66 | 4776.61 | 1510.02 | 2365.31 | 1309.8 | 1972.78 |
| 1879.32 | 3714.57 | 1705.25 | 4256.79 | 1505.87 | 2602.83 | 1305.34 | 2265.61 |
| 1874.69 | 2330.6 | 1699.13 | 3135.83 | 1500.05 | 2728.24 | 1299.54 | 1389.5 |
| 1870.7 | 2616.33 | 1696.86 | 4457.84 | 1495.38 | 2199.42 | 1293.17 | 1806.59 |
| 1867.3 | 4148.88 | 1691.42 | 3939.72 | 1486.67 | 2835.6 | 1290.17 | 2768.41 |
| 1853.81 | 4829.67 | 1688.8 | 3833.86 | 1483.5 | 2904.72 | 1286.54 | 1562.22 |
| 1850.01 | 4996.36 | 1685.09 | 4502.43 | 1476.27 | 2356.64 | 1283.65 | 2440.96 |
| 1846.12 | 4664.17 | 1678.42 | 4283.67 | 1458.14 | 2850.61 | 1274.84 | 1397.68 |
| 1836.92 | 3563.31 | 1660.05 | 4407.33 | 1454.75 | 1968.68 | 1271.74 | 2136.27 |
| 1818.15 | 5298.56 | 1654.82 | 3581.54 | 1448.38 | 2951.24 | 1263.66 | 1675.7 |

### 2003 Results ( NUV

Figure 4.2-4 shows the spectral resolution for the NUV channels.  It is apparent that the G225M, G285M, and G230L channels all meet specifications.  However, the G185M appears to have lower resolution than specified at the shortest wavelengths.  This is thought to be due to residual misalignment between RASCAL and COS.

Figure 5.2-4: Measured spectral resolution for the four NUV channels.  The solid lines indicate the bandpass of each channel.  The filled circles represent the measured spectral resolution for individual emission lines.  The G225M, G285M, and G230L channels all clearly meet their respective spectral resolution requirements.  The G185M data indicates that the spectral resolution may not meet requirements at the shortest wavelengths, where data do not exist due to absorption of the shortest wavelenghs by the GN2.  This is thought to be due to a slight misalignment between COS and RASCAL.  Also note that the G185M and G225M data were acquired with the instrument at GN2, not vacuum, in order to minimize the misalignment between COS and RASCAL.

### 2006 Test Results

Analysis of the spectral resolution of the COS data was repeated in 2006.  The external wavecal spectra used to determine the wavelength solutions were also used to find spectral resolutions.  Unlike in 2003, all the data analyzed were acquired in vacuum. No corrections were made for drifts, but the exposure times of the data (300 sec) were shorter than the exposures analyzed in 2003. The alignment between the COS thermal balance fixture and RASCAL was much better in 2006 than in 2003, leading to the expectation that some of the low spectral resolutions measured in Appendix B would be improved in 2006.

Tests:	1111 - FUV CDS Pt-Ne Group 1

1161 - CDS Pt-Ne spectra G185M

1171 - CDS Pt-Ne spectra G225M

1181 - CDS Pt-Ne spectra G285M

1191 - CDS Pt-Ne spectra G230L

Figure 5.2-5, Figure 5.2-6, and Figure 5.2-7 show the measured spectral resolutions for the FUV gratings from the 2006 tests.  The 2006 version of the CDS delivered fewer FUV counts to COS than in 2003, so there were fewer external calibration lines of sufficient signal to measure the FWHM for spectral resolution determinations.  This was particularly true for G130M, where the number of measured lines is small and the scatter on the measurements relatively large.  However, there is enough data to show that the G130M spectral resolutions are higher in the 2006 data than in 2003.  The more recent measurements indicate that G130M meets the spectral resolution requirement of R≥20,000 over 80% of the active waveband.  (We don’t have measurements <1180 Å, but there is no reason to expect the spectral resolution to decline more than the linear drop with wavelength.) The G160M and G140L measurements are consistent with the 2003 results.

Figure 5.2-5:  The measured spectral resolutions for the G130M grating from the 2006 thermal vacuum tests.  The solid lines show the active bandpasses for the two grating segments while the dotted line shows the spectral resolution requirement for the grating.

Figure 5.2-6: The measured spectral resolutions for the G160M grating from the 2006 thermal vacuum tests.  The solid lines show the active bandpasses for the two grating segments while the dotted line shows the spectral resolution requirement for the grating.

Figure 5.2-7: The measured spectral resolutions for the G140lM grating from the 2006 thermal vacuum tests.  The solid line shows the active bandpass for the grating segment while the dotted line shows the spectral resolution requirement for the grating.

Figure 5.2-8 shows the resolution as a function of wavelength for the NUV gratings. As expected, the measured spectral resolutions are higher in 2006 than in 2003, due to the improved alignment in the test configuration.  In particular, G185M now meets the spectral resolution requirement over the full bandpass.  As with the 2003 data, the highest and lowest spectral resolution points are likely artifacts: in the former case, caused by poor detections of faint features with anomalously narrow spreads and in the latter case, by poor fits to lines or line blends.

Figure 5.2-8:  Spectral resolution as a function of wavelength for the NUV modes. G185M is in red, G225M is in green, G285M is in blue, and G230L is in light blue. The solid lines indicate the bandpass and spectral resolution requirement for each channel.

### BOA Spectral Resolution

When COS was first assembled and tested in a GN2 environment it was discovered that the image quality through the BOA was severely degraded.  The BOA is a 2 mm diameter piece of a MgF2 neutral density that is 2 mm thick.  The BOA was fabricated by taking a far larger neutral filter and reshaping it to meet the needs of the COS project.

When the poor image quality was first identified two potential causes of the degradation were investigated: wedge within the BOA and a tilt of the BOA due to installation error.  Tilt of the BOA was quickly ruled out.  Ray-trace modeling of the COS TA1 channel including a 15 arc-minute wedge successfully reproduced the observed point spread function (see Figures 4.2-9 and 4.2-10).  An attempt was made to directly measure the wedge in the spare BOA, however, the small dimensions of the BOA made a direct measurement impossible.  As a side note, when the optic was procured there was no specification on the wedge of the part; wedge being defined as the angle between the front and back surfaces of the filter.  Therefore, in the absence of any other empirical data the cause of the degradation in image quality is assumed to be due to a 15 arc-minute wedge between the front and back surfaces of the BOA.

#### Description

During Appendix B testing data were acquired to measure the BOA transmission function (see section 4.5) using the NUV and FUV low resolution modes, G230L and G140L.  These data sets can be used to determine the spectral resolution for these channels, which is presented in this section.

The performance of the medium resolution channels can be estimated using empirical data and theoretical models, as discussed below.

Tests:	3300 – FUV BOA transmission & resolution

3310 – NUV BOA transmission & resolution

Relevant Exposures:

Table 5.2-4: Exposures for 2003 BOA spectral resolution tests.

| File | Channel/C | Comments |
| --- | --- | --- |
| xp=1800 s |  | C104 | G140L/ 1320Å | texp=1800 s |
| CSIL03267212608 | G285M3000 | texp=1800 s |
| CSIL03267223054 | G285M3360 | texp=1800 s |
| CSIL03267233540 | G285M2635 | texp=1800 s |

#### 2003 Results

Figure 5.2-9 and Figure 5.2-10 show the measured BOA spectral resolution and the spectrum used to measure the resolution for the FUV G140L channel.  Figure 5.2-11 and Figure 5.2-12 present the same information for the NUV G230L channel.  The FUV BOA resolution is ~1500, about 0.75 times that of the PSA, which has a spectral resolution requirement of ≥ 2000.  The NUV BOA resolution is ~500, about 3 times lower than the spectral requirement of ≥ 1700.

The resolution of the NUV M modes can be estimated from a TA1 image, because the NUV gratings are planar and are inserted into a collimated beam.  Figure 5.2-13 shows the point spread function for a point source taken through the BOA, the corresponding dispersion (vertical profile) and cross-dispersion (horizontal profile) line profiles, and Gaussian fits to the profiles.  Figure 5.2-14 shows the predicted results from a ray-trace model of the TA1 channel assuming a 15 arc-minute wedge in the BOA.  Because the resolution of the NUV channel is dispersion limited, it is possible to estimate the spectral resolution for the medium resolution channels using the known image size and measured dispersion.  Figure 5.2-15 shows the predicted resolutions based on the measured image size of 14.26 pixels FWHM (based on the TA1 image shown in Figure 5.2-13).

Finally, Figure 5.2-16 shows the predicted spectral resolution for the FUV G130M and G160M channels based on a ray-trace model of the two channels that includes a 15 arc-minute wedge in the BOA.

Table 5.2-5:  BOA 2003 spectral resolutions.

| Channel |  |  | R =  | a0 | a1 | dispersion |
| --- | --- | --- | --- | --- | --- | --- |
| G225M | 2250 | 0.52 | 3541.34 | -0.03642 | -2.09E-07 | 0.0366 |
| G225M | 2250 | 0.49 | 4582.52 | -0.03423 | -1.97E-07 | 0.0344 |
| G285M | 2850 | 0.57 | 4957.55 | -0.04005 | -2.58E-07 | 0.0403 |
| G230L | 3000 | 5.55 | 540.93 | -0.38774 | -1.15E-06 | 0.389 |

Figure 5.2-9:  Measured spectral resolution for the G140L channel.

Figure 5.2-10: The PtNe spectrum acquired through the BOA.  The data is from file CSIL03285213104.

Figure 5.2-11: Measured BOA spectral resolution for the G230L channel.

Figure 5.2-12: The PtNe spectra acquired through the BOA used to determine the spectral resolution.  The spectra were extracted from CSIL03267212608, CSIL03267223054, and CSIL03267233540.

Figure 5.2-13: The upper two panels show a TA1 image through the BOA of a single point source produced by the CAOS HST optical simulator.  The images are displayed with two different stretches to high-light structures within the image.  The lower panels show the line spread functions in the dispersion and cross-dispersion directions.

Figure 5.2-14: Ray-trace spot diagram of the TA1 image with a 15 arc-minute wedge in the BOA.  Divide the FWHM by 0.025 to get the units in pixels.

Figure 5.2-15: Predicted spectral resolutions for the NUV channels through the BOA.  These predictions are based on the measured dispersion for the central wavelength setting and the measured FWHM in the dispersion direction shown in Figure 4.2-9.

Figure 5.2-16: Predicted FUV spectral resolution assuming a 15 arc-minute wedge  between the front and back surfaces of the BOA.  These results are based on ray-trace simulations of the spectral performance; however, the model does not taken into account wavelength dependence in the index of refraction of MgF2.

#### Results of 2006 Tests

Tests:	3300 – FUV BOA transmission & resolution

3310 – NUV BOA transmission & resolution

The same tests executed in Appendix B were repeated in Appendix C. There are no strict CEI specification requirements for BOA spectral resolution, therefore our aim here is only to show that no changes have occurred since Appendix B testing.

For the NUV, there were three G230L BOA exposures used for BOA-NUV spectral resolution testing. The results of this analysis are shown in the Figure 5.2-17 below. The Appendix B (2003) points are show in blue, and the Appendix C (2006) points are shown in red. There has been no change in the NUV BOA spectral resolution since Appendix B (2003).

Figure 5.2-17:  Measured NUV BOA spectral resolution in 2003 and 2006.

For the FUV, one G140L BOA exposure (CSIL06337025400) was  used for BOA-FUV spectral resolution testing. The results of this analysis are shown in Figure 5.2-18 below. The Appendix B (2003) points are shown in blue, and the Appendix C (2006) points are shown in red. The 2003 data points that were presented in Figure 5.2-9 above are connected by the dashed line.  The 2006 data points show a lower spectral resolution in the FUV than seen in 2003.  However, in Appendix C testing no effort was made to optimally focus COS with the BOA (as was done in Appendix B).  The Appendix C FUV-BOA observations were made with OSM1 at the PSA focus position. While this has little impact on NUV resolution, its effect on the FUV resolution is noticeable (as the index of refraction of  MgF2 rises at shorter wavelengths). As a result, there is no reason to believe that the FUV-BOA resolution has actually changed since Appendix B.

Figure 5.2-18:  FUV BOA spectral resolution in 2003 and 2006.

## Spatial Resolution

### CEI Requirements

Section 4.2.3 of the CEI lists the specific requirements pertaining to spatial resolution.  In part the specification reads, “The spectrum of a single point source centered in the Primary Science Aperture (PSA) shall contain 90% of the energy within a range of 300 m or less in the direction perpendicular to dispersion.

### Description

In Appendix B, the spatial resolution of the FUV and NUV channels was measured in separate tests.  The FUV spatial resolution was measured as part of the geometric distortion calibration of the FUV detector.  In this case the 7x7 pinhole array was used in RASCAL to produce distinct spectra separated by 1".  The individual pinholes are separated by 380 m in the spatial dimension and 100 m in the spectral dimension.  The original purpose of this pinhole array was to sample at a fine scale localized geometric distortions, hence the multiple columns in the spectral dimension.  Fortunately, the separation of the rows in the spatial dimension are sufficient to demonstrate spatial imaging.

One thing that was overlooked was the need to demonstrate the spatial resolution in all three FUV channels.  Therefore, we only have sufficient data to demonstrate performance in the G160M channel.

The NUV spatial imaging was measured using a column of pinholes, each separated by 1".  In this case the spatial imaging was demonstrated for all NUV modes.

### FUV spatial resolution

Tests:	2731 – Geometrical Correction PSA 7x7 pinhole array

Relevant Exposures:

Table 5.3-1: Exposure list for 2003 FUV spatial resolution test.

| File | Channel/C | Comments |
| --- | --- | --- |
| 430L03288074030 | G160M/1600 Å | 15 mA, RASCAL TM2 tip = -0.0387 |
| CSIL03288080430 | G160M/1600 Å | 15 mA, RASCAL TM2 tip = -0.0397 |
| CSIL03288082630 | G160M/1600 Å | 15 mA, RASCAL TM2 tip = -0.0407 |
| CSIL03288084830 | G160M/1600 Å | 15 mA, RASCAL TM2 tip = -0.0437 |

The exposures listed above are all essentially the same.  The RASCAL TM2 mirror was adjusted to direct flux through the pinholes.  These files represent the only high quality information we have regarding the FUV spatial imaging.

#### 2003 Results

Figure 4.3-1 shows the FUV detector image and extracted line profiles in the spatial dimension.  The FUV detector has 24 m y- pixels, therefore, 12.5 pixels represents 300 m.  The 1 widths for each Gaussian in the spatial direction range from 1.05 to 1.33 pixels, so 99% of the counts fall within 11.97 pixels in the worst case, meeting the CEI specification.

y- pixels

Figure 4.3-1: The upper panel shows an expanded view of the 2D pinhole array image.  Only 3 pinholes in the cross-dispersion direction are evident because the PSA blocks the other pinholes.  The lower panel shows the profiles in the cross dispersion direction including the Gaussian parameters for each peak.

### NUV spatial resolution

Tests:	2250 – NUV Spatial Resolution

Relevant Exposures:

Table 5.3-2: Exposure list for 2003 NUV spatial resolution test.

| File | Channel/C | Comments |
| --- | --- | --- |
| CSIL03265180906 | G185M / 1850 Å | Texp = 300 sec |
| CSIL03265183936 | G225M / 2250 Å | Texp = 300 sec |
| CSIL03265185935 | G285M / 2850 Å | Texp = 300 sec |
| CSIL03265192007 | G230L / 3000 Å | Texp = 300 sec |

#### 2003 Results

The nature of the NUV optical path makes it possible to characterize the imaging performance with a single grating.  Figure 4.3-2 shows the G225M spectra acquired as part of Test 2250.  Clearly evident are the 3 pinhole sources.  The measured cross dispersion profiles suggest that 99% of the total counts fall within 342 m (3 width) and that 95% falls within 152 m (2 width).  Thus the CEI specification is met.

Figure 4.3-2: The G225M image of 3 pinhole sources.  The locations of the NUV stripes are shown by ovals.  The lower panel shows the cross dispersion profile and corresponding Gaussian fits to the data.

### 2006 Test Results

Tests:	3300 – FUV BOA Transmission and Resolution

3310 – NUV BOA Transmission and Resolution

The exposures used to measure BOA transmission and resolution (which also included PSA measurements in each setting) were also examined to verify that point source spectra continue to meet the encircled energy requirements in the cross-dispersion direction.

COS FUV digital elements (DE) are 24 m in the cross-dispersion (‘Y’) direction, therefore the CEI specification is that 90% of the counts fall within ± 300/24 = 12.5 DE.  As presented below, both PSA and FUV observations exceed the specifications.

Table 5.3-3: Results of 2006 FUV spatial resolution test.

| Aperture | Grating | C (Å) | Segment | Filename | % within ± 12 pixels |
| --- | --- | --- | --- | --- | --- |
| PSA | G140L | 1230 | A | CSIL06337021910 | 99.3 |
| BOA | G140L | 1230 | A | CSIL06337025400 | 96.3 |

Pixels on the NUV MAMA are 25.4 m on a side, therefore the CEI specification requires that 90% of the counts fall within  ± 300/25 = 12 cross-dispersion (‘X’) pixels. As presented below, both PSA and BOA NUV observations exceed the specification.

Table 5.3-4: Results of 2006 NUV spatial resolution test.

| Aperture | Grating | C (Å) | Stripe | Filename | % within ± 12 pixels |
| --- | --- | --- | --- | --- | --- |
| PSA | G230L | 3000 | B | CSIL06337040102 | 95.5 |
| PSA | G230L | 3360 | A | CSIL06337045256 | 95.8 |
| PSA | G230L | 2635 | B | CSIL06337054450 | 95.9 |
| BOA | G230L | 3000 | B | CSIL06337043507 | 93.2 |
| BOA | G230L | 3360 | A | CSIL06337052701 | 93.6 |
| BOA | G230L | 2635 | B | CSIL06337061855 | 91.4 |

## Sensitivity

### CEI Requirements

Section 4.2.4 and Table 4-4 in the CEI list the requirements for instrument sensitivity.  Section 4.2.7 and Table 4-6 place requirements on the second order efficiency.

### Description

The approach to the efficiency calibration was to treat COS as a detector, and compare its response to that of a reference detector when both viewed the same flux of light. The reference detector was the RASCAL CsTe PMT. This detector was calibrated at the Laboratory for Atmospheric and Space Physics (LASP) in Boulder, CO relative to a NIST calibrated standard diode in the spring of 2003. The source was a Pt-Ne emission line lamp on the CDS monochromator channel. Lines between 1180Å <  < 3064 Å were used. The monochromator slits allowed approximately 10 Å to pass, centered on a bright emission line. The RASCAL 100m circular aperture was used. This provided a healthy signal, and produced a somewhat larger image than a point source to average the COS response over many pixels. During Appendix A only one or two wavelengths were measured for each grating, chosen to sample near the expected peak efficiency. During Appendix B we measured six or more wavelengths for each grating spanning as much of the full wavelength range as possible.

The data-taking procedure included the following steps:

- Insert the PMT into the optical path using its linear stage

- Measure the PMT dark count rate with the CDS shutter closed

- Select the appropriate monochromator grating (FUV or NUV)

- Select the wavelength of interest with the monochromator

- Measure the PMT count rate with the lamp current near 10 milliamps

- Adjust the current to provide at least a few hundred cts/sec, preferably near 1000 cts/sec

- Measure the scattered light contribution to the gross PMT signal

- Remove the PMT from the optical path

- Take a COS exposure with the desired grating and wavelength setting. Exposure times were typically 100 seconds, occasionally longer for faint signals.

- Reinsert the PMT into the optical path

- Repeat the PMT count rate measurement

- Do a quick-look analysis by hand to verify that the data were of good quality

- Move onto the next wavelength or grating

For each FUV grating a single setup position was used. The images of the different emission lines fell on their appropriate regions of the detector. The same basic exposure was repeated for each wavelength. The NUV gratings used different setup wavelengths and different stripes for the different wavelengths. For the NUV M gratings we always had one wavelength that could be measured in all three stripes using different settings. Once underway we could measure three or four wavelengths per hour.

The data analysis is very simple.

PMT count rate = flux * PMT QE

COS count rate = flux * COS efficiency

We tried to be sure that the flux was the same for the two measurements, so that…

COS efficiency = (COS count rate / PMT count rate) * PMT QE

The COS count rate was measured by summing the counts within a range of pixels surrounding the emission line image and dividing by the exposure time. The range of pixels was chosen empirically by the data analyst and test conductor to include the entire 10 Å of spectrum provided by the monochromator.  In a few cases the NUV spectrum was too near the edge of the detector to ensure that all of the light had been captured by COS. The exposure was repeated with the OSM2 grating nudged a step or two to move the image towards the center of the stripe. There were no corrections made or needed for background counts or count-rate non-linearity effects. The uncertainty in the COS count rate was estimated from photon statistics as 1 = sqrt(total counts)/exposure time. The flux in the input light and the exposure times were selected to produce thousands of counts in the final image, so that the uncertainty due to this source was negligible.

The PMT count rate was the average of the measurements made before and after the COS exposure. The rate for each measurement was the gross count rate with the dark count rate (very low) or scattered light (if measured) subtracted. The count rates and 1 uncertainties reported by the Labview PMT control software were used. The Labview program uses the actual standard deviation of the 100 one second integrations (or however many we requested) as the reported 1.  Checking a few test cases showed that it is very close to the value estimated from 1 = sqrt(total counts)/exposure time.

The gratings in the monochromator are not of extremely high quality, and some scattered light is present. Most of the Pt-Ne lines we used are bright enough that the background is small. The FUV lines at the short wavelength end are not bright, and the signal measured by the PMT contained a significant number of longer wavelength photons not recorded by the COS measurement. We did not realize this during the Appendix A tests, and no correction for this effect was made. During the Appendix B phase we estimated this scattered component by making measurements with the monochromator set for  = 1050Å, a wavelength for which no light should be passing through CDS due to the MgF2 window on the lamp and coatings on all of the optics. The PMT count rate measured with this setting was subtracted from the reading obtained with the monochromator set for the wavelength of the emission line being used for calibration. This correction increased the formal uncertainties in the derived COS efficiency, but should be a better estimate.

The PMT QE was the value derived by LASP after adjustment for the annular profile of the RASCAL illumination.  The PMT calibration data is recorded in COS-11-0042 entitled “Calibration Report for the RAS/Cal CsTe Photo-Multiplier Tube.”  The uncertainties resulting from that adjustment were used for the QE errors. These fractional uncertainties range from 7% to 10% of the value of the QE, and dominate the overall errors for all except the faint FUV wavelengths.

The uncertainties in the resulting COS efficiencies were propagated using standard formulas, such as…

X = u  +  v   or  X = u - v, then  2x = 2u + 2v

X = u*v,  or X = u/v, then 2x/x2= 2u/u2 + 2v/v2

The sum and difference formulas are used for taking averages and subtracting backgrounds. The product and quotient formulas for calculating count rates, comparing COS count rates to that of the PMT and multiplying by the PMT QE.

Tables 4.4-1 and 4.4-2 present all of the high quality measurements made during the science calibration. Figure 4.4-1 show the efficiencies and the values expected from the most current component measurements.

Tests:	1210	G130M Sensitivity

- G160M Sensitivity

- G140L Sensitivity

- G185M Sensitivity

- G185M/G225M Sensitivity

- G225M Sensitivity

- G285M Sensitivity

- G230L Sensitivity

- TA1 Sensitivity

1295	TA1-BRT Sensitivity

Relevant Exposures:

Numerous files were taken by the COS team, but not all were used to compute the net system efficiency.  The list below is a comprehensive list of all files that were taken during the efficiency testing.  The data files NOT used to compute the system efficiency are in italics text and were included in the list for future reference.  The dates and test # can be used to cross reference the exposure list and the electronic history files for a more thorough understanding of how the test was conducted or issues that were being explored.

Table 5.4-1: Exposure list for 2003 sensitivity tests.

| File | Date | Test # | Channel | c | Test  |
| --- | --- | --- | --- | --- | --- |
| CSIL03265000336 | 9/21/03 | 1270 | G285M | 2657 | 2659 |
| CSIL03265002706 | 9/21/03 | 1270 | G285M | 2657 | 2540 |
| CSIL03265004706 | 9/21/03 | 1270 | G285M | 2739 | 2734 |
| CSIL03265010907 | 9/21/03 | 1270 | G285M | 2952 | 2830 |
| CSIL03265011906 | 9/21/03 | 1270 | G285M | 2850 | 2830 |
| CSIL03265012936 | 9/21/03 | 1270 | G285M | 2719 | 2830 |
| CSIL03265014006 | 9/21/03 | 1270 | G285M | 2850 | 2830 |
| CSIL03265014735 | 9/21/04 | 1270 | G285M | 2850 | 2830 |
| CSIL03265020536 | 9/21/03 | 1270 | G285M | 2998 | 2996 |
| CSIL03265023007 | 9/21/03 | 1270 | G285M | 3064 | 3057 |
| CSIL03265025305 | 9/21/03 | 1260 | G225M | 2186 | 2085 |
| CSIL03265030831 | 9/21/03 | 1260 | G225M | 2250 | 2144 |
| CSIL03265032335 | 9/21/03 | 1260 | G225M | 2268 | 2262 |
| CSIL03265033807 | 9/21/03 | 1260 | G225M | 2357 | 2357 |
| CSIL03265035032 | 9/21/03 | 1260 | G225M | 2339 | 2440 |
| CSIL03265040336 | 9/21/03 | 1260 | G225M | 2390 | 2487 |
| CSIL03265041406 | 9/21/03 | 1260 | G225M | 2186 | 2290 |
| CSIL03265042305 | 9/21/03 | 1260 | G225M | 2283 | 2290 |
| CSIL03265044236 | 9/21/03 | 1260 | G225M | 2186 | 2290 |
| CSIL03265045136 | 9/21/03 | 1260 | G225M | 2283 | 2290 |
| CSIL03265050037 | 9/21/03 | 1260 | G225M | 2390 | 2290 |
| CSIL03265052106 | 9/21/03 | 1250 | G185M | 1817 | 1723 |
| CSIL03265053236 | 9/21/03 | 1250 | G185M | 1817 | 1723 |
| CSIL03265054437 | 9/21/03 | 1250 | G185M | 1882 | 1777 |
| CSIL03265060235 | 9/22/03 | 1250 | G185M | 1850 | 1846 |
| CSIL03265061336 | 9/22/03 | 1250 | G185M | 1835 | 1937 |
| CSIL03265062807 | 9/22/03 | 1250 | G185M | 1971 | 1972 |
| CSIL03265064106 | 9/22/03 | 1250 | G185M | 1953 | 2050 |
| CSIL03265070206 | 9/22/03 | 1250 | G185M | 1786 | 1883 |
| CSIL03265071506 | 9/22/03 | 1250 | G185M | 1882 | 1883 |
| CSIL03265072706 | 9/22/03 | 1250 | G185M | 1986 | 1883 |
| CSIL03265074236 | 9/22/03 | 1255 | G185M | 2010 | NST |
| CSIL03265074806 | 9/22/03 | 1255 | G185M | 2010 | NST |
| CSIL03265075237 | 9/22/03 | 1255 | G185M | 2010 | NST |
| CSIL03265082135 | 9/22/03 | 1280 | G230L | 2950 | 1723 |
| CSIL03265084906 | 9/22/03 | 1280 | G230L | 2950 | 1723 |
| CSIL03265090105 | 9/22/03 | 1280 | G230L | 2950 | 1723 |
| CSIL03265092607 | 9/22/03 | 1280 | G230L | 3000 | 1846 |
| CSIL03265094036 | 9/22/03 | 1280 | G230L | 3000 | 2050 |
| CSIL03265095807 | 9/22/03 | 1280 | G230L | 3000 | 2085 |
| CSIL03265101606 | 9/22/03 | 1280 | G230L | 3360 | 2262 |
| CSIL03265103135 | 9/22/03 | 1280 | G230L | 2635 | 2487 |
| CSIL03265104435 | 9/22/03 | 1280 | G230L | 2635 | 2659 |
| CSIL03265110136 | 9/22/03 | 1280 | G230L | 2950 | 2830 |
| CSIL03265111606 | 9/22/03 | 1280 | G230L | 3000 | 2998 |
| CSIL03265112736 | 9/22/03 | 1281 | G230L | 3000 | 2085 |
| CSIL03265113636 | 9/22/03 | 1281 | G230L | 2635 | 2085 |
| CSIL03265114606 | 9/22/03 | 1281 | G230L | 3360 | 2085 |
| CSIL03265121336 | 9/22/03 | 1290 | TA-1 | - | 1723 |
| CSIL03265123506 | 9/22/03 | 1290 | TA-1 | - | 1846 |
| CSIL03265125307 | 9/22/03 | 1290 | TA-1 | - | 2262 |
| CSIL03265131106 | 9/22/03 | 1290 | TA-1 | - | 2487 |
| CSIL03265132337 | 9/22/03 | 1290 | TA-1 | - | 2830 |
| CSIL03265134736 | 9/22/03 | 1290 | TA-1 | - | 2998 |
| CSIL03265143906 | 9/22/03 | 1290 | TA-1 | - | 1248 |
| CSIL03265150436 | 9/22/03 | 1290 | TA-1 | - | 1524 |
| CSIL03265153406 | 9/22/03 | 1295 | TA-1 BRT | - | 1723 |
| CSIL03265154636 | 9/22/03 | 1295 | TA-1 BRT | - | 1723 |
| CSIL03265160906 | 9/22/03 | 1295 | TA-1 BRT | - | 2262 |
| CSIL03265163235 | 9/22/03 | 1295 | TA-1 BRT | - | 2487 |
| CSIL03265165406 | 9/22/03 | 1295 | TA-1 BRT | - | 2998 |
| CSIL03265171837 | 9/22/03 | 1295 | TA-1 BRT | - | 1248 |
| CSIL03265174306 | 9/22/03 | 1295 | TA-1 BRT | - | 1524 |
| CSIL032841542545 | 10/11/03 | 1210 | G130M | 1309 | 1249 |
| CSIL03284160055 | 10/11/03 | 1210 | G130M | 1309 | 1249 |
| CSIL03284161725 | 10/11/03 | 1210 | G130M | 1309 | 1216 |
| CSIL03284163452 | 10/11/03 | 1210 | G130M | 1309 | 1180 |
| CSIL03284165624 | 10/11/03 | 1210 | G130M | 1309 | 1327 |
| CSIL03284171253 | 10/11/03 | 1210 | G130M | 1309 | 1379 |
| CSIL03284173055 | 10/11/03 | 1210 | G130M | 1309 | 1430 |
| CSIL03284174424 | 10/11/03 | 1210 | G130M | 1309 | 1430 |
| CSIL03284182126 | 10/11/03 | 1220 | G160M | 1600 | 1430 |
| CSIL03284183555 | 10/11/03 | 1220 | G160M | 1600 | 1482 |
| CSIL03284185255 | 10/11/03 | 1220 | G160M | 1600 | 1524 |
| CSIL03284190655 | 10/11/03 | 1220 | G160M | 1600 | 1621 |
| CSIL03284191855 | 10/11/03 | 1220 | G160M | 1600 | 1669 |
| CSIL03284193526 | 10/11/03 | 1220 | G160M | 1600 | 1723 |
| CSIL03284200425 | 10/11/03 | 1230 | G140L | 1230 | 1723 |
| CSIL03284202226 | 10/11/03 | 1230 | G140L | 1230 | 1524 |
| CSIL03284203755 | 10/11/03 | 1230 | G140L | 1230 | 1430 |
| CSIL03284205327 | 10/11/03 | 1230 | G140L | 1230 | 1248 |
| CSIL03284210956 | 10/11/03 | 1230 | G140L | 1230 | 1327 |
| CSIL03284212626 | 10/11/03 | 1230 | G140L | 1230 | 1937 |
| CSIL03284215057 | 10/11/03 | 1230 | G140L | 1230 | 1248 |
| CSIL03284222027 | 10/11/03 | 1240 | G130M | 1309 | 1216 |
| CSIL03284223956 | 10/11/03 | 1240 | G130M | 1309 | 1379 |
| CSIL03284225425 | 10/11/03 | 1240 | G160M | 1600 | 1482 |
| CSIL03284230556 | 10/11/03 | 1240 | G160M | 1600 | 1669 |
| CSIL03285154919 | 10/12/03 | 1265 | G225M | 2390 | 1249 |
| CSIL03285160951 | 10/12/03 | 1265 | G285M | 2617 | 1249 |
| CSIL03285163550 | 10/12/03 | 1265 | G230L | 2635 | 1249 |
| CSIL03285170051 | 10/12/03 | 1265 | G225M | 2357 | 1180 |
| CSIL03285172421 | 10/12/03 | 1265 | G225M | 2339 | 1216 |
| CSIL03285175220 | 10/12/03 | 1265 | G285M | 3057 | 1524 |
| CSIL03285181320 | 10/12/03 | 1265 | G230L | 3000 | 1524 |
| CSIL03285184320 | 10/12/03 | 1265 | G285M | 3035 | 1574 |
| CSIL03285190250 | 10/12/03 | 1265 | G230L | 3000 | 1574 |

### 2003 Results – 1st Order Efficiencies

Table 5.4-2: COS FUV Efficiency Measurements during 2003 science calibration in vacuum

|  |  |  |  |  |  | COS efficiency |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Appendix | Channel | c (Å) | segment | Test  (Å) | cts/ph | rel. uncertainty | 1  |
| B | G130M | 1309 | B | 1180 | 0.1686 | 0.245 | 0.041 |
| B | G130M | 1309 | B | 1216 | 0.1975 | 0.248 | 0.049 |
| A | G130M | 1309 | B | 1248 | 0.1748 | 0.075 | 0.013 |
| B | G130M | 1309 | B | 1248 | 0.1917 | 0.214 | 0.041 |
| A | G130M | 1309 | A | 1327 | 0.1128 | 0.094 | 0.011 |
| A | G130M | 1309 | A | 1327 | 0.1091 | 0.111 | 0.012 |
| B | G130M | 1309 | A | 1327 | 0.1159 | 0.192 | 0.022 |
| B | G130M | 1309 | A | 1379 | 0.1042 | 0.286 | 0.030 |
| B | G130M | 1309 | A | 1430 | 0.0903 | 0.169 | 0.015 |
| A | G160M | 1600 | B | 1430 | 0.1204 | 0.062 | 0.007 |
| B | G160M | 1600 | B | 1430 | 0.1167 | 0.141 | 0.016 |
| B | G160M | 1600 | B | 1482 | 0.1114 | 0.133 | 0.015 |
| B | G160M | 1600 | B | 1524 | 0.1071 | 0.128 | 0.014 |
| A | G160M | 1600 | A | 1621 | 0.0746 | 0.081 | 0.006 |
| B | G160M | 1600 | A | 1621 | 0.0639 | 0.161 | 0.010 |
| B | G160M | 1600 | A | 1669 | 0.0581 | 0.127 | 0.007 |
| B | G160M | 1600 | A | 1723 | 0.0487 | 0.141 | 0.007 |
| B | G140L | 1230 | A | 1248 | 0.1066 | 0.096 | 0.010 |
| A | G140L | 1230 | A | 1327 | 0.0827 | 0.093 | 0.008 |
| B | G140L | 1230 | A | 1327 | 0.0652 | 0.244 | 0.016 |
| B | G140L | 1230 | A | 1430 | 0.0642 | 0.195 | 0.013 |
| B | G140L | 1230 | A | 1524 | 0.0528 | 0.142 | 0.007 |
| B | G140L | 1230 | A | 1723 | 0.0309 | 0.137 | 0.004 |
| B | G140L | 1230 | A | 1937 | 0.0065 | 0.091 | 0.001 |

Table 5.4-3: COS NUV Efficiency Measurements during 2003 science calibration in vacuum

|  |  |  |  |  |  | COS efficiency |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Appendix | Channel | c (Å) | stripe | Test  (Å) | cts/ph | rel. uncertainty | 1  |
| B | G185M | 1817 | A | 1723 | 0.0320 | 0.123 | 0.004 |
| B | G185M | 1882 | A | 1777 | 0.0394 | 0.103 | 0.004 |
| A | G185M | 1850 | B | 1846 | 0.0355 | 0.084 | 0.003 |
| B | G185M | 1850 | B | 1846 | 0.0377 | 0.117 | 0.004 |
| B | G185M | 1986 | A | 1883 | 0.0364 | 0.083 | 0.003 |
| B | G185M | 1882 | B | 1883 | 0.0372 | 0.083 | 0.003 |
| B | G185M | 1786 | C | 1883 | 0.0360 | 0.083 | 0.003 |
| B | G185M | 1835 | C | 1937 | 0.0322 | 0.075 | 0.002 |
| B | G185M | 1971 | B | 1972 | 0.0292 | 0.087 | 0.003 |
| B | G185M | 1953 | C | 2050 | 0.0255 | 0.085 | 0.002 |
| B | G185M | 1986 | C | 2085 | 0.0230 | 0.074 | 0.002 |
| B | G185M | 2010 | C | 2129 | 0.0196 | 0.075 | 0.001 |
| B | G225M | 2186 | A | 2085 | 0.0140 | 0.077 | 0.001 |
| B | G225M | 2186 | A | 2085 | 0.0137 | 0.075 | 0.001 |
| B | G225M | 2010 | C | 2129 | 0.0165 | 0.074 | 0.001 |
| B | G225M | 2250 | A | 2144 | 0.0169 | 0.076 | 0.001 |
| A | G225M | 2268 | B | 2262 | 0.0231 | 0.065 | 0.002 |
| B | G225M | 2268 | B | 2262 | 0.0266 | 0.074 | 0.002 |
| B | G225M | 2390 | A | 2290 | 0.0263 | 0.075 | 0.002 |
| B | G225M | 2283 | B | 2290 | 0.0271 | 0.075 | 0.002 |
| B | G225M | 2186 | C | 2290 | 0.0266 | 0.075 | 0.002 |
| B | G225M | 2357 | B | 2357 | 0.0301 | 0.067 | 0.002 |
| A | G225M | 2357 | C | 2440 | 0.0254 | 0.064 | 0.002 |
| B | G225M | 2339 | C | 2440 | 0.0292 | 0.067 | 0.002 |
| A | G225M | 2390 | C | 2487 | 0.0248 | 0.070 | 0.002 |
| B | G225M | 2390 | C | 2487 | 0.0288 | 0.074 | 0.002 |
| A | G285M | 2676 | A | 2540 | 0.0181 | 0.066 | 0.001 |
| B | G285M | 2657 | A | 2540 | 0.0200 | 0.068 | 0.001 |
| A | G285M | 2657 | B | 2659 | 0.0189 | 0.063 | 0.001 |
| B | G285M | 2657 | B | 2659 | 0.0218 | 0.070 | 0.002 |
| B | G285M | 2739 | B | 2734 | 0.0205 | 0.086 | 0.002 |
| A | G285M | 2952 | A | 2830 | 0.0152 | 0.098 | 0.001 |
| A | G285M | 2952 | A | 2830 | 0.0153 | 0.098 | 0.001 |
| A | G285M | 2952 | A | 2830 | 0.0149 | 0.098 | 0.001 |
| B | G285M | 2952 | A | 2830 | 0.0174 | 0.102 | 0.002 |
| B | G285M | 2850 | B | 2830 | 0.0172 | 0.102 | 0.002 |
| B | G285M | 2719 | C | 2830 | 0.0170 | 0.102 | 0.002 |
| B | G285M | 2996 | B | 2998 | 0.0105 | 0.115 | 0.001 |
| B | G285M | 3057 | B | 3064 | 0.0089 | 0.105 | 0.001 |
| B | G230L | 2950 | A | 1723 | 0.0235 | 0.128 | 0.003 |
| B | G230L | 3000 | A | 1846 | 0.0303 | 0.119 | 0.004 |
| B | G230L | 3000 | A | 2050 | 0.0306 | 0.086 | 0.003 |
| B | G230L | 3360 | A | 2085 | 0.0303 | 0.078 | 0.002 |
| A | G230L | 3360 | A | 2262 | 0.0246 | 0.065 | 0.002 |
| B | G230L | 3360 | A | 2262 | 0.0273 | 0.076 | 0.002 |
| B | G230L | 2635 | B | 2487 | 0.0232 | 0.075 | 0.002 |
| B | G230L | 2635 | B | 2659 | 0.0204 | 0.066 | 0.001 |
| B | G230L | 2950 | B | 2830 | 0.0143 | 0.103 | 0.001 |
| B | G230L | 3000 | B | 2998 | 0.0079 | 0.116 | 0.001 |
| B | TA1 |  | A | 1248 | 4.88E-05 | 0.154 | 0.000 |
| B | TA1 |  | A | 1524 | 6.17E-05 | 0.130 | 0.000 |
| B | TA1 |  | A | 1723 | 0.0483 | 0.131 | 0.006 |
| B | TA1 |  | A | 1846 | 0.0594 | 0.116 | 0.007 |
| B | TA1 |  | A | 2262 | 0.0512 | 0.076 | 0.004 |
| A | TA1 |  | A | 2487 | 0.0424 | 0.070 | 0.003 |
| B | TA1 |  | A | 2487 | 0.0473 | 0.075 | 0.004 |
| B | TA1 |  | A | 2830 | 0.0323 | 0.103 | 0.003 |
| B | TA1 |  | A | 2998 | 0.0198 | 0.124 | 0.002 |
| B | TA1-BRT |  | A | 1248 | 0.0008 | 0.110 | 0.000 |
| B | TA1-BRT |  | A | 1524 | 0.0023 | 0.078 | 0.000 |
| B | TA1-BRT |  | A | 1723 | 0.0043 | 0.101 | 0.000 |
| B | TA1-BRT |  | A | 2262 | 0.0028 | 0.078 | 0.000 |
| A | TA1 BRT |  | A | 2487 | 0.0031 | 0.070 | 0.000 |
| B | TA1-BRT |  | A | 2487 | 0.0032 | 0.077 | 0.000 |
| B | TA1-BRT |  | A | 2998 | 0.0012 | 0.114 | 0.000 |

Figure 5.4-1: Efficiency plots for each channel representing the data in Tables Table 5.4-2 and Table 5.4-3.

### 2003 Results – 2nd Order Efficiencies

The light that falls on a given pixel of the detector satisfies the condition that m = constant, where m is the order of diffraction and  is the wavelength of light. The numerical value of the constant is determined by the groove spacing of the grating and the angles of incidence and diffraction. All of the spectroscopic modes of COS were designed to operate in the first order of diffraction, m=1. Wavelengths whose products with m=2, m=3 etc. equal the same constant will overlap the m=1 spectra at the same pixel locations. If these wavelengths can be transmitted by the optical system and registered by the detector they will create a confusing mixture of spectral features. This effect is known as 2nd order overlap. COS minimizes this problem using several factors.

The FUV channel is not susceptible to higher order overlap. The optics of COS and HST are coated with Al and MgF2. These surfaces do not reflect wavelengths  < 1150Å with significant efficiency. Multiple reflections essentially eliminate these short wavelengths.  The FUV detector is used between 1150Å <  < 1775Å for the M gratings, and is only required to work between 1230Å <  < 1800Å for G140L. The longest wavelength that could overlap is 900Å, which is not reflected by the optical system.

The HST optics reflect all wavelengths longward of 1150Å with good efficiency. The NUV MAMA detector responds well to light in the range 1150Å <  < 3200Å. Therefore the NUV modes designed for m ≥ 2300Å when m=1 will be vulnerable to 2nd order overlap when m=2 and  >1150Å. COS is not susceptible to 3rd order light, since it is not intended to observe  ≥ 3450Å. No second order light can reach G185M. Modes G225M, G285M and G230L are susceptible to overlap, and two means were provided to attenuate the second order light. All of the NUV optics were coated with a version of Al + MgF2 whose reflectivity decreases strongly shortward of 1650Å. The net throughput for four reflections is less than 1% for wavelengths  < 1250Å. All second order light within the required wavelength range of G225M is attenuated, but not extinguished, this way. Gratings G285M and G230L operate at longer wavelengths where the reflectivity of the optics and the sensitivity of the NUV detector are both high. A 2mm thick fused silica order sorter was placed in front of the gratings, so that the light makes two passes through the filter before reaching the detector. UV grade fused silica transmits well for  > 1700Å, but is almost totally opaque for  < 1600Å. We therefore expect no significant second order overlap for these gratings for  < 3200Å.

Test number 1265 was run during the Appendix B phase to measure the 2nd order throughput of G225M, G285M and G230L. The experimental setup and data reduction was the same as for the normal sensitivity measurements. An FUV line from the Pt-Ne lamp was isolated by the monochromator, its flux was measured by the RASCAL PMT, and its count rate was recorded with the appropriate COS NUV mode where it might show up in 2nd order. Exposure times were all 10 minutes. All data were of high quality. Of the nine measurements made, positive detections of the 2nd order image were obtained only for two wavelengths with G225M. No 2nd order light was detected for G285M or G230L, confirming that the order sorter filter performed properly. One complication in the data analysis was that the 1st order spectrum of the Pt-Ne lamp appears faintly in the data. The FUV grating in the monochromator is not of very high quality, and light of all wavelengths from the lamp gets scattered into the exit slit at low levels. We compared the spectrum of the region expected to contain the 2nd order image with high quality 1st order spectra of the Pt-Ne lamp obtained with other tests, and unambiguously identified the features due to overlapping 2nd order light.

#### Results for G225M:

Light with wavelength 1219Å was detected in 2nd order with a throughput of 1.12 x 10-4. Light with wavelength 1249Å was detected in 2nd order with a throughput of 3.73 x 10-4.

The measured response of G225M to 1st order light at 2440Å was 0.03 (270 and 80 times higher). The FUV grating G130M detected 1219Å and 1248Å in 1st order with efficiencies near 0.12 (over 1000 and 300 times higher).

#### Results for G285M and G230L:

No 2nd order images were detected. Judging from the quality of the NUV spectra a very generous upper limit of 10 counts in 600 seconds can be allowed. This gives an upper limit 10-6 for any 2nd order throughput for these gratings.

#### Conclusions:

The Appendix B calibration results confirm that the design of COS avoided any problems with spectral contamination from higher orders of diffraction. None of the FUV gratings are susceptible, nor is G185M. G225M has a small throughput between 2300Å <  < 2500Å, which was agreed to be acceptable during the trade studies that led to its design. The order sorters of G285M and G230L block all higher order light within their required wavelength bands.

### 2003 Results – 1st Order Efficiencies w/ FUV Detector QE Grid Off

Two data sets were acquired where the sensitivity of the FUV channel was measured with the FUV detector QE grid off.  In test 1240 monochromatic emission lines were used.  In tests 1110 and 2750 full spectra were acquired.  This test was run for informational purposes, not to demonstrate a CEI requirement.

Tests:	1240 – FUV sensitivity with QE Grid Off

1110 – PtNe Group 1 Spectra (grid on)

2750 – PtNe Group 1 Spectra (grid off)

Relevant Exposures:

Table 5.4-4:  Exposure list for 2003 FUV detector QE tests.

| File | Date | Test # | Channel | c | Test  |
| --- | --- | --- | --- | --- | --- |
| CSIL03284222027 | 10/11/03 | 1240 | G130M | 1309 | 1216 |
| CSIL03284223956 | 10/11/03 | 1240 | G130M | 1309 | 1379 |
| CSIL03284225425 | 10/11/03 | 1240 | G160M | 1600 | 1482 |
| CSIL03284230556 | 10/11/03 | 1240 | G160M | 1600 | 1669 |
| CSIL03286020938 | 10/12/03 | 1110 | G130M | 1309 | PSA |
| CSIL03286021646 | 10/12/03 | 1110 | G130M | 1309 | WCA |
| CSIL03286033938 | 10/12/03 | 1110 | G160M | 1600 | PSA |
| CSIL03286034546 | 10/12/03 | 1110 | G160M | 1600 | WCA |
| CSIL03286050338 | 10/12/03 | 1110 | G140L | 1230 | PSA |
| CSIL03286064155 | 10/13/03 | 2750 | G130M | 1309 | WCA |
| CSIL03286064903 | 10/13/03 | 2750 | G130M | 1309 | PSA |
| CSIL03286072355 | 10/13/03 | 2750 | G160M | 1600 | WCA |
| CSIL03286073003 | 10/13/03 | 2750 | G160M | 1600 | PSA |
| CSIL03286060155 | 10/13/03 | 2750 | G140L | 1230 | WCA |

Note: where PSA or WCA is called out for the wavelength the entire detector image was used to compute the count rate.  PtNe spectra were used in all cases.

Should the situation arise where the FUV DQE enhancement grid must be turned off due to anomalous operating conditions, e.g. excessive coronal emission, the sensitivity of COS was measured at 4 wavelengths with the DQE grid off.  The DQE enhancement grid forces photoelectrons generated between MCP pores back onto the MCP, thus increasing the probability of initiating an electron cascade in the stack.  Thus, the DQE is increased by 30-40%.

The sensitivities of COS with the DQE grid off were measured as follows:

FUV DQE Measurement Notes with QE GRID OFF

G130M_A: 6712 counts in 200 sec in spectral region on FUV detector

PMT rate = (54.0+51.4)/2 = 52.7 cps

PMT QE at 1379Å is 0.068

QE = 33.56/((52.7-19.9)/0.068) = 0.0696

The 19.9 cps represents out of band light as measured

with a CaF filter in place

G130M_B: 19379 counts in 100 seconds

PMT rate = (239.0+234.8)/2 = 236.9 cps

PMT QE at 1216Å is 0.117

QE = 193.79/((236.9-39.0)/0.117) = 0.1146

The 39 cps represents out of band light as measured

with a CaF filter in place

G160M_A: 2152 counts in 100 seconds

PMT rate = (62.8+71.3)/2 = 67.06 cps

PMT QE at 1669Å is 0.138

QE = 21.52/(67.06/0.138) = 0.0443

G160M_B: 6002 counts in 100 seconds

PMT rate = (60.8+62.7)/2 = 61.75 cps

PMT QE at 1482Å is 0.0803

QE = 60.02/(61.75/0.0802) = 0.0780

Now, the QE as measured for those wavelengths with the QE grid ON (see previous sections) are....

G130M_A: 1379Å -> 0.1042

G130M_B: 1216Å -> 0.1975

G160M_A: 1669Å -> 0.0581

G160M_B: 1482Å -> 0.1114

Forming the ratio of (ON-OFF)/ON measures the QE contribution from the web:

G130M_A: 0.33

G130M_B: 0.42

G160M_A: 0.24

G160M_B: 0.30

Evaluating the data acquired during tests 1110 and 2750 yields a similar result.  In this case the total counts in each PSA or WCA were used to calculate the contribution from the web.  The results are shown Table 4.4-3 below.  All results are consistent with expectations.

Table 5.4-5: Raw Data and Final Results for FUV DQE with the FUV Detector QE Grid ON and OFF.

| File | Channel | c | Aperture | Seg. | Count Rate |
| --- | --- | --- | --- | --- | --- |
| QE GRID ON |  |  |  |  |  |
| CSIL03286020938_1_rawtag_a_gc.fits | G130M | 1309 | PSA-FUV | FUVA | 382.587 |
| CSIL03286020938_1_rawtag_b_gc.fits | G130M | 1309 | PSA-FUV | FUVB | 607.517 |
| CSIL03286021646_1_rawtag_a_gc.fits | G130M | 1309 | WCA-FUV | FUVA | 242.05 |
| CSIL03286021646_1_rawtag_b_gc.fits | G130M | 1309 | WCA-FUV | FUVB | 167.017 |
| CSIL03286033938_1_rawtag_a_gc.fits | G160M | 1600 | PSA-FUV | FUVA | 179.777 |
| CSIL03286033938_1_rawtag_b_gc.fits | G160M | 1600 | PSA-FUV | FUVB | 723.68 |
| CSIL03286034546_1_rawtag_a_gc.fits | G160M | 1600 | WCA-FUV | FUVA | 238.35 |
| CSIL03286034546_1_rawtag_b_gc.fits | G160M | 1600 | WCA-FUV | FUVB | 710.367 |
| CSIL03286050338_1_rawtag_a_gc.fits | G140L | 1230 | PSA-FUV | FUVA | 1442.03 |
| CSIL03286051016_1_rawtag_a_gc.fits | G140L | 1230 | WCA-FUV | FUVA | 914.833 |
| QE GRID OFF |  |  |  |  |  |
| CSIL03286064155_1_rawtag_a_gc.fits | G130M | 1309 | PSA-FUV | FUVA | 287.388 |
| CSIL03286064155_1_rawtag_b_gc.fits | G130M | 1309 | PSA-FUV | FUVB | 445.053 |
| CSIL03286064903_1_rawtag_a_gc.fits | G130M | 1309 | WCA-FUV | FUVA | 175.925 |
| CSIL03286064903_1_rawtag_b_gc.fits | G130M | 1309 | WCA-FUV | FUVB | 120.658 |
| CSIL03286072355_1_rawtag_a_gc.fits | G160M | 1600 | PSA-FUV | FUVA | 135.977 |
| CSIL03286072355_1_rawtag_b_gc.fits | G160M | 1600 | PSA-FUV | FUVB | 513.788 |
| CSIL03286073003_1_rawtag_a_gc.fits | G160M | 1600 | WCA-FUV | FUVA | 185.45 |
| CSIL03286073003_1_rawtag_b_gc.fits | G160M | 1600 | WCA-FUV | FUVB | 537.217 |
| CSIL03286060155_1_rawtag_a_gc.fits | G140L | 1230 | PSA-FUV | FUVA | 1078.87 |
| CSIL03286060833_1_rawtag_a_gc.fits | G140L | 1230 | WCA-FUV | FUVA | 708.211 |
| Contribution to DQE by MCP web: | Channel | c | Aperture | Seg. | Web Contrib. |
| Web contribution = (ON-OFF)/ON | G130M | 1309 | PSA-FUV | FUVA | 0.25 |
| (ON is with QE grid on and | G130M | 1309 | PSA-FUV | FUVB | 0.27 |
| OFF is with QE grid off) | G130M | 1309 | WCA-FUV | FUVA | 0.27 |
|  | G130M | 1309 | WCA-FUV | FUVB | 0.28 |
|  | G160M | 1600 | PSA-FUV | FUVA | 0.24 |
|  | G160M | 1600 | PSA-FUV | FUVB | 0.29 |
|  | G160M | 1600 | WCA-FUV | FUVA | 0.22 |
|  | G160M | 1600 | WCA-FUV | FUVB | 0.24 |
|  | G140L | 1230 | PSA-FUV | FUVA | 0.25 |
|  | G140L | 1230 | WCA-FUV | FUVA | 0.23 |

### 2006 Sensitivity Measurements

The sensitivity observations made in Appendix B were repeated in Appendix C with the same test execution (but with the new CDS hardware). The analysis of the data was also repeated in the same manner.  The RASCAL CsTe photo-multiplier tube (PMT) used as the reference detector was recalibrated at LASP prior to the 2006 observations. The PMT calibration data is recorded in COS-11-0042 entitled “Calibration Report for the RAS/Cal CsTe Photo-Multiplier Tube.”  The FUV sensitivity tests with the QE detector grid turned off were not repeated in 2006. The 2006 CDS had better gratings and much lower scattered light which led to reduced uncertainties on the sensitivity measurements.

Tests:	1210	G130M Sensitivity

1220	G160M Sensitivity

1230	G140L Sensitivity

1250	G185M Sensitivity

1255	G185M/G225M Sensitivity

1260	G225M Sensitivity

1270	G285M Sensitivity

1280	G230L Sensitivity

1290	TA1 Sensitivity

1295	TA1-BRT Sensitivity

The sensitivity measurements are given in Table 5.4-6 and Table 5.4-7 for the FUV and NUV, respectively.  The sensitivities are shown graphically in Figure 5.4-2 and Figure 5.4-3 for both the 2003 and 2006 data.  Figure 5.4-4 shows the percentage change between 2003 and 2006 for each grating.

Figure 4.4-3 shows substantial changes in reported throughputs between the 2003 and 2006 calibrations.  We believe that the increase in throughput at shorter wavelengths is at least partially an artifact of the test setup, while the long wavelength performance changes are attributable to changes in the instrument performance.

The ~10-44% increase in reported FUV throughput between 1300Å and 1500Å is probably due to a change in the polarization content in the calibration beam at these wavelengths.  While it is difficult to say if the 2006 or 2003 short wavelength data is more reliable, the 44% increase in the G140L 1327Å is not consistent with component level measurements, casting doubt on the 2006 values.  Furthermore, the polarization scrambler used to randomize the polarization of the 2006 CDS output was not completely effective at shorter wavelengths, and design constraints imposed by the need to place the CDS in vacuum in 2006 lead to a design which was more prone to polarization than the previous incarnation.

At  wavelengths longer than 1600Å we were able to measure the polarization content of the 2006 calibration beam and note that it was effectively unpolarized, while no measurements were made of the 2003 CDS polarization content.  In addition, the instrument sensitivity to polarized light was directly measured in 2007 at wavelengths beyond 2200Å and the unpolarized response was found to match the 2006 thermal vacuum data.  Consequently, the 2006 data is considered more reliable than the 2003 data for wavelengths longer than 1600Å.

The general decrease in apparent throughput at longer wavelengths could be due to the change in polarization content of the calibration beam, with the 2003 values being artificially high.  The change in the G225M and G285M grating throughputs departs substantially from the G230L and TA1 throughput changes and is believed to be due to a slow oxide growth on the bare aluminum optics.  This would change their sensitivity as a function of polarization, effectively reducing sensitivity to unpolarized light.  These results are discussed in separate documents: COS-11-0045a, COS-11-048 and COS-11-0049. Note that despite the drop in sensitivity, all the gratings continue to meet their CEI specifications on performance.

Table 5.4-6: 2006 FUV Sensitivity Measurements

|  |  |  |  |  |  | COS efficiency |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Appendix | Channel | c (Å) | Segment | Test  (Å) | cts/ph | rel. uncertainty | 1  |
| C | G130M | 1309 | B | 1216 | 0.1852 | 0.081 | 0.015 |
| C | G130M | 1309 | B | 1248 | 0.1735 | 0.098 | 0.017 |
| C | G130M | 1309 | A | 1327 | 0.1382 | 0.047 | 0.006 |
| C | G130M | 1309 | A | 1379 | 0.1291 | 0.047 | 0.006 |
| C | G130M | 1309 | A | 1430 | 0.1115 | 0.048 | 0.005 |
| C | G130M | 1309 | A | 1430 | 0.1086 | 0.056 | 0.006 |
| C | G160M | 1600 | B | 1430 | 0.1306 | 0.054 | 0.007 |
| C | G160M | 1600 | B | 1482 | 0.1099 | 0.056 | 0.006 |
| C | G160M | 1600 | B | 1524 | 0.0995 | 0.049 | 0.005 |
| C | G160M | 1600 | A | 1621 | 0.0574 | 0.056 | 0.003 |
| C | G160M | 1600 | A | 1669 | 0.0505 | 0.053 | 0.003 |
| C | G160M | 1600 | A | 1723 | 0.0399 | 0.060 | 0.002 |
| C | G140L | 1230 | A | 1248 | 0.1041 | 0.137 | 0.014 |
| C | G140L | 1230 | A | 1327 | 0.0943 | 0.135 | 0.013 |
| C | G140L | 1230 | A | 1430 | 0.0699 | 0.083 | 0.006 |
| C | G140L | 1230 | A | 1524 | 0.0530 | 0.054 | 0.003 |
| C | G140L | 1230 | A | 1723 | 0.0263 | 0.066 | 0.002 |
| C | G140L | 1230 | A | 1937 | 0.0049 | 0.052 | 0.0003 |

Table 5.4-7: 2006 NUV Sensitivity Measurements

|  |  |  |  |  |  | COS Efficiency |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Appendix | Channel | c (Å) | Stripe | Test c (Å) | cts/ph | rel. uncertainty | 1 |
| C | G185M | 1817 | A | 1723 | 0.0293 | 0.056 | 0.002 |
| C | G185M | 1882 | A | 1777 | 0.0338 | 0.045 | 0.002 |
| C | G185M | 1850 | B | 1846 | 0.0327 | 0.049 | 0.002 |
| C | G185M | 1986 | A | 1883 | 0.0299 | 0.047 | 0.001 |
| C | G185M | 1882 | B | 1883 | 0.0303 | 0.047 | 0.001 |
| C | G185M | 1786 | C | 1883 | 0.0294 | 0.047 | 0.001 |
| C | G185M | 1835 | C | 1937 | 0.0283 | 0.049 | 0.001 |
| C | G185M | 1971 | B | 1972 | 0.0238 | 0.062 | 0.002 |
| C | G185M | 1953 | C | 2050 | 0.0219 | 0.061 | 0.001 |
| C | G185M | 1986 | C | 2085 | 0.0191 | 0.058 | 0.001 |
| C | G185M | 2010 | C | 2129 | 0.0173 | 0.058 | 0.001 |
| C | G225M | 2186 | A | 2085 | 0.0127 | 0.059 | 0.0007 |
| C | G225M | 2186 | A | 2085 | 0.0119 | 0.059 | 0.0009 |
| C | G225M | 2010 | C | 2129 | 0.0151 | 0.058 | 0.0009 |
| C | G225M | 2250 | A | 2144 | 0.0147 | 0.060 | 0.0009 |
| C | G225M | 2268 | B | 2262 | 0.0211 | 0.058 | 0.001 |
| C | G225M | 2390 | A | 2290 | 0.0217 | 0.058 | 0.001 |
| C | G225M | 2283 | B | 2290 | 0.0221 | 0.058 | 0.001 |
| C | G225M | 2186 | C | 2290 | 0.0210 | 0.059 | 0.001 |
| C | G225M | 2357 | B | 2357 | 0.0301 | 0.067 | 0.002 |
| C | G225M | 2339 | C | 2440 | 0.0239 | 0.063 | 0.002 |
| C | G225M | 2390 | C | 2487 | 0.0232 | 0.061 | 0.001 |
| C | G285M | 2657 | A | 2540 | 0.0142 | 0.062 | 0.0009 |
| C | G285M | 2657 | B | 2659 | 0.0166 | 0.059 | 0.001 |
| C | G285M | 2739 | B | 2734 | 0.0149 | 0.064 | 0.001 |
| C | G285M | 2952 | A | 2830 | 0.0135 | 0.094 | 0.001 |
| C | G285M | 2850 | B | 2830 | 0.0139 | 0.094 | 0.001 |
| C | G285M | 2719 | C | 2830 | 0.0138 | 0.094 | 0.001 |
| C | G285M | 2996 | B | 2998 | 0.0091 | 0.089 | 0.0008 |
| C | G285M | 3057 | B | 3064 | 0.0078 | 0.086 | 0.0007 |
| C | G230L | 2950 | A | 1723 | 0.0202 | 0.055 | 0.001 |
| C | G230L | 3000 | A | 1846 | 0.0261 | 0.048 | 0.001 |
| C | G230L | 3000 | A | 2050 | 0.0257 | 0.061 | 0.002 |
| C | G230L | 3360 | A | 2085 | 0.0255 | 0.060 | 0.0002 |
| C | G230L | 3360 | A | 2262 | 0.0242 | 0.061 | 0.002 |
| C | G230L | 2635 | B | 2487 | 0.0207 | 0.061 | 0.001 |
| C | G230L | 2635 | B | 2659 | 0.0181 | 0.060 | 0.001 |
| C | G230L | 2950 | B | 2830 | 0.0128 | 0.094 | 0.001 |
| C | G230L | 3000 | B | 2998 | 0.0075 | 0.157 | 0.001 |
| C | TA1 |  | A | 1248 | 4.88E-05 | 0.154 | 0.000 |
| C | TA1 |  | A | 1524 | 6.17E-05 | 0.130 | 0.000 |
| C | TA1 |  | A | 1723 | 0.0401 | 0.055 | 0.002 |
| C | TA1 |  | A | 1846 | 0.0491 | 0.044 | 0.002 |
| C | TA1 |  | A | 2262 | 0.0466 | 0.058 | 0.003 |
| C | TA1 |  | A | 2487 | 0.0420 | 0.060 | 0.002 |
| C | TA1 |  | A | 2830 | 0.0314 | 0.094 | 0.003 |
| C | TA1 |  | A | 2998 | 0.0198 | 0.089 | 0.002 |
| C | TA1-BRT |  | A | 1248 | 0.0008 | 0.143 | 0.0001 |
| C | TA1-BRT |  | A | 1524 | 0.0032 | 0.049 | 0.0002 |
| C | TA1-BRT |  | A | 1723 | 0.0054 | 0.056 | 0.0003 |
| C | TA1-BRT |  | A | 2262 | 0.0037 | 0.061 | 0.0002 |
| C | TA1-BRT |  | A | 2487 | 0.0034 | 0.054 | 0.0002 |
| C | TA1-BRT |  | A | 2998 | 0.0014 | 0.091 | 0.0001 |

Figure 5.4-2: FUV sensitivity measurements in 2003 and 2006.  The 2003 measurements are shown in dark blue and the 2006 measurements in light blue. The CEI specifications are shown as lines on the grating plots:  the solid line is the CEI maximum (which must be exceeded at one wavelength) and the dotted line is the CEI minimum (which must be exceeded at all wavelengths).

Figure 5.4-3:  NUV sensitivity measurements in 2003 and 2006.  The 2003 measurements are shown in dark blue and the 2006 measurements in light blue.  The points in pink were repeated measurements in 2006. The CEI specifications are shown as lines on the grating plots:  the solid line is the CEI maximum (which must be exceeded at one wavelength) and the dotted line is the CEI minimum (which must be exceeded at all wavelengths).

Figure 5.4-4:  Percent change in measured COS throughput between 2003 and 2006 observations.

## Bright Object aperture transmission

### CEI Requirement

Section 4.2.6 and Table 4.5 of the CEI specification list the specific requirements for the COS bright object aperture (BOA).  For the purposes of this discussion, the BOA must have transmission of no more than 1% across the FUV and NUV band passes (e.g. >ND2).

### 2003 Test Description & Data Reduction

The transmission of the BOA was computed by dividing the observed counts from an external lamp through the primary science aperture (PSA) into the observed counts of the same light source through the BOA, with an appropriate scaling for the difference in exposure times (PSA observations consisted of two 120 second exposures and the BOA observation consisted of a single 1800 second exposure).  The transmission at FUV wavelengths was measured during Test 3300 using the G140L channel.  The NUV transmission was measured during Tests 3310 and 3310A using the three wavelength settings of the G230L channel.  Tests 3300 and 3310 were conducted using an external PtNe lamp through the CDS.  Test 3310A used an external D2 lamp through the CDS.

Test 3310 was originally thought to be sufficient to characterize the BOA transmission function.  However, a preliminary evaluation of the data suggested that differences in the spectral resolution between the PSA and BOA were introducing noise into the calculation.  Therefore, Test 3310A was initiated using a D2 continuum lamp instead of the PtNe line lamp, thus eliminating variations in the spectral resolution as a concern.  Ultimately both tests produced similar results.

For each test the spectra were extracted and binned from ~14000 spectral bins to 16 bins for the FUV data or 1024 to 16 for the NUV data.  This increased the number of counts per bin, decreasing the statistical error in the computation of the transmission.  The data were then scaled by 240/1800 to account for the differences in exposure times.  PSA data from before and after the BOA exposures were used, thus the 240 or 2x120.  The mathematical expressions for the transmission and error in the transmission are as follows;

In this case CBOA and CPSA are the measured counts in a given spectral bin.  Cbkgnd is the background counts for a similarly sized spectral bin.

### FUV Channel

Tests: 	3300 – FUV BOA Throughput and Resolution

Relevant Exposures:

Table 5.5-1: Exposure list for 2003 FUV BOA throughput and resolution tests.

| Test 3300 | Description |
| --- | --- |
| CSIL03285204854 | c=1320,PSA,texp=120 sec |
| CSIL03285213104 | c=1320,BOA,texp=1800 sec |
| CSIL03285214514 | c=1320,PSA,texp=120 sec |

#### 2003 Results

Table 4.5-1 and Figure 4.5-1 (at the end of this section) show the wavelength, transmission (T), and statistical error (T) for Test 3300 in tabular and graphical format respectively.

Table 5.5-2: Results for Test 3300

| (Å) | T | T |
| --- | --- | --- |
| 1227.96 | 0.00726 | 0.00012 |
| 1309.88 | 0.00916 | 0.00017 |
| 1391.8 | 0.00634 | 0.00015 |
| 1473.72 | 0.00636 | 0.00010 |
| 1555.64 | 0.00762 | 0.00019 |
| 1637.56 | 0.00645 | 0.00025 |
| 1719.48 | 0.00624 | 0.00027 |
| 1801.4 | 0.00583 | 0.00019 |
| 1883.32 | 0.00638 | 0.00028 |
| 1965.24 | 0.00630 | 0.00028 |
| 2047.16 | 0.00604 | 0.00061 |
| 2129.08 | 0.01102 | 0.00147 |
| 2211 | 0.01547 | 0.00420 |
| 2292.92 | 0.03945 | 0.01454 |
| 2374.84 | 0.02888 | 0.01466 |
| 2456.76 | 0.00981 | 0.00275 |

### NUV Channel

Tests:	3310, 3310A – NUV BOA Transmission and Resolution

Relevant Exposures:

Table 5.5-3: Exposure list for 2003 NUV BOA transmission and resolution tests.

| Test 3310 | Test 3310A | Description |
| --- | --- | --- |
| CSIL03267204612 | CSIL03273163316 | c=3000, PSA, texp=120 s |
| CSIL03267212608 | CSIL03273171312 | c=3000, BOA, texp=1800 s |
| CSIL03267213804 | CSIL03273172508 | c=3000, PSA, texp=120 s |
| CSIL03267215058 | CSIL03273173802 | c=3360, PSA, texp=120 s |
| CSIL03267223054 | CSIL03273181758 | c=3360, BOA, texp=1800 s |
| CSIL03267224250 | CSIL03273182954 | c=3360, PSA, texp=120 s |
| CSIL03267225544 | CSIL03273184248 | c=2635, PSA, texp=120 s |
| CSIL03267233540 | CSIL03273192244 | c=2635, BOA, texp=1800 s |
| CSIL03267234736 | CSIL03273193440 | c=2635, PSA, texp=120 s |

#### 2003 Results

Tables 4.5-2 and 4.5-3 present the transmission as computed from Test 3310 and 3310A respectively.  Figure 1 shows the wavelength, transmission (T), and statistical error (T) for Test 3310A, while Figure 4.5-2 shows the transmission computed from Test 3310.

Table 5.5-4: Results for Test 3310 – PtNe line lamp spectra

| c = 2635, Stripe A | c = 3000, Stripe A |
| --- | --- |
| (Å) | T | T | (Å) | T | T |
| 2745.14 | 0.00466 | 0.00028 | 2027.06 | 0.00653 | 0.00058 |
| 2720.18 | 0.00458 | 0.00028 | 2002.03 | 0.00663 | 0.00059 |
| 2695.21 | 0.00458 | 0.00028 | 1977 | 0.00573 | 0.00055 |
| 2670.24 | 0.00462 | 0.00028 | 1951.97 | 0.00585 | 0.00056 |
| 2645.28 | 0.00434 | 0.00027 | 1926.94 | 0.00587 | 0.00055 |
| 2620.31 | 0.00457 | 0.00028 | 1901.91 | 0.00780 | 0.00065 |
| 2595.34 | 0.00441 | 0.00027 | 1876.88 | 0.00653 | 0.00057 |
| 2570.38 | 0.00425 | 0.00027 | 1851.85 | 0.00621 | 0.00057 |
| 2545.41 | 0.00446 | 0.00028 | 1826.82 | 0.00557 | 0.00054 |
| 2520.44 | 0.00443 | 0.00027 | 1801.79 | 0.00618 | 0.00056 |
| 2495.48 | 0.00439 | 0.00027 | 1776.76 | 0.00615 | 0.00057 |
| 2470.51 | 0.00409 | 0.00026 | 1751.72 | 0.00603 | 0.00056 |
| 2445.55 | 0.00438 | 0.00027 | 1726.69 | 0.00679 | 0.00059 |
| 2420.58 | 0.00429 | 0.00027 | 1701.66 | 0.00538 | 0.00053 |
| 2745.14 | 0.00466 | 0.00028 | 2027.06 | 0.00653 | 0.00058 |
| 2720.18 | 0.00458 | 0.00028 | 2002.03 | 0.00663 | 0.00059 |
| c = 3000, Stripe B | c = 3360, Stripe A |
| (Å) | T | T | (Å) | T | T |
| 3165.37 | 0.00373 | 0.00032 | 2441.51 | 0.00517 | 0.00035 |
| 3140.42 | 0.00392 | 0.00032 | 2416.49 | 0.00553 | 0.00036 |
| 3115.46 | 0.00408 | 0.00033 | 2391.48 | 0.00516 | 0.00034 |
| 3090.51 | 0.00399 | 0.00032 | 2366.46 | 0.00478 | 0.00033 |
| 3065.56 | 0.00382 | 0.00031 | 2341.44 | 0.00529 | 0.00035 |
| 3040.6 | 0.00373 | 0.00031 | 2316.42 | 0.00569 | 0.00036 |
| 3015.65 | 0.00429 | 0.00033 | 2291.41 | 0.00483 | 0.00033 |
| 2990.69 | 0.00369 | 0.00031 | 2266.39 | 0.00517 | 0.00034 |
| 2965.74 | 0.00388 | 0.00032 | 2241.37 | 0.00504 | 0.00034 |
| 2940.79 | 0.00424 | 0.00033 | 2216.35 | 0.00531 | 0.00035 |
| 2915.83 | 0.00400 | 0.00032 | 2191.34 | 0.00539 | 0.00035 |
| 2890.88 | 0.00419 | 0.00033 | 2166.32 | 0.00498 | 0.00034 |
| 2865.93 | 0.00372 | 0.00031 | 2141.3 | 0.00567 | 0.00036 |
| 2840.97 | 0.00419 | 0.00033 | 2116.28 | 0.00485 | 0.00034 |
| 2816.02 | 0.00429 | 0.00033 | 2091.27 | 0.00536 | 0.00035 |
| 2791.07 | 0.00400 | 0.00032 | 2066.25 | 0.00534 | 0.00035 |

Table 5.5-5: Results for Test 3310A – D2 continuum lamp spectra

| c = 2635, Stripe A | c = 3000, Stripe A |
| --- | --- |
| (Å) | T | T | (Å) | T | T |
| 2795.08 | 0.00455 | 0.00032 | 2077.12 | 0.00619 | 0.00043 |
| 2770.11 | 0.00436 | 0.00031 | 2052.09 | 0.00660 | 0.00044 |
| 2745.14 | 0.00490 | 0.00033 | 2027.06 | 0.00627 | 0.00044 |
| 2720.18 | 0.00494 | 0.00033 | 2002.03 | 0.00604 | 0.00043 |
| 2695.21 | 0.00455 | 0.00032 | 1977 | 0.00557 | 0.00041 |
| 2670.24 | 0.00435 | 0.00031 | 1951.97 | 0.00589 | 0.00042 |
| 2645.28 | 0.00473 | 0.00032 | 1926.94 | 0.00613 | 0.00043 |
| 2620.31 | 0.00487 | 0.00033 | 1901.91 | 0.00600 | 0.00042 |
| 2595.34 | 0.00475 | 0.00033 | 1876.88 | 0.00595 | 0.00043 |
| 2570.38 | 0.00422 | 0.00031 | 1851.85 | 0.00636 | 0.00043 |
| 2545.41 | 0.00432 | 0.00031 | 1826.82 | 0.00625 | 0.00044 |
| 2520.44 | 0.00457 | 0.00032 | 1801.79 | 0.00629 | 0.00044 |
| 2495.48 | 0.00420 | 0.00031 | 1776.76 | 0.00572 | 0.00042 |
| 2470.51 | 0.00441 | 0.00031 | 1751.72 | 0.00627 | 0.00044 |
| 2445.55 | 0.00484 | 0.00033 | 1726.69 | 0.00586 | 0.00042 |
| 2420.58 | 0.00430 | 0.00031 | 1701.66 | 0.00634 | 0.00044 |
| c = 3000, Stripe B | c = 3360, Stripe A |
| (Å) | T | T | (Å) | T | T |
| 3165.37 | 0.00525 | 0.00058 | 2441.51 | 0.00486 | 0.00028 |
| 3140.42 | 0.00356 | 0.00049 | 2416.49 | 0.00527 | 0.00029 |
| 3115.46 | 0.00362 | 0.00049 | 2391.48 | 0.00560 | 0.00031 |
| 3090.51 | 0.00426 | 0.00051 | 2366.46 | 0.00499 | 0.00029 |
| 3065.56 | 0.00473 | 0.00056 | 2341.44 | 0.00548 | 0.00030 |
| 3040.6 | 0.00514 | 0.00059 | 2316.42 | 0.00524 | 0.00030 |
| 3015.65 | 0.00404 | 0.00053 | 2291.41 | 0.00526 | 0.00029 |
| 2990.69 | 0.00486 | 0.00055 | 2266.39 | 0.00532 | 0.00029 |
| 2965.74 | 0.00469 | 0.00055 | 2241.37 | 0.00505 | 0.00029 |
| 2940.79 | 0.00418 | 0.00052 | 2216.35 | 0.00532 | 0.00029 |
| 2915.83 | 0.00471 | 0.00055 | 2191.34 | 0.00523 | 0.00029 |
| 2890.88 | 0.00442 | 0.00053 | 2166.32 | 0.00515 | 0.00029 |
| 2865.93 | 0.00496 | 0.00056 | 2141.3 | 0.00537 | 0.00030 |
| 2840.97 | 0.00445 | 0.00054 | 2116.28 | 0.00538 | 0.00030 |
| 2816.02 | 0.00486 | 0.00056 | 2091.27 | 0.00569 | 0.00031 |
| 2791.07 | 0.00425 | 0.00052 | 2066.25 | 0.00541 | 0.00030 |

Figure 5.5-1: FUV and NUV BOA transmission computed from data acquired during Tests 3300 and 3310A.

Figure 5.5-2: NUV BOA transmission computed from data acquired from Test 3310.

### 2006 Test Results

Tests:	3300 – FUV BOA transmission and resolution

### 3310 – NUV BOA transmission and resolution

#### FUV

One set of G140L exposures (central wavelength = 1230 Å) allow us to quantify the BOA transmission across the FUV bandpass.  This set consists of two 120 second PSA exposures (CSIL06337021910 and CSIL06337030547) and one 1800 second BOA exposure (CSIL06337025400). The segment A BOA and PSA spectra were wavelength calibrated, background subtracted, then divided into 16 equal segments.

The table below lists 1) the central wavelength of each segment, 2) the BOA/PSA transmission in percentage, 3) the 1-sigma error of the transmission, 4) the count rate (in counts per second) of the BOA exposure, and 5) the count rate of the merged PSA exposure.

All measured FUV BOA transmissions agree with previous measurements and exceed the requirements.

Table 5.5-6: 2006 FUV BOA transmission and resolution test results.

| (Å) (1) | Trans (%) (2) | Error (%) (3) | BOA cts/sec (4) | PSA cts/sec (5) |
| --- | --- | --- | --- | --- |
| 2047.2 | 0.58 | 0.02 | 0.6 | 104.8 |
| 1965.2 | 0.57 | 0.01 | 1.22 | 214.6 |
| 1883.3 | 0.59 | 0.02 | 0.67 | 112.8 |
| 1801.4 | 0.61 | 0.02 | 0.5 | 81.4 |
| 1719.5 | 0.61 | 0.02 | 0.43 | 69.9 |
| 1637.6 | 0.6 | 0.02 | 0.93 | 154.8 |
| 1555.6 | 0.62 | 0.01 | 2.24 | 359.3 |
| 1473.7 | 0.63 | 0.02 | 0.55 | 86.9 |
| 1391.8 | 0.65 | 0.03 | 0.3 | 46.7 |
| 1309.9 | 0.78 | 0.04 | 0.27 | 34.2 |
| 1228 | 0.78 | 0.08 | 0.1 | 13.1 |

A comparison with previous results is given in Figure 5.5-3 below. The Appendix C data are plotted with magenta triangles (FUV) and magenta diamonds (NUV). The NUV and FUV measured transmission agree in the overlap region of 1900-2000Å.

#### NUV

Four sets of G230L exposures allow us to quantify the BOA transmission across the NUV bandpass.  Each set consists of two 120 second PSA exposures and one 1800 second BOA exposure.

Details of the observations are listed in the table below. Columns in this table are (1) PSA filenames, (2) BOA filenames, (3) Central wavelength setting, (4) NUV stripe measured, (5) Wavelength at the center of the stripe, (6) measured transmission (in percentage) of the BOA relative to the PSA, (7) 1-sigma error of the measured transmission, (8) BOA count rate (in counts per second), and (9) PSA count rate (in counts per second).

All measured NUV BOA transmissions agree with previous measurements and exceed the requirements.

Table 5.5-7: 2006 NUV BOA transmission and resolution results.

| PSA filenames (CSILxxxx) (1) | BOA filename (CSILxxxx) (2) | C (Å) (3) | S (4) | (Å) (5) | Trans (%) (6) | Error (%) (7) | BOA cts/sec (8) | PSA cts/sec (9) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 06337040102 06337044532 | 06337061855 | 2635 | B | 1877 | 0.56 | 0.02 | 0.846 | 150.0 |
| 06337040102 06337044532 | 06337043507 | 3000 | A | 2241 | 0.51 | 0.02 | 2.665 | 525.4 |
| 06337045256 06337053726 | 06337043507 | 3000 | B | 2595 | 0.42 | 0.01 | 3.756 | 887.8 |
| 06337054450 06337062920 | 06337052701 | 3360 | A | 2966 | 0.36 | 0.01 | 2.196 | 611.7 |

Figure 5.5-3:  Comparison of 2003 and 2006 BOA transmission measurements.

## signal to noise

### CEI Requirements

Section 4.2.5 and Table 4-4 of the CEI list the requirements for the COS instrument signal to noise performance.  For the purposes of this discussion signal to noise is defined as the “reciprocal of the root-mean-square (RMS) scatter of data points about a smooth function fit to those points.”  In summary, the COS instrument shall support at least 30:1 signal to noise during routine operations and 100:1 under optimal conditions.

### FUV Channel

Five test procedures were used to characterize the flat-field response of the FUV detector. These tests (#850, #1700, #1720, #1730, and #3000) provided 95 internal flat-field calibration lamp exposures per FUV detector segment that were suitable for characterizing the intrinsic efficiency variations of the digital elements (DE).  All tests for FUV segment ‘A’ used the‘G130M grating, while all segment ‘B’ tests used the G160M grating. Tests #1700, #1720, #1730, and #3000 were specifically performed for purposes of obtaining the flat-field, while test #850 “FUV Repeatability Monitor” provided additional exposures as part of stability testing. The illumination of the FUV segments was adjusted throughout the tests to paint the lifetime cross-dispersion science regions of the detectors. In geometrically corrected images, we considered cross-dispersion (XD) ‘Y’ digital element values 377 to 578, and the dispersion direction (DD) ‘Y’ digital element values 1130 through 15241 to be the science region of segment ‘A’ of the FUV detector.  For segment ‘B’, the XD range was taken to be digital values 436 to 636, and the DD range was taken to be 1324 to 15546. We restrict our analysis to these regions. Furthermore, we define a resolution element (RE) to be 6(DD)x10(XD) digital elements (DE), resulting in ~2350 RE per segment.

The combined segment ‘A’ flat-field image (super-flat) contained 1.84E8 counts, with a median counts/DE over the science region of 276, and a median photon statistic S/N of 17 per DE, or 129 per RE. The combined segment ‘B’ flat-field image contained 1.79E8 counts, with a median counts/DE over the science region of 296, and a median photon statistic S/N of 18 per DE, or 134 per RE.

2003 FUV Flat Field Analysis

The dispersion and cross-dispersion profiles of the FUV ‘super-flats’ are shown in Figures 4.6-1 (A) and 4.6-2 (B). The strong dips in the upper panels of these figures are shadows from the grid-wires, which are periodic in the DD. Also shown in the bottom (XD) panels are the nominal spectral locations, and the XD extent of the PSA at the FUV detector. To determine the DE-to-DE variations (the P-flat) from the structure associated with the grid-wires and the illumination from the calibration lamps (the L-flat), polynomials were constructed along columns of the super-flats. For each column in the science region, least-squares polynomials of order 1 (linear) to 5 were constructed. These polynomials form the FUV L-flats of varying accuracy.  The 3rd order produced the lowest reduced 2, and we adopt this as our L-flat. Dividing the FUV super-flat by the L-flat defines the P-flat.

To quantify the variations inherent to the P-flat, we construct histograms of the P-flat values for each segment. The histograms, along with the measured Gaussian widths (), are shown in Figure 5.6-4.  The FUV P-flat Gaussian widths indicate the maximum achievable S/N without flat-field correction. The FUV P-flat distribution indicates that, at the DE level, the standard deviations are 15-20%, with a higher standard deviation for segment ‘A’.  At the RE level, the P-flat distributions show standard deviations of ~5-6%, implying that the maximum S/N per RE achievable without flat-fielding is ~20.

To predict the actual S/N achievable when applying the FUV P-flats, we examined data taken during the 17 science and wavelength calibration exposure pairs of test 2120, “FUV high quality spectra”.  Each exposure pair consisted of a CO absorption line spectrum (Kr lamp used as the light source) and an internal wavelength calibration exposure.  The exposures were taken at a series of OSM offsets to enable the data to be dithered (FP_SPLIT). To determine the dispersion offsets, the wavelength spectra were cross-correlated at the 1/10 of a DE level.  Due to characteristics of the CDS, the segment ‘A’ spectra contained significantly fewer counts than the segment ‘B’ spectra. Figure 4.6-3 shows the S/N achieved for a line-free region of the segment ‘B’ spectra for five reduction algorithms;

Raw (thermal correction (TC) only),

Geometric correction (GC) +TC (GC+TC)

FP_SPLIT (FP)+TC+GC (FP+GC),

FP_SPLIT+TC+flatfielding (FF) using TC only (FP+FF-GC+TC), and

fully corrected (FP+FF+GC+TC).

The results are compared to the maximum S/N achievable due to photon statistics (Photon noise = √counts). Extractions not using a flatfield (FF) reach a S/N per RE limit of ~20. The dithering extraction (FP_SPLIT) partially corrects the DE-to-DE variations, and can achieve S/N per RE of ~40.  Applying both dithering and the derived P-flats corrects the digital element-to-digital element variations close to the limits of our photon statistics.

Finally, Figure 4.6-5 shows the full G130M Kr lamp spectrum with the CO absorption cell in place for segments A and B.

Figure 5.6-1: Histograms in X and Y for FUV02 segment A showing the number and distribution of counts used to generate the flat field image.

Figure 5.6-2: Histograms in X and Y for FUV02 segment A showing the number and distribution of counts used to generate the flat field image.

Figure 5.6-3: Measured signal to noise versus counts per resolution element under different correction assumptions.

Figure 5.6-4: Distribution of residuals in the final FUV flat fields.

Figure 5.6-5: G130M Kr lamp spectra with a CO absorption cell in place used to evaluate the signal-to-noise performance of COS.

#### 2006 FUV Flat Field Analysis

The 2006 CDS was capable of delivering more light from the D2 flat field lamp in the FUV than the 2003 CDS could provide.  As a result, in 2006 we obtained external flat field data for the FUV.

Tests:  1301 – FUV CDS lamp brightness

1300 – FUV external flat field S/N=30

1399 – FUV faint source

Test #1301 was a setup test to verify settings for the external deuterium (D2) lamp. Test #1300 acquired D2 observations through the wide open aperture in RASCAL.  Test #1399 was similar to #1300 except that the D2 observations were acquired through the 10m RASCAL aperture to simulate a point source spectrum.  The data analysis below concentrates on this final set of observations, as they more closely mimic the type of external flat field source we will be able to acquire on orbit.

Test #1399 was performed on 12/06/06 as part of the COS Appendix C testing to determine whether an external source (a Deuterium lamp, D2) could be used to obtain a flat-field (FF) spectrum for the FUV channel. Previous attempts in Appendix B testing at flat-fielding with a traditional 2-D flat using an internal source did not improve the data quality. During this test, 180 second G160M exposures were taken at each of the twenty central wavelength and FP-OFFSET (FP) position listed in the table below.

Table 5.6-1: Exposure list for 2006 FUV flat field tests.

| Dataset | Wavelength Setting (Å) | FP-OFFSET |
| --- | --- | --- |
| CSIL06340100500 | 1577 | -1 |
| CSIL06340101249 | 1577 | 0 |
| CSIL06340102038 | 1577 | 1 |
| CSIL06340102936 | 1589 | -2 |
| CSIL06340103725 | 1589 | -1 |
| CSIL06340104514 | 1589 | 0 |
| CSIL06340105303 | 1589 | 1 |
| CSIL06340110201 | 1600 | -2 |
| CSIL06340110950 | 1600 | -1 |
| CSIL06340111739 | 1600 | 0 |
| CSIL06340112528 | 1600 | 1 |
| CSIL06340113426 | 1611 | -2 |
| CSIL06340114215 | 1611 | -1 |
| CSIL06340115004 | 1611 | 0 |
| CSIL06340115753 | 1611 | 1 |
| CSIL06340120653 | 1623 | -2 |
| CSIL06340121442 | 1623 | -1 |
| CSIL06340122231 | 1623 | 0 |
| CSIL06340123020 | 1623 | 1 |

After thermal and geometric correction, the spectra where divided into ‘odd’ and ‘even’ samples. These spectra shown in Figure 5.6-6 below.  The external D2 lamp produces a continuum only at the longest wavelengths (above ~1600Å, the lower pixel portion of segment ‘A’).  We focused our flat-fielding efforts on the region of the detector where the spectra are colored blue and red. The ten red regions were added to produce the even flat-field and the ten blue regions were combined to produce the odd flat-field. Because the continuum is very flat in this region, normalization of the flat-field was achieved by a simple linear fit.

Figure 5.6-6: External D2 spectra from 2006 thermal vacuum testing used for FUV flat field analysis.  The spectra have been divided into two samples, “odd” and “even.”

The same spectra where then aligned in wavelength space, and the same regions were added to create odd and even test spectra. The wavelength alignment was performed by a cross-correlation of the portion of the D2 spectrum with strong lines (the upper pixel portion of the spectra). The wavelength aligned spectra are shown in Figure 5.6-7 below (with an arbitrary wavelength scale); again, the test portions of the spectra are shown in blue and red.

Figure 5.6-7: FUV external D2 spectra for flat-field analysis.  The spectra have been aligned in wavelength space.

The odd flat-field was used to correct the merged even test spectra, and vice-versa. In this way, no data was ever flat-fielded by itself, or by data taken at the same wavelength region. Because the spectrum and the flat-field shared the same illumination on the detector (cross-dispersion profile), the flat-fielding was performed in one dimension (the spectral dimension). In other words, each merged data column was used to create the flat-field value for that detector column. The 1D flat-field is shown in Figure 5.6-8 below. Various features such as hex, grid wires, and hot spots are clearly visible.

Figure 5.6-8: One dimensional flat-fields created from the odd and even data sets.

In Figure 5.6-9 below, the results of this flat-fielding can be observed. The upper left panel (labeled “noFP, no FF”) shows the normalized, odd sample added in detector space (it is the odd flat-field). The distribution at the right shows the column to column variations, and is an indication of the maximum S/N without FP-dithering or flat-fielding (FF). The second row shows the normalized spectra added in wavelength space, and reveals S/N improvement from the FP-dithered positions. The third row shows the normalized spectrum after FP-dithering and the inclusion of the even FF.  Finally, the bottom row shows the normalized FP+FF spectrum on a per resolution element basis. The results shown in this figure only use the highest S/N portion of the merged spectra.

Figure 5.6-9: Results of flat fielding for different combinations of flats plus application of focal plane splits.

To illustrate the effectiveness of the 1D flat-fielding, the above process was repeated after the addition of each of the ten (odd or even) test spectra, and is plotted in Figure 5.6-10 below against the photon limited result and the photon limited result factoring in the quality of our FFs (photon statistics of about +/- 3%).  Starting at the top of the figure, the solid line with triangles shows the photon-limited result with a perfect FF. The solid black line without triangles shows the maximum achievable S/N with the FF obtained in this test and ten FP positions. The results to the left of the vertical dashed line are per column values, while results to the right are per RE. The solid blue and red lines are the odd and even test spectra FFd and FP-dithered as previously described. Deviations of the odd and even test spectra from the theoretical maximum are due mixed S/N regions of the merged spectra as more and more spectra and wavelength ranges are added to the test spectra. Just below the test spectra results, the green solid line shows the theoretical maximum if no FP dithering was used, but our FF was still applied. Finally, at the bottom the S/N achieved in our odd and even test spectra are shown with FP dithering, but no flat-fielding. Unlike the previous figure, the entire merged spectrum was used in the figure, and the final S/N values are lower than the those obtained previously when only using the highest S/N portions.  These results indicate that high signal to noise observations will be possible in the FUV with COS on orbit once acquisition of an external “flat” source (such as a nearby white dwarf) is acquired and used to construct a one dimensional spectral flat field correction.

Figure 5.6-10: Measured signal to noise versus counts per resolution element under different correction assumptions for the 2006 FUV flat field data set.

### NUV Channel

Three procedures were used to characterize the flat-field response of the NUV detector. The first test (#1750) used the internal calibration lamp Flat #1, while the other two tests (#2505 and #2506) used an external calibration lamp D2.  Test #2506 was added to extend the cross-dispersion coverage of test 2505 and is included in this analysis. In this analysis cross-dispersion (XD) ‘X’ pixel values 500 through 900, and the dispersion direction (DD) ‘Y’ pixel values 2 through 1021 were considered to be the science region of the detector. This analysis is restricted to this region. Furthermore, a resolution element (RE) is defined to be 3x3 pixels (p), resulting in 340 RE per spectral stripe. Our fiducial location spectral stripes are: A, X =  861; B, X= 759; and C, X=619. All flat-field exposures were taken with the G185M grating.

Test #1750, “NUV Calibration Sub-System Flat Fields, S/N=30”, consisted of 27 exposures with a total exposure time of 64.8 ksec. The combined NUV internal exposure contained 7.54E7 counts. The median counts/p over the science region was 210. The median signal to noise ratio (S/N) was 15 per p, or 44 per RE.

Test # 2505, “ NUV Calibration Delivery System, S/N = 100’, and its cross-dispersion extension, Test #2506, consisted of 44 exposures with a total exposure time 24.5 ksec. The combined external exposure contained 3.59E9 counts. The median counts/p over the science region was 8707. The median S/N was 94 per p, or 280 per RE.

To create the highest quality NUV flat-field, all data from tests 1750, 2505 and 2506 were combined to create a NUV calibration `super-flat’, with most of the counts coming from the external tests. The combined Flat-field image contained 3.62E9 counts. The median counts/p over the science region was 8920. The median S/N was 95 per p, or 284 per RE

### 2003 Results

The dispersion and cross-dispersion profiles of the NUV super-flat are shown in Figure 5.6-11. Also shown in Figure 5.6-11 are the spectral stripe locations.  By extracting from the super-flat 1D spectra at the spectral stripe locations, the S/N as a function of spectral location (wavelength) can be derived. Figure 5.6-13 shows the S/N achieved per RE from the NUV super-flat for the three science stripes.  To convert to S/N per pixel, simply divide the displayed S/N by 3 (√9).

The small scale deviations from a smooth extracted spectrum are the result of pixel-to-pixel variations of the NUV detector response. To extract the pixel-to-pixel variations (the P-flat) from the structure in Figure 5.6-11 associated with the illumination from the calibrations lamps (the L-flat),  polynomials were constructed along columns of the super-flat. For each column in the science region, least-squares polynomials of order 1 (linear) to 6 were constructed. These polynomials form the NUV L-flats of varying accuracy.  The parabolic (order =2) produced the lowest reduced 2, and we adopted this as our final L-flat. Dividing the NUV super-flat by the L-flat defines the P-flat.

To quantify the variations inherent to the P-flat, we extracted flat-field spectra (per RE) at the stripe locations. The histograms of the spectra, along with the measured Gaussian widths (), are shown in Figure 5.6-12.  The Gaussian widths define the maximum achievable S/N without flat-field correction of the NUV data. The S/N values are indicated for each stripe in Figure 5.6-12. Without flat-fields, NUV spectra are limited to S/N of ~50.

To predict the S/N achievable when applying the NUV flatfields, we examined data taken during the 54 exposures of test 2170, “NUV high quality spectra”. Each of these exposures used the D2 lamp, taken with an internal wavelength calibration exposure.  The exposures were taken at a series of OSM offsets to enable the data to be dithered (FP_SPLIT). To determine the dispersion offsets, the internal wavelength spectra were cross-correlated. Figure 5.6-14 shows the S/N achieved for the ‘C’ stripe for three reduction algorithms; Raw (no corrections), FP_SPLIT, and FP_SPLIT plus flat-fielding (FF). The results are compared to the maximum S/N achievable due to photon statistics (√counts). Due to the Gaussian nature of the P-flat,  the raw extraction reaches a S/N limit of 50. The dithering extraction (FP_SPLIT), however, partially corrects the pixel-to-pixel variations, and can achieve high S/N with no limit detected by the calibration tests. Applying both dithering and the derived P-flats fully corrects the pixel-to-pixel variations to the limit of our photon statistics.

Finally, Figure 5.6-15 shows the complete D2 spectrum used for this analysis.

Figure 5.6-11: Counts per pixel used to derive the NUV flat fields and achievable signal to noise.

Figure 5.6-12: Histograms of the residual errors for each spectra.  The width is an indication of the maximum achievable signal to noise without flat fielding.

Figure 5.6-13: Signal to noise per resolution element for the data.

Figure 5.6-14: Signal to noise per resolution element as a function of counts and processing step.

Figure 5.6-15: G185M spectrum of a D2 lamp with an O2 absorption cell used to evaluate the signal-to-noise performance of the COS instrument.

2006 Results

The NUV flat-field analysis was not repeated in the 2006 thermal vacuum tests.

## Field of View

### CEI Requirements

Section 4.2.6 of the CEI and Table 4-5 list the specifications for the field of view of the COS instrument.  In general terms the CEI states that the COS instrument shall have two apertures, a Prime Science Aperture (PSA) and a Bright Object Aperture (BOA).  The BOA shall have at least a factor of 100 attenuation compared to the PSA.  Each aperture shall have a 2.5" diameter working field of view.  These requirements are met by design and implementation.

### Description

The 2.5" requirement is satisfied by the physical size of the PSA and BOA and was measured as part of component inspection at delivery.  However, during Appendix B the PSA aperture was fully illuminated to measure the offsets from the internal wavelength calibration lamp image center to the center of the science aperture and additionally demonstrate the total field of view and look for potential sources of stray or scattered light.  The aberrated nature of the HST PSF allows light from field angles outside the 2.5" diameter of the apertures to enter the instrument.  Specifically, ray-trace models predict that objects within a 4" diameter centered on an aperture will be visible in the science data.

To verify the optical performance of the COS apertures the region around the PSA was over-illuminated and an image acquired with the TA-1 mode in Appendix B. These measurements were not repeated in Appendix C.

Tests:	1437 – Image of LINE1 lamp vs. Flooded Aperture

1410 – TA1 Field of View Mapping

Relevant Exposures:

Table 5.7-1: Exposure list for 2003 field of view tests.

| File | Channel/C | Comments |
| --- | --- | --- |
| CSIL03289175054 | TA-1 | Fully illuminated PSA image |
| CSIL03289191553 | TA-1 | Fully illuminated BOA image |
| CSIL03269170802 | TA-1 | Test 1410: |
| CSIL03269171202 | TA-1 | PSA scanned across the RAS/Cal image |
| CSIL03269171602 | TA-1 | All exposures with D2 lamp for 100 sec. |
| CSIL03269172002 | TA-1 |  |
| CSIL03269172402 | TA-1 |  |
| CSIL03269172802 | TA-1 |  |
| CSIL03269173201 | TA-1 |  |
| CSIL03269173600 | TA-1 |  |
| CSIL03269174001 | TA-1 |  |
| CSIL03269174401 | TA-1 |  |
| CSIL03269174809 | TA-1 |  |
| CSIL03269175332 | TA-1 |  |
| CSIL03269175731 | TA-1 |  |
| CSIL03269180131 | TA-1 |  |
| CSIL03269180532 | TA-1 |  |
| CSIL03269180931 | TA-1 |  |
| CSIL03269181331 | TA-1 |  |
| CSIL03269181731 | TA-1 |  |
| CSIL03269182131 | TA-1 |  |
| CSIL03269182531 | TA-1 |  |
| CSIL03269182930 | TA-1 |  |
| CSIL03269183340 | TA-1 |  |

### 2003 Results

As stated above, ray-trace models predict that objects within a 4" diameter, corresponding to 167 pixels in the TA-1 mode, will be visible in the science data.  Examining the images for the files presented above we see that in each case the size of the image is ~167 pixels, exactly as we would have predicted (see Figure 4.7-1).  It is worth noting that the asymmetry in the illumination pattern of the image is likely due to irregularities in the light produced within the lamp and not due to vignetting within the COS instrument.  This is because non-uniformity in the image cannot generally be induced by vignetting some portion of a converging, diverging, or collimated beam.  This sort of non-uniformity is generally produced either by the object or vignetting at an image plane.  Since COS does not form an image plane within the instrument the non-uniformity can only come from the source or vignetting right at the aperture.

In addition, during Test 1410 the COS PSA was scanned across the  point source formed by RASCAL and the count rate monitored.  The count rates were symmetric about the center of the aperture, so vignetting at or near the aperture is unlikely, leaving source non-uniformity as the most probable of the observed structure.  A comparison of the measured PSA transmission and the predicted transmission from a ray-trace model is shown in Figure 4.7-2.

Figure 5.7-1: TA-1 image of a fully illuminated PSA aperture.  The circle in the upper right image is 167 pixels in diameter and highlights how the observed image is as large as expected from ray-trace models.

Figure 5.7-2: Comparison of the measured PSA transmission as a function of off-axis angle and the predicted transmission from ray-trace models.

## Stray and Scattered Light

### Requirements

The Contract End Item (CEI) Specification (STE-063) states that diffuse and scattered light shall contribute no more than 2% residual intensity to the signal in the core of a saturated absorption line measured with any of the medium dispersion modes in the spectrum of a point source in the PSA. The residual intensity shall be measured in the net spectra after extraction from the two dimensional gross data and measurement and removal of background light using COS data processing algorithms.

The COS Calibration Requirements and Procedures (AV-03) states that the primary measurement is to obtain a continuum exposure with saturated absorption lines at a signal to noise level of 30:1 per resolution element. Compare the continuum level to the level at the core of the saturated line.  A secondary test is to examine a high S/N external Pt-Ne spectrum to search for light between the emission lines.  (Note, this secondary test was not run due to potential for significant permanent charge extraction from the FUV detector.)

### FUV

The following tests were executed in Appendix B (2003).  The CDS did not contain an absorption cell in 2006, so the tests were not repeated in Appendix C (2006).

Tests: 	2100 – Initial Absorption Cell Spectra

2110 – FUV Scattered Light

Relevant Exposures:

Table 5.8-1: Exposure list for 2003 FUV stray and scattered light tests.

| File | Channel/C | Comments |
| --- | --- | --- |
| CSIL03289040431 | G130M/1309 Å | A few saturated bands in Å |
| CSIL03289042300 | G160M/1600 Å | Saturated bands in B |
| CSIL03289050500 | G140L/1230 Å | Saturated or nearly so in A |
| CSIL03289051900 | G160M/1600 Å | Saturated in B |
| CSIL03289053131 | G130M/1309 Å | A saturated, B saturated or very close |
| CSIL03289055131 | G130M/1309 Å | A saturated, B close |
| CSIL03289061831 | G160M/1600 Å | B saturated |
| CSIL03289065031 | G140L/1230 Å | A saturated or close to saturated |

All of the spectra have nearby unabsorbed or weakly absorbed regions from which to measure the unattenuated flux.

#### Analysis

This analysis focuses on two exposures, one from each medium-resolution grating, which show a nice series of saturated absorption bands:  CSIL03289051900 (G160M, segment B only), and CSIL03289053131 (G130M, both segments).  For each spectrum and appropriate segment, a one-dimensional spectrum was created by performing a sum in the cross-dispersion direction covering the full width at zero intensity (FWZI) of the external spectrum.  A background light spectrum was also created by extracting another one-dimensional spectrum of the same width away from the target spectrum.  The FUV spectra are shown in Figure 4.8-1.

#### Results

CSIL03289053131, Seg A:  The peak intensity in the unattenuated spectral regions decreases smoothly from 131 counts (near pixel 2000) to 61 counts (near pixel 14250).  The first three absorption cores are the widest.  They run from pixels 3191 -- 3794, 5929 -- 6386, and 8464 -- 8904.  The mean count in these regions is 0.02, with an rms of 0.25 and a maximum count value of 2.  Taking the conservative unabsorbed count rate of 61 counts gives a 2% residual level of 1.2 counts, which is easily met in the observed spectrum.

CSIL03289053131, Seg B:  The peak unattenuated count rate is roughly 70 counts in the two unattenuated spectral regions around pixels 2700 and 4500.  The first two absorption bands only just approach saturation, while the third does not become saturated. In the narrow regions, 2024 - 2087 and 3903 - 3935, the mean counts are 0.23, with a 0.6 pixel rms and a maximum pixel value of 2.  The 2% residual level is 1.4 counts, so measured scattered light meets specifications.

CSIL03289051900:  The unattenuated counts in the three brightest humps in the spectrum average roughly 190 counts.  For the stray and scattered light, the average and deviation were calculated for the four saturated bands near these unattenuated spectral regions:  pixels 6763 - 7356, 9459 - 10015, 11866 - 12483, and 14224 - 14753.  The average counts over all four regions is 0.04 counts.  The rms is 0.3 counts the maximum single count in a pixel is 3.  The 2% residual intensity level is 3.8 counts, so again the scattered light is well within specifications.

Figure 5.8-1: FUV absorption spectra acquired during Tests 2100 and 2110.  Panels (a) and (b) were acquired with G130M and panel (c) with G160M.  The solid bars show the regions used to measure the stray and scattered light.

### NUV

The following tests were executed during Appendix B.  There was no absorption cell available in 2006, so the tests were not repeated in Appendix C.

Tests: 	2150 – NUV O2 Initial Spectra

2160 – NUV Scattered Light

Relevant Exposures:

Table 5.8-2: Exposure list for 2003 NUV stray and scattered light tests.

| File | Channel/Stripe/C | Comments |
| --- | --- | --- |
| CSIL03270041709 | G185M / B/ 1817Å | Absorption cell pressure = 700 Torr |
| CSIL03270080108 * | G185M / A / 1784Å | Absorption cell pressure = 700 Torr |
| CSIL03270084139 | G185M / B / 1817Å | Absorption cell pressure = 700 Torr |
| CSIL03270033410 ** | G185M / B /1817Å | Continuum reference spectrum |

* The central wavelength of Stripe B in this exposure (the nominal wavelength for a given setting) is 1882Å, but Stripe A runs from 1766 – 1801Å.

** This is a reference spectrum for the 1817Å exposures taken at 200 mTorr that gives the count rate in the unabsorbed continuum.  The exposure time on this exposure is 600 sec, so its counts need to be multiplied by 3 to give the expected continuum level for the saturated exposures.

There is no reference spectrum for the 1784 Å spectrum.

#### Analysis

For all spectra, a row sum was used to find the centroid of each stripe. A 20 pixel window centered on the middle of each stripe was extracted to obtain 1-D spectra. A 20 pixel wide background spectrum in between stripes B and A in each exposure (centered well away from each stripe) was also measured. The background spectrum was subtracted from the stripe spectrum at the pixel level before analysis.

Regions in the spectra where the absorption line cores appear to be fully saturated were selected for analysis.  Most of the saturated regions are narrow, 10 -- 20 pixels wide.  However, the A stripe of CSIL03270080108 is completely saturated for pixels >755.

Saturated regions:

CSIL03270041709:  pixels 524 -- 547;  840 -- 849;  868 -- 894

CSIL03270084139:  pixels 472 -- 481;  501 -- 509;  526 -- 554; 779 -- 790; 816 -- 825;  841 -- 852;  863 -- 897

CSIL03270080108:  pixels 155 -- 186;  634 -- 661;  783 – 1024

#### Results

The reference spectrum for the two 1817Å observations shows that the B-stripe unabsorbed intensity (counts multiplied by 3 to give the counts in 1800 sec) is 315 counts for pixels <775 and 293 counts for 775 ≤  p ≤ 900.  Therefore, 2% residual counts corresponds to 6.3 counts in the first region and 5.9 counts in the second.

It is less clear what the unabsorbed count rate is for the 1784Å spectrum.  The A stripe nominally covers 1766 – 1801Å, so we can estimate the long wavelength end of the A stripe based on the short wavelength counts in the 1817Å reference spectrum, which nominally goes just out to 1800Å and has a count total (scaled up by 3) of 215 counts.  A stricter limit can be set by the maximum observed counts in the A stripe,  which is 158 counts at pixel 9.  This is over-conservative, though, since the entire A stripe appears to be absorbed, with no true continuum present.

The counts in the saturated regions are:

CSIL03270041709:  The 524 -- 547 region has a mean count value of 2 and an rms of 2.3, below the 6.3 count limit.  The maximum counts in a single pixel in this region is 10, but this appears to be due to an unabsorbed region rather than stray or scattered light. The mean residual intensity is 0.6%. The other two regions, which look much flatter, have mean counts of 0.76, an rms of 1.5, and a maximum count of 5. All of these are below the 2% residual intensity limit of 5.9 counts.  The mean residual intensity in these regions is 0.3%.

CSIL03270084139:  This is the same setup as the previous exposure, but at higher pressure in the absorption cell.  The first three regions (pixels in the 400s and 500s;  see above) have a mean count of 1.5, an rms of 1.8, and a max of 5.  The mean residual intensity is 0.5%.  The final four regions (700s and 800s) have a mean of 0.7, an rms of 1.4, and a max of 5.  The mean residual intensity is 0.2%.

CSIL03270080108:  The mean counts in the absorbed regions is 0.07.  The rms is 0.99 and the max count is 5 (although again, this could be caused be unabsorbed flux rather than scattered light; see near pixel 850).  This is well within the 2% residual intensity limit, so long as the unabsorbed counts are >3.5!

Figure 4.8-2 shows the 1-D spectra used for the stray and scattered light analysis for the three cases examined.  For the two 1817Å exposures, the reference spectrum (multiplied by 3) is also shown.  The red dashed lines indicate the continuum level used in the analysis.  The blue bars underneath the spectra show the saturated regions used.

Figure 5.8-2: Data used to calculate the scattered light from the G185M grating.  Panels (a) and (b) show stripe B, C=1817Å.  The red line denotes the continuum used to calculate the scattered light in the saturated absorption lines, which are noted by the blue lines below the spectra.  Panel (c) shows the G185M spectrum in stripe C, which has a central wavelength of 1784Å.  The red lines in (c) show the continuum assumed for the scattered light calculation.

## Image stability & Drift CompensAtion

### CEI Requirements

Section 4.2.8 of the CEI states that knowledge of the drift shall be provided which allows it to be corrected with a residual uncertainty of not more than 0.25 resolution elements per hour.

### Description

During Appendix B (2003) testing a series of tests were conducted where spectra from RASCAL and the internal wavelength calibration lamps (hereafter referred to as “wavecals”) were acquired simultaneously.  Specifically, data were acquired for G130M, G160M, G140L, and G285M with exposure times of 6500 seconds.  In the case of the G285M channel, two 6500 second exposures were acquired, effectively characterizing the drift over a 13,000 second observation.  It is also worth noting that 6500 seconds is the maximum observation time for any COS observation, so these observations cover all possible COS exposure times.

The simultaneous wavecal and PSA spectra provide the ability to test different methods for tracking and correcting time dependent drift due to the OSM1 and/or the OSM2 mechanisms.  Drift was measured in one of two ways using only the wavecal spectra, either by computing the average center of individual emission lines or by cross-correlating a wavecal spectrum  acquired at time t against the wavecal spectrum acquired at t=0.  Figure 4.9-1 graphically depicts what was done for the G285M data.  The drift was measured for wavecal exposure times (twav) ranging from 30 to 180 seconds and times between exposures (tdwell) between 300 and 1200 seconds.  In fact, subsequent work demonstrated at an aperiodic sampling could provide more efficient tracking of the drift and was used to generate the FUV resolution curves presented in this document.  Aperiodic sampling is also described in more detail in OP-01 (COS-01-0001) and AV-03 (COS-01-0003).

Once the drift was characterized a time dependent correction term, which removes the drift, was added to both the x and y location of individual photon events in the science spectrum.  The correction term is simply the measured drift multiplied by –1.  The correction terms for those events falling between wavecal exposures were computed by either linearly interpolating between the drift measured at times t1 and t2 or by fitting the data with a 5th order polynomial function and using  the derived function to compute the correction term.

The performance of the drift correction was evaluated using two parameters, the FWHM of the time dependent average line center and the FWHM of the line spread function of a drift-corrected emission line in the PSA spectrum.  The FWHM of the average line center is a measure of correction algorithm’s ability to track and correct drift.  The FWHM of the line spread function tracks the performance of the correction algorithm by measuring the pre-and post-correction resolution, the ultimate purpose of the drift correction.

Figure 4.9-2 summarizes the measurement and correction of the drift.  The panels at the left show raw and corrected average line centers in the dispersion and cross-dispersion directions for a single emission line in the PSA spectrum.  Each figure also shows the FWHM of the corrected line center expressed in resolution elements (for the short wavelength for the exposure), the exposure time for the wavecal (twav), and the time between wavcal exposures (tdwell). The FWHM is computed using the IDL STDDEV function and multiplying the result by 2.354.  The diamonds indicate where wavecal exposures were taken.  The right hand figures show the measured drift, expressed in pixels, as functions of time.  Recall that the drift is measured using the wavecal data only.

Figure 5.9-1: The left panel shows the G285M image used in this analysis with the 3 emission lines that were used to measure the drift.  The right panels show the same data, but with the spectra used in the cross-correlation.  For the cross-correlation analysis all three spectra were collapsed together into a single, combined pseudo-spectrum, one for each dimension.  This provided more lines for the cross-correlation algorithm and would be simpler in a pipeline processing application.

Figure 4.9-3 shows the line profile of an emission line in the PSA spectrum in the dispersion and cross-dispersion directions before and after correcting for mechanism drift shown in Figure 4.9-2.  The FWHM in pixels is computed by first fitting a Gaussian profile to the histogram (shown as a dotted line) and then multiplying the standard deviation by 2.354.  Note the significant improvement in spectral width after correcting for drift.

Figure 5.9-2: Drift correction results for the G285M data using line center tracking.  Right hand panels show the measured drift for each stripe.  Left hand panels show the line center for an emission line in the science spectrum before and after drift correction.

Figure 5.9-3: Line widths for an emission line in the science spectrum before and after correction.  Note the improvement in spectral resolution after correction of the drift.

Tests:	2300 FUV Grating Stability

2355 NUV Grating Stability

Relevant Exposures:

Table 5.9-1: Exposure list for 2003 image stability and drift compensation tests.

| File | Channel/C | Comments |
| --- | --- | --- |
| CSIL03285043406_1_rawtag.fits | G130M / 1309Å | Moderate drift, ~3 pixels |
| CSIL03285081037_1_rawtag.fits | G160M / 1600Å | Low drift, ~1.5 pixels |
| CSIL03285101309_1_rawtag.fits | G140L / 1230Å | Large drift, ~8 pixels |
| CSIL03285123358_1_rawtag.fits | G285M / 2850Å | Large drift, ~8 pixels |
| CSIL03285144027_1_rawtag.fits | G285M / 2850Å | No drift, ~0 pixels |

### Results

The first task was to compare the performance of the emission line tracking versus cross-correlation algorithms for measuring the drift of the spectrum.  This was conducted using the G285M data, because this data exhibited large spectral drift.  The performance of the line tracking versus cross-correlation was evaluated over a range of wavecal exposure times and dwell times.  Table 4.9-1 presents the results.

It should also be pointed out that the 5th order polynomial fit, while evaluated, was ultimately dropped for all the analyses presented here.  The reason is that the polynomial function required an a priori knowledge of the shape of the drift.  A linear interpolation does not require any assumption about the shape of the drift curve and thus can be understood in terms of the data only.  When the drift of the mechanisms has been more fully mapped during in orbit operations it may be advantageous to employ a parametric function to model the drift; however, at the time of this writing there is insufficient data to support the use of such a function.

Table 5.9-2: Drift measured with different techniques and time scales.

|  |  | Method for Tracking Drift |
| --- | --- | --- |
|  |  | Line Centers | Cross-correlation |
| twav (s) | tdwell (s) | FWHM of Centroid (resels) | FWHM of line width (pixels) | FWHM of Centroid (resels) | FWHM of line width (pixels) |
| 10 | 600 | 0.44 | 3.19 | 0.21 | 2.91 |
| 30 | 600 | 0.28 | 2.88 | 0.20 | 2.82 |
| 60 | 600 | 0.20 | 2.78 | 0.21 | 2.80 |
| 120 | 600 | 0.23 | 2.78 | 0.21 | 2.77 |
| 60 | 150 | 0.23 | 2.81 | 0.21 | 2.81 |
| 60 | 300 | 0.24 | 2.86 | 0.20 | 2.80 |
| 60 | 600 | 0.20 | 2.78 | 0.21 | 2.80 |
| 60 | 900 | 0.28 | 2.91 | 0.23 | 2.83 |
| 60 | 1200 | 0.27 | 2.88 | 0.27 | 2.88 |

Several points regarding these data are worthy of note:

- Tracking the line centers requires a wavecal exposure time ≥  60 seconds.  Presumably, this is because this ensures sufficient photons to accurately compute a average position.  This could be alleviated by choosing brighter lines, should they exist.

- The cross-correlation method does not need as many photons to accurately determine the drift.  This is good because it does NOT require detailed understanding of the spectrum for a given wavelength setting.

- The optimum dwell for this analysis appears to be ~600 seconds.  This is because the derivative of the drift is highest in the first 600 seconds.  If the tdwell is larger than 600 seconds then the linear interpolation between measured drift points under estimates the drift correction.  If a parametric model for the drift is eventually developed then decreasing the frequency of wavecal exposures could be a possibility.  Also note that an aperiodic sampling is a more efficient means of accurately tracking the drift while minimizing the total number of wavelength calibration exposures.  See OP-01 (COS-01-0001) and AV-03 (COS-01-0003) for additional details on aperiodic sampling of the drift.

In summary, it was determined that a cross-correlation method for measuring the spectral drift was as accurate as tracking the average line center.  Cross-correlation also has the advantange that no knowledge of the exact instrument configuration is required, i.e. a list of lines for tracking the drift is not required for each grating configuration.  Therefore, all subsequent analyses use cross-correlation to measure the drift and linear interpolation to compute the time dependent drift function.

There remains the question of the validity of these techniques for other gratings, where the drift may be different and could be uncorrectable.  To confirm that the technique was robust it was applied to data sets acquired for the G130M, G160M, and G140L channels and also reapplied to the G285M data set over a consistent grid of wavecal exposure time and dwell times.  These data are expressed graphically in Figures 4.9-4, 4.9-5, 4.9-6, and 4.9-7.  In each case the figure consists of the residual drift, spectral, and spatial widths as functions of tdwell and twav.  For the G130M and G160M data the FUV detector segments were each evaluated separately.  Table 4.9-2 presents the full data set.  Figures 4.9-8, 4.9-9, and 4.9-10 show examples of the drift results for the FUV channels.

The results of the study are encouraging, confirming the validity of the correction algorithm and providing guidance for operating the COS instrument in flight.

Table 5.9-3: Measured drift in spectral and spatial directions.

| G130MA Results: | Segment A | Segment B |
| --- | --- | --- |
| tdwell (s) | twav (s) | Drift (resel) | Spectral (p) | Spatial (p) | Drift (resel) | Spectral (p) | Spatial (p) |
| 180 | 30 | 0.315 | 6.411 | 9.316 | 0.431 | 6.788 | 11.312 |
| 180 | 60 | 0.227 | 6.142 | 9.302 | 0.436 | 6.878 | 11.321 |
| 180 | 90 | 0.201 | 6.093 | 9.294 | 0.238 | 6.372 | 11.324 |
| 180 | 120 | 0.115 | 5.964 | 9.293 | 0.218 | 6.333 | 11.307 |
| 180 | 180 | 0.122 | 5.947 | 9.292 | 0.197 | 6.290 | 11.315 |
| 300 | 30 | 0.395 | 6.567 | 9.307 | 0.367 | 6.679 | 11.315 |
| 300 | 60 | 0.268 | 6.267 | 9.306 | 0.406 | 6.849 | 11.346 |
| 300 | 90 | 0.153 | 6.010 | 9.287 | 0.331 | 6.597 | 11.323 |
| 300 | 120 | 0.117 | 5.927 | 9.288 | 0.200 | 6.295 | 11.312 |
| 300 | 180 | 0.115 | 5.942 | 9.285 | 0.159 | 6.208 | 11.316 |
| 600 | 30 | 0.255 | 6.237 | 9.309 | 0.572 | 7.298 | 11.329 |
| 600 | 60 | 0.181 | 6.076 | 9.300 | 0.280 | 6.504 | 11.336 |
| 600 | 90 | 0.171 | 6.013 | 9.287 | 0.170 | 6.259 | 11.315 |
| 600 | 120 | 0.109 | 5.924 | 9.297 | 0.184 | 6.275 | 11.323 |
| 600 | 180 | 0.104 | 5.930 | 9.281 | 0.173 | 6.253 | 11.319 |
| 900 | 30 | 0.280 | 6.252 | 9.305 | 0.177 | 6.249 | 11.312 |
| 900 | 60 | 0.240 | 6.188 | 9.272 | 0.429 | 6.866 | 11.317 |
| 900 | 90 | 0.134 | 5.976 | 9.290 | 0.175 | 6.256 | 11.304 |
| 900 | 120 | 0.173 | 6.052 | 9.271 | 0.156 | 6.249 | 11.314 |
| 900 | 180 | 0.116 | 5.919 | 9.302 | 0.191 | 6.300 | 11.294 |
| G160MA Results: | Segment A | Segment B |
| tdwell (s) | twav (s) | Drift (resel) | Spectral (p) | Spatial (p) | Drift (resel) | Spectral (p) | Spatial (p) |
| 180 | 30 | 0.146 | 6.421 | 2.989 | 0.098 | 5.571 | 5.152 |
| 180 | 60 | 0.124 | 6.383 | 2.977 | 0.098 | 5.541 | 5.154 |
| 180 | 90 | 0.121 | 6.348 | 2.952 | 0.104 | 5.525 | 5.151 |
| 180 | 120 | 0.125 | 6.351 | 2.949 | 0.102 | 5.526 | 5.152 |
| 180 | 180 | 0.123 | 6.335 | 2.947 | 0.103 | 5.522 | 5.159 |
| 300 | 30 | 0.138 | 6.416 | 2.984 | 0.094 | 5.578 | 5.154 |
| 300 | 60 | 0.122 | 6.361 | 2.973 | 0.096 | 5.535 | 5.154 |
| 300 | 90 | 0.126 | 6.359 | 2.947 | 0.109 | 5.536 | 5.155 |
| 300 | 120 | 0.137 | 6.373 | 2.950 | 0.096 | 5.516 | 5.153 |
| 300 | 180 | 0.125 | 6.333 | 2.933 | 0.104 | 5.531 | 5.159 |
| 600 | 30 | 0.168 | 6.442 | 2.985 | 0.111 | 5.578 | 5.157 |
| 600 | 60 | 0.126 | 6.392 | 2.977 | 0.103 | 5.530 | 5.158 |
| 600 | 90 | 0.130 | 6.346 | 2.953 | 0.095 | 5.525 | 5.154 |
| 600 | 120 | 0.120 | 6.323 | 2.939 | 0.107 | 5.529 | 5.154 |
| 600 | 180 | 0.123 | 6.336 | 2.950 | 0.112 | 5.538 | 5.161 |
| 900 | 30 | 0.141 | 6.391 | 3.015 | 0.108 | 5.567 | 5.161 |
| 900 | 60 | 0.125 | 6.346 | 2.973 | 0.097 | 5.556 | 5.166 |
| 900 | 90 | 0.126 | 6.363 | 2.954 | 0.099 | 5.506 | 5.158 |
| 900 | 120 | 0.128 | 6.333 | 2.967 | 0.105 | 5.524 | 5.157 |
| 900 | 180 | 0.124 | 6.331 | 2.953 | 0.110 | 5.548 | 5.164 |
| G140L Results: | Segment A |  |  |  |
| tdwell (s) | twav (s) | Drift (resel) | Spectral (p) | Spatial (p) |  |  |  |
| 180 | 30 | 0.107 | 6.663 | 3.975 |  |  |  |
| 180 | 60 | 0.109 | 6.700 | 3.959 |  |  |  |
| 180 | 90 | 0.098 | 6.694 | 3.956 |  |  |  |
| 180 | 120 | 0.101 | 6.665 | 3.949 |  |  |  |
| 180 | 180 | 0.103 | 6.690 | 3.957 |  |  |  |
| 300 | 30 | 0.123 | 6.687 | 3.973 |  |  |  |
| 300 | 60 | 0.123 | 6.712 | 3.958 |  |  |  |
| 300 | 90 | 0.100 | 6.680 | 3.956 |  |  |  |
| 300 | 120 | 0.105 | 6.670 | 3.954 |  |  |  |
| 300 | 180 | 0.112 | 6.704 | 3.956 |  |  |  |
| 600 | 30 | 0.166 | 6.811 | 3.974 |  |  |  |
| 600 | 60 | 0.131 | 6.731 | 3.968 |  |  |  |
| 600 | 90 | 0.138 | 6.747 | 3.949 |  |  |  |
| 600 | 120 | 0.127 | 6.710 | 3.954 |  |  |  |
| 600 | 180 | 0.121 | 6.722 | 3.951 |  |  |  |
| 900 | 30 | 0.184 | 6.836 | 3.981 |  |  |  |
| 900 | 60 | 0.162 | 6.808 | 3.957 |  |  |  |
| 900 | 90 | 0.155 | 6.764 | 3.958 |  |  |  |
| 900 | 120 | 0.163 | 6.807 | 3.948 |  |  |  |
| 900 | 180 | 0.151 | 6.791 | 3.948 |  |  |  |
| G285M Results: |  |  |  |  |  |  |
| tdwell (s) | twav (s) | Drift (resel) | Spectral (p) | Spatial (p) |  |  |  |
| 180 | 30 | 0.211 | 2.736 | 2.859 |  |  |  |
| 180 | 60 | 0.214 | 2.802 | 2.801 |  |  |  |
| 180 | 90 | 0.224 | 2.716 | 2.802 |  |  |  |
| 180 | 120 | 0.220 | 2.672 | 2.789 |  |  |  |
| 180 | 180 | 0.245 | 2.691 | 2.871 |  |  |  |
| 300 | 30 | 0.214 | 2.728 | 2.879 |  |  |  |
| 300 | 60 | 0.205 | 2.793 | 2.801 |  |  |  |
| 300 | 90 | 0.212 | 2.658 | 2.795 |  |  |  |
| 300 | 120 | 0.223 | 2.663 | 2.792 |  |  |  |
| 300 | 180 | 0.238 | 2.687 | 2.870 |  |  |  |
| 600 | 30 | 0.208 | 2.774 | 2.826 |  |  |  |
| 600 | 60 | 0.216 | 2.774 | 2.808 |  |  |  |
| 600 | 90 | 0.212 | 2.657 | 2.783 |  |  |  |
| 600 | 120 | 0.218 | 2.661 | 2.771 |  |  |  |
| 600 | 180 | 0.241 | 2.676 | 2.889 |  |  |  |
| 900 | 30 | 0.255 | 2.774 | 2.915 |  |  |  |
| 900 | 60 | 0.246 | 2.774 | 2.832 |  |  |  |
| 900 | 90 | 0.249 | 2.774 | 2.833 |  |  |  |
| 900 | 120 | 0.251 | 2.706 | 2.816 |  |  |  |
| 900 | 180 | 0.255 | 2.686 | 2.917 |  |  |  |

Notes: Drift is the FWHM of the residual drift of the emission line center measured in resolution elements appropriate for the specific channel.  Spectral (p) is the FWHM of the drift-corrected line spread function in the spectral direction measured in pixels.  Spatial (p) is FWHM the drift-corrected spatial dimension measured in pixels.

Figure 5.9-4: Drift-correction performance for the G130M channel for segments A and B as a function of wavecal exposure time and dwell time.

Figure 5.9-5: Drift-correction performance for the G160M channel for segments A and B as a function of wavecal exposure time and dwell time.

Figure 5.9-6:  Drift-correction performance for the G140L channel as a function of wavecal exposure time and dwell time.

Figure 5.9-7: Drift-correction performance for the G285M channel as a function of wavecal exposure time and dwell time.

Figure 5.9-8: Drift correction results for G130M data for segment A.

Figure 5.9-9: Drift correction results for G160M data for segment A.

Figure 5.9-10: Drift correction results for G140L data for segment A.

### Recommendations

Based on the data presented above the following exposure and dwell times are recommended:

Table 5.9-4: Recommendations for exposure and dwell times for drift correction.

| Channel | twav (s) | tdwell (s) (t≤ 1200s) | tdwell (s) (t>1200s) |
| --- | --- | --- | --- |
| G130M | 90 | ≤ 600 | ≤ 3600 |
| G160M | 60 | ≤ 600 | ≤ 3600 |
| G140L | 30 | ≤ 600 | ≤ 3600 |
| G285M | 60 | ≤ 600 | ≤ 3600 |
| Remaining NUV channels | 60 | ≤ 600 | ≤ 3600 |

### 2006 Tag-flash Verification Testing

Tests:	5000 – FUV tag-flash demonstration

5500 – NUV tag-flash demonstration

As a result of the 2003 testing discussed above, it was decided that all COS time-tagged observations would be taken in “tag-flash” observing mode in which the internal wavelength calibration lamp is turned on, or flashed, during science exposures. The lamp will be flashed at the beginning of every exposure and at varying intervals during the exposure, where the timing of the flashes is determined by a number of variables including the length of the exposure and the time since the last major grating wheel move.  Implementation of tag-flash in the COS flight software was completed and uploaded prior to 2006 thermal vacuum tests.  Appendix C included two lengthy tests to verify the correct execution of tag-flash (as well as subsequent correct treatment of tag-flash wavelength calibration data by calcos, the COS data reduction pipeline).  The data were analyzed at Space Telescope Science Institute and the results are published in a STScI instrument report:  COS Technical Instrument Report 2007-03 (COS TIR 2007-03), by C. Keyes.

## NUV Imaging Capability

### CEI Requirements

Section 4.2.9 of the CEI states in part, “The image mode shall be capable of distinguishing two equally bright point sources separated by 1.0 arc second in any direction.”

### Description

Data for this test was acquired as part of a larger test to characterize the imaging performance of the NUV channel, specifically Test 2250 – NUV spatial Resolution.  The test consisted using a row of pinholes as the entrance aperture for RASCAL.  Three of these pinholes were evident in the NUV TA1 image.  The pinholes were separated such that they formed distinct images separated by 1" at the PSA.

Tests:	2250 – NUV Spatial Resolution

Relevant Exposures:

Table 5.10-1: Exposure list for 2003 NUV spatial resolution test.

| File | Channel/C | Comments |
| --- | --- | --- |
| CSIL03265193406 | TA-1 | Texp = 30 sec |
| CSIL03265195137 | TA-1 BRT | Texp = 30 sec |

### 2003 Results

Figure 4.10-1 shows the TA1 image of the 3 pinhole sources.  Note how the image widths in Figure 4.10-2 show the TA1-BRT image of the 3 pinhole sources.  Immediately apparent is the fact that there is a double image.  This was initially discovered during GN2 testing early in the development and is due to the fact that the order sorter has a slight wedge of 30 arc-seconds.  The upper three pinhole images are from the front surface reflection off of the order sorter.  The lower three images are from light reflecting off of the back surface, thus they are dimmer by a factor of 0.48.

Figure 5.10-1: A TA1 image of the 3 pinhole sources with corresponding 2-D Gaussian profile fits to the data.

Figure 5.10-2: TA1-BRT image of the 3 pinhole sources including Gaussian fits which indicate that the two images are separated by 20.5 pixels in the dispersion direction.

### 2006 Results

Test:  2250 – NUV spatial resolution

### Observations of the NUV spatial resolution were repeated in 2006 using the same test (#2250) that was performed in 2003. The same pinhole array was also used, creating distinct images separated by 1" at the PSA. Figure 5.10-3 shows the pinhole image from the Appendix C observation.  The third pinhole wasn’t well illuminated in 2006, so the third pinhole image, though present, is quite faint and is unlabeled in the figure. Because the alignment between RAS/CAL and COS was better in 2006 than in 2003, the image sizes were expected to be smaller in the 2006 data.  This is confirmed by the FWHM of the 2-D Gaussian fits to the images, which are of order 2 pixels in 2006 and 3 in 2003. (Note that FWHM is shown here, while ( was given in Figure 5.10-1, so the ( values from 2003 need to be multiplied by 2.355 for comparison with the 2006 results.)

Figure 5.10-3:  A TA-1 image of the 3 pinhole sources with corresponding FWHM for 2D Gaussian fits to the data.  The third pinhole wasn’t strongly illuminated and is not labeled in the figure.

## FUV/NUV Background Rates

### 2003 FUV Background Results

To quantify the FUV detector intrinsic backgrounds, fourteen exposures were taken with no light incident on the detector. Table 4.11-1 below shows the exposure names, exposure times, and counts on each segment (‘A’ and ‘B’).  All data were thermally and geometrically corrected prior to co-addition. Figures 4.11-1 and 4.11-2 show the combined  highly scaled FUV dark images; circles indicate the location of the stim pulses.  For segment ‘A’, the total number of counts in the dark image was 532539 counts, with a maximum counts/digital element (DE) of 6523.  The average count rate over segment ‘A’ was 9.46 counts/s, or by area, 1.11 counts/s/cm2. For segment ‘B’, the total number of counts was 586027 counts, with a maximum counts/DE of 6416. The average count rate over segment ‘B’ was 10.41 counts/s, or by area, 1.23 counts/s/cm2.

Table 5.11-1: FUV background files and rates.

| Filename | Exposure (sec) | Counts‘A’ | Counts‘B’ |
| --- | --- | --- | --- |
| CSIL03273035446 | 6500 | 103286 | 107146 |
| CSIL03282011458 | 1800 | 13774 | 17551 |
| CSIL03282031158 | 1800 | 37928 | 15322 |
| CSIL03282050358 | 1800 | 12781 | 17672 |
| CSIL03282065558 | 1800 | 14273 | 17601 |
| CSIL03282084758 | 1800 | 14610 | 18939 |
| CSIL03282112320 | 6500 | 49444 | 56631 |
| CSIL03282200820 | 6500 | 102941 | 58664 |
| CSIL03284021918 | 6000 | 4009 | 5757 |
| CSIL03284031316 | 1200 | 7732 | 11968 |
| CSIL03284053521 | 6500 | 41551 | 61138 |
| CSIL03285021022 | 6500 | 41686 | 56768 |
| CSIL03286141723 | 6500 | 39127 | 75101 |
| CSIL03289225425 | 6500 | 49396 | 65768 |
| Total | 56301 | 532539 | 586027 |

Figure 5.11-1: Background image for segment A of the FUV detector.  The total segment background rate is 9.4 cps.

Figure 5.11-2: Background image for segment B of the FUV detector.  The total segment background rate is 10.4 cps

#### 2006 FUV Background Results

The CEI specification for the FUV channel is a background rate of < 0.5 counts/sec/cm2 over the science region of the detector. Each segment of the COS FUV channel has an area of 8.5 cm2.  The initial 2006 FUV dark exposure (CSIL06335132318) showed count rates uniformly elevated with respect to the 2003 FUV dark.  It was believed that the FUV ion pump gauge, which had not been on in 2003 but was in 2006 during this exposure, was the source of the higher background.  Accordingly, a second 6500 second exposure (CSIL06340002822) with no light incident on the detector and with the ion pump gauge turned off was obtained to verify the dark count rate of the FUV channel.  (The ion pump gauge will not be active on orbit once the FUV door has been opened on COS.) After thermal and geometric correction, this exposure showed 23046 counts on the ‘A’ segment, and 59736 on the ‘B’ segment over the entire detector. In terms of area, over the entire detector, the ‘A’ segment had a count rate of 0.417 c/s/cm2, while for the ‘B’ segment the count rate was 1.075 cts/s/cm2. Of note on segment B were 35615 counts along the bottom edge of the detector (a count rate of 5.5 cts/sec) and a hot spot with 308 counts (0.05 counts/sec).

When examined over the spectral region (an extraction stripe 26 ‘Y’ elements high at the nominal PSA location on the detector), the following count rates were observed:

A= 1265 counts/(6500 sec * (26/404)*8.5 cm^2) = 0.356 cts/s/cm2

B=1328 counts/(6500 sec * (26/387)*8.5 cm^2) = 0.358 cts/s/cm2

The FUV detector background rate meets the CEI specification.

### NUV Background

To quantify the NUV detector intrinsic background, two exposures were taken in Appendix B with no light incident on the detector. The first test (CSIL03271070834) was a 300 sec ACCUM image, while the second test (CSIL03264141459) was a 6500 sec TIME-TAG image. Figure 4.11-3 shows the combined NUV dark image. The total number of counts in the image is 18221. The maximum number of counts in any pixel was 3 (only 1 pixel at [X,Y]=[146,141]).  The average count rate over the entire detector was 2.68 counts/s. The count rate per pixel (p) was measured at 2.56E-06 counts/s/p, or by area, 0.409 counts/s/cm2.

Figure 5.11-3: Background image of the NUV detector.  The detector has a background count rate of 2.7 cps.

#### 2006 NUV Background Results

The CEI specification for the NUV channel is a background rate of  < 4E-6 counts/pixel/sec (0.64 counts/sec/cm^2) over the science region of the detector. The area of the NUV MAMA is 2.56 x 2.56 cm, or 6.5536 cm^2. A 6500 second ACCUM exposure (CSIL06334130410) with no light incident on the detector was obtained to verify the dark count rate of the NUV channel. This exposure showed 22280 counts (3.3E-6 counts/sec/pixel, or 0.523 counts/s/cm^2) uniformly distributed across the detector. A 299 second time-tag dark exposure (CSIL06335154046) contained 994 counts (3.2e-06 counts/sec/pixel, or 0.507 counts/s/cm^2). The NUV detector background rate meets the CEI specification.

## Calibration Subsystem

### CEI Requirements

Section 4.3.2 of the CEI lists the basic requirements of the on-board calibration subsystem.  This includes redundant wavelength calibration and flat fielding lamps.

### Description

The count rates for the various channel configurations, lamps, and lamp currents were measured from a variety of tests conducted during Appendix A and B in 2003.  In all cases the full detector count rate was measured and the data was not background subtracted.

Tests:	Appendix A, Tests 200, 300, and 325

Appendix B, Tests 1160, 1170, 1180, 1190, 1110, and 1120

### Wavelength Calibration Lamp Count Rates

Table 5.12-1: FUV wavelength lamp count rates.

| Grating/c | Measured Count Rate (Segment A/Segment B) |
| --- | --- |
|  | LO | MED | HIGH |
|  | Line 1 | Line 2 | Line 1 | Line 2 | Line 1 | Line 2 |
| G130M/1291 | - | - | 250/150 | - | - | - |
| G130M/1300 | - | - | 250/150 | - | - | - |
| G130M/1309 | - | - | 240/170 | 140/90 | - | - |
| G130M/1318 | - | - | 250/200 | - | - | - |
| G130M/1327 | - | - | 250/220 | - | - | - |
| G160M/1577 | - | - | 250/680 | - | - | - |
| G160M/1589 | - | - | 250/720 | - | - | - |
| G160M/1600 | - | - | 240/700 | 200/350 | - | - |
| G160M/1611 | - | - | 300/700 | - | - | - |
| G160M/1623 | - | - | 300/700 | - | - | - |
| G140L/1105 | - | - | 980/ - | - | - | - |
| G140L/1230 | 230/ - | 55/ - | 910/ - | 490/ - | - | - |

Table 5.12-2: NUV wavelength lamp count rates.

| Grating/c | Measured Count Rate (Line1/Line2) |
| --- | --- |
|  | LO | MED | HIGH |
| G185M/1786 | - | 225 | - |
| G185M/1817 | - | 325 | - |
| G185M/1835 | - | 255 | - |
| G185M/1850 | - | 170/150 | - |
| G185M/1864 | - | 200 | - |
| G185M/1882 | - | 240 | - |
| G185M/1890 | - | 240 | - |
| G185M/1900 | - | 320 | - |
| G185M/1913 | - | 300 | - |
| G185M/1921 | - | 390 | - |
| G185M/1941 | - | 330 | - |
| G185M/1953 | - | 260 | - |
| G185M/1971 | - | 200 | - |
| G185M/1986 | - | 250 | - |
| G185M/2010 | - | 300 | - |
| G225M/2186 | - | 390 | - |
| G225M/2217 | - | 250 | - |
| G225M/2233 | - | 350 | - |
| G225M/2250 | - | 360/310 | - |
| G225M/2268 | - | 330 | - |
| G225M/2283 | - | 390 | - |
| G225M/2306 | - | 340 | - |
| G225M/2325 | - | 300 | - |
| G225M/2339 | - | 360 | - |
| G225M/2357 | - | 460 | - |
| G225M/2373 | - | 415 | - |
| G225M/2390 | - | 570 | - |
| G225M/2410 | - | 340 | - |
| G285M/2617 | - | 710 | - |
| G285M/2637 | - | 670 | - |
| G285M/2657 | - | 870 | - |
| G285M/2676 | - | 550 | - |
| G285M/2695 | - | 630 | - |
| G285M/2709 | - | 670 | - |
| G285M/2719 | - | 800 | - |
| G285M/2739 | - | 540 | - |
| G285M/2850 | - | 630/615 | - |
| G285M/2952 | - | 610 | - |
| G285M/2979 | - | 340 | - |
| G285M/2996 | - | 400 | - |
| G285M/3018 | - | 430 | - |
| G285M/3035 | - | 580 | - |
| G285M/3057 | - | 790 | - |
| G285M/3074 | - | 380 | - |
| G285M/3094 | - | 330 | - |
| G230L/2635 | 450/60 | 2170 | - |
| G230L/2950 |  | 2220 | - |
| G230L/3000 | 560/105 | 2250 | - |
| G230L/3360 | 410/70 | 1720/1500 | 5020/3230 |
| TA1 | 2460/465 | - | - |
| TA1BRT | 190/35 | - | - |

### Flat Field Lamp Count Rates

Table 5.12-3: FUV flat field lamp count rates (events/second).

| Grating/c | Measured Count Rate (Segment A/Segment B) |
| --- | --- |
|  | LO | MED | HIGH |
|  | Flat 1 | Flat 2 | Flat 1 | Flat 2 | Flat 1 | Flat 2 |
| G130M/1309 | 7600/- | 6700/- | 14100/- | 11800/- | - | - |
| G160M/1600 | -/11600 | -/10500 | -/19200 | -/19500 | - | - |

Table 5.12-4: NUV flat field lamp count rates (events/second).

| Grating/c | Measured Count Rate |
| --- | --- |
|  | LO | MED | HIGH |
|  | Flat 1 | Flat 2 | Flat 1 | Flat 2 | Flat 1 | Flat 2 |
| G185M/1850 | - | 490 |  |  |  | 1400 |
| G225M/2250 | 480 | 320 |  |  |  |  |
| G285M/2850 | 120 | 65 |  |  |  |  |

The data above were collected in July 2003 during Appendix A testing (see tests 200 and 250).  During Appendix B it was noted that the count rates appeared to be dropping.  this was found by evaluating the count rates observed during four Repeatibility Monitors (Test 850).  The table below shows the dates, sequence of tests, and observed count rates during interspersed repeatability monitor tests.

Table 5.12-5: Flat field lamp usage in 2003.

|  |  | Flat #2/ HI | Flat #1/MED | Flat #1/LOW |
| --- | --- | --- | --- | --- |
| Date | Test # & Comments | G185M | G130M-A | G160M-A |
| 9/25,26/2003 | 1750–NUV internal flats 1&2 |  |  |  |
| 10/2/2003 | 2515-NUV flat NCM1 |  |  |  |
| 10/9/2003 | 850-#1 | 1373 | 10485 | 9387 |
| 10/11/2003 | 1700-FUV internal flat (6 hrs) |  |  |  |
| 10/13/2003 | 850#2 | 1359 | 9913 | 8984 |
| 10/13/2003 | 3000-FUV internal flat (6 hrs) |  |  |  |
| 10/15/2003 | 850-#4 | 1350 | 9594 | 8763 |
| 10/15/2003 | 1720-FUV offset flat field |  |  |  |
| 10/16/2003 | 850-#5 | 1339 | 9344 | 8598 |

This table shows that there is ~0.5% decrease in lamp intensity per hour of use.  In total the lamps lost ~10% of their flux during Appendix B testing.  Flat #2 has not had as much use as Flat #1 and therefore has not suffered the same loss in brightness.  This should be kept in mind during flat field planning on orbit.

Table 5.12-6 gives the total usage of the COS flight lamps as of June 2008.  It does not include the initial lamp evaluation period, which adds roughly five hours to each lamp total.

Table 5.12-6: Total usage of COS flight lamps prior to launch.

|  | PtNe #1 (hrs) | PtNe#2 (hrs) |
| --- | --- | --- |
| LOW | 18.0 | 14.9 |
| MED | 112.4 | 54.0 |
| HIGH | 34.8 | 5.5 |
|  | D2 #1 (hrs) | D2 #2 (hrs) |
| LOW | 14.9 | 4.5 |
| MED | 23.4 | 0.9 |
| HIGH | 42.0 | 17.9 |

## Operational Parameters

### FUV

#### Nominal Stim Locations

Table 5.13-1 gives the nominal stim locations for detector segment A.  The final values for the stim locations for both detector segments is given in COS-03-0090, “Generating the COS Reference Files.”

#### Table 5.13-1: Stim locations for FUV detector segment A.

| Stim Locations, Segment A |
| --- |
| Left hand stim location, DISP direction | Sx1 | 383 |
| Left hand stim location, X-DISP direction | Sy1 | 33 |
| Right hand stim location, DISP direction | Sx2 | 15994 |
| Right hand stim location, X-DISP direction | Sy2 | 984 |

#### Geometric Distortion Map

The geometric distortion of the FUV02 detector was measured during Appendix B Test 2730.  A full description of the derivation of the geometric distortion map is presented in COS-03-0090, “Generating the COS Reference Files.”

#### Location of Spectra

These tables present the locations of the spectra in units of pixels from 2003 data.  In all cases the location of spectrum is described using a linear function of the form, y = mx + b.

Table 5.13-2: Locations of FUV spectra in 2003 thermal vacuum testing.

| PSA Spectral Constants |
| --- |
|  |  | G130M | G160M | G140L |
| Detector Segment |  | A | B | A | B | A | B |
| Slope (x10-5) | m | 0.379 | 5.08 | -5.92 | -0.885 | 10.0 | - |
| y-intercepts |  |  |  |  |  |  |  |
| Spectrum | b | 483.8 | 543.4 | 478.3 | 537.1 | 489.2 | - |
| Background region 1 | bbk1 | 547.8 | 607.4 | 542.3 | 601.1 | 553.2 | - |
| Background region 2 | bbk2 | 419.8 | 479.4 | 414.3 | 473.1 | 425.2 | - |
| Spectrum extraction half height | n | 64 | 64 | 64 | 64 | 64 | 64 |
| Background extraction half height | n2 | 64 | 64 | 64 | 64 | 64 | 64 |
| Background extraction width | w | TBD | TBD | TBD | TBD | TBD | TBD |

| WCA Spectral Constants |
| --- |
|  |  | G130M | G160M | G140L |
| Detector Segment |  | A | B | A | B | A | B |
| Slope (x10-5) | m | 5.05 | 7.54 | -0.312 | -0.283 | 19.2 | - |
| y-intercept | b | 587.9 | 647.0 | 582.2 | 640.4 | 595.8 | - |

### NUV

#### Location of Spectra

These tables present the location of the relevant spectra in pixels from 2003 data.  In all the cases the locations of the spectral stripes are described using a linear function of the form,

x = my + b.

Table 5.13-3: Location of NUV spectra in 2003 thermal vacuum testing.

| PSA Spectral Constants |
| --- |
|  |  | G185M | G225M | G285M | G230L |
| Slope |  |  |  |  |  |
| Spectrum A | ma | -0.00420 | -0.000925 | -0.00386 | -0.00143 |
| Spectrum B | mb | -0.00479 | -0.00137 | -0.00374 | -0.00224 |
| Spectrum C | mc | -0.00559 | -0.00304 | -0.00542 | -0.00591 |
| y-intercepts |  |  |  |  |  |
| Spectrum A | ba | 845 | 859 | 833 | 857 |
| Spectrum B | bb | 749 | 754 | 737 | 754 |
| Spectrum C | bc | 617 | 613 | 604 | 614 |
| Background region 1 | bbk1 | 950 | 950 | 950 | 950 |
| Background region 2 | bbk2 | 150 | 150 | 150 | 150 |
| Spectrum extraction half height | n | 32 | 32 | 32 | 32 |
| Background extraction half height | n2 | 32 | 32 | 32 | 32 |
| Background extraction width | w | TBD | TBD | TBD | TBD |

| WCA Spectral Constants |
| --- |
|  |  | G185M | G225M | G285M | G230L |
| Slope |  |  |  |  |  |
| Spectrum A | ma | -0.00612 | 0.000544 | -0.00294 | -0.00137 |
| Spectrum B | mb | -0.00445 | -0.00197 | -0.00284 | -0.00261 |
| Spectrum C | mc | -0.00507 | -0.00254 | -0.00331 | -0.00191 |
| y-intercepts |  |  |  |  |  |
| Spectrum A | ba | 467 | 487 | 459 | 486 |
| Spectrum B | bb | 373 | 384 | 363 | 384 |
| Spectrum C | bc | 242 | 244 | 233 | 246 |

### Target Acquisition

See Appendix 5.4 for detailed calibration results regarding target acquisition.

# Appendix

## 2003 Calibration Planning

| test | test | day | date |
| --- | --- | --- | --- |
| number | name | completed |  |
|  | RASCAL tip/tilt adjustment for COS | Sat/Sun | 9/20/2003 |
|  | RASCAL tip/tilt for PMT | Sun | 9/21/2003 |
|  | Tom's flaming doughnut | Sun | 9/21/2003 |
| 50 | TA1 aperture scan | Sat/Sun | 9/20/2003 |
| 50 | TA1 Focus Sweeps | Mon | 10/20/2003 |
| 50 | TA1 Focus Sweeps | Tues | 10/21/2003 |
| 60 | NUV focus sweeps, TA1 | Sat/Sun | 9/21/2003 |
| 65 | NUV focus sweeps, grating | Sun | 9/21/2003 |
| 66 | G185M, G225M, G230L focus sweeps | Tue | 9/23/2003 |
| 70 | FUV focus sweeps | Thur | 10/9/2003 |
| 850 | Repeatability monitor #1 | Thur | 10/09/03 |
| 850 | Repeatability Monitor #2 | Mon | 10/13/2003 |
| 850 | Repeatability monitor #3 | Wed | 10/15/2003 |
| 850 | Repeatability monitor 4 | Thur | 10/16/2003 |
| 1110 | FUV CDS Pt-Ne Group 1 | Mon | 10/13/03 |
| 1120 | FUV CDS Pt-Ne Group 2 | Mon | 10/13/03 |
| 1155 | NUV G185M CDS Pt-Ne Spectra in N2 | Tues | 10/21/2003 |
| 1156 | NUV G225M CDS Pt-Ne Spectra in N2 | Wed | 10/22/2003 |
| 1160 | NUV CDS Pt-Ne G185M | Mon | 9/22/2003 |
| 1170 | NUV CDS Pt-Ne G225M | Tue | 9/23/2003 |
| 1180 | NUV CDS Pt-Ne G285M | Tue | 9/23/2003 |
| 1190 | NUV CDS Pt-Ne G230L | Tue | 9/23/2003 |
| 1210 | FUV G130M sensitivity | Sat | 10/11/03 |
| 1220 | FUV G160M sensitivity | Sat | 10/11/03 |
| 1230 | FUV G140L sensitivity | Sat | 10/11/03 |
| 1240 | FUV sensitivity with QE grid off | Sat | 10/11/03 |
| 1250 | NUV G185M sensitivity | Mon | 9/22/2003 |
| 1255 | G185M/G225M sensitivity | Wed | 9/24/2003 |
| 1260 | NUV G225M sensitivity | Sun | 9/21/2003 |
| 1265 | G225M 2nd order sensitivity | Sun | 10/12/03 |
| 1270 | NUV G285M sensitivity | Sun | 9/21/2003 |
| 1280 | NUV G230L sensitivity | Mon | 9/22/2003 |
| 1290 | NUV TA1 sensitivity | Mon | 9/22/2003 |
| 1295 | NUV TA1-BRT sensitivity | Mon | 9/22/2003 |
| 1350 | NUV CDS D2 lamp brightness | Thur | 9/25/2003 |
| 1360 | RASCAL tip/tilt adjustments | Thur | 9/25/2003 |
| 1370 | PSA offsets | Thur | 9/25/2003 |
| 1385 | Dry run of NUV flat-field test | Thur | 9/25/2003 |
| 1390 | Refine FCA position | Wed | 9/24/2003 |
| 1410 | TA1 FOV mapping | Fri | 9/26/2003 |
| 1420 | Spiral search | Fri | 9/26/2003 |
| 1430 | Image mode TA centroids | Fri | 9/26/2003 |
| 1433 | NUV TA IMCALs with Mech. Offsets | Sun | 9/28/2003 |
| 1435 | Flooded PSA with Pt-Ne lamp | Sun | 9/28/2003 |
| 1437 | NUV TA flooded aperture with Kr | Thur | 10/16/2003 |
| 1440 | TA image mode target centering | Fri | 9/26/2003 |
| 1450 | TA dispersed mode centroids | Tues | 10/14/2003 |
| 1455 | NUV Dispersed mode TA centroids | Sat | 9/27/2003 |
| 1460 | TA dispersed light phase 4 | Tues | 10/14/2003 |
| 1465 | NUV TA dispersed light phase 4 | Sat | 9/27/2003 |
| 1470 | TA dispersed light phase 5 | Tues | 10/14/2003 |
| 1475 | NUVTA dispersed light phase 5 | Sat | 9/27/2003 |
| 1700 | FUV cal ss flats S/N=30 | Sat | 10/11/03 |
| 1720 | FUV flats aperture offset 2 | Wed | 10/15/2003 |
| 1730 | FUV flats aperture offset 3 | Fri | 10/17/2003 |
| 1750 | NUV cal SS flat-field, S/N = 30 #1 | Thur | 9/25/2003 |
| 1750 | NUV cal SS flat-field, S/N = 30 #2 | Fri | 9/26/2003 |
| 2100 | FUV CO initial spectra | Wed | 10/15/2003 |
| 2110 | FUV scattered light | Thur | 10/16/2003 |
| 2120 | FUV high quality spectra | Thur | 10/16/2003 |
| 2150 | NUV O2 initial spectra | Fri/Sat | 9/27/2003 |
| 2160 | NUV scattered light | Sat | 9/27/2003 |
| 2170 | NUV high quality spectra | Sat | 9/27/2003 |
| 2170 | High S/N O2 spectra | Thur | 10/2/2003 |
| 2250 | NUV spatial resolution | Mon | 9/22/2003 |
| 2300 | FUV grating stability | Sun | 10/12/03 |
| 2305 | FUV grating stability | Sun | 10/12/03 |
| 2306 | G130M Grating Stability #1 | Mon | 10/13/2003 |
| 2306 | G130M Grating Stability #2 | Wed | 10/15/2003 |
| 2307 | FUV stability | Fri | 10/17/2003 |
| 2307 | NUV stability | Mon | 10/20/2003 |
| 2350 | NUV grating stability | Wed | 9/24/2003 |
| 2355 | G285M Stability | Sun | 9/28/2003 |
| 2355 | NUV grating stability | Sun | 10/12/03 |
| 2355 | NUV grating stability | Sun | 10/12/03 |
| 2505 | NUV CDS flat-field, S/N = 30 | Thur/Fri | 9/26/2003 |
| 2506 | NUV flats with CDS D2 lamp | Thur | 10/16/2003 |
| 2515 | NUV Flat-field NCM1 position refinement | Thur | 10/2/2003 |
| 2700 | FUV HV variability | Thur | 10/09/03 |
| 2705 | FUV HV variability | Thur | 10/09/03 |
| 2706 | FUV HV variability | Thur | 10/09/03 |
| 2710 | FUV timing threshold settings | Fri | 10/10/03 |
| 2715 | FUV timing threshold settings | Fri | 10/10/03 |
| 2725 | FUV walk settings | Fri | 10/10/03 |
| 2726 | FUV walk settings | Fri | 10/10/03 |
| 2730 | FUV geometric corrections PSA | Wed | 10/15/2003 |
| 2731 | Geom Corrections PSA 7x7 pinhole | Wed | 10/15/2003 |
| 2735 | Geometrical Correction WCA part | Sun | 10/12/03 |
| 2735 | Geom Corrections WCA | Tues | 10/14/2003 |
| 2740 | FUV dark count rate #1 | Thur | 10/09/03 |
| 2740 | FUV dark count rate #2 | Fri | 10/10/03 |
| 2740 | FUV dark count rate #3 | Sat | 10/11/03 |
| 2740 | FUV dark count rate 3 | Thur | 10/16/2003 |
| 2741 | FUV dark count rate, QE grid off | Mon | 10/13/03 |
| 2745 | NUV dark count rate | Sun | 9/21/2003 |
| 2750 | FUV resolution, QE grid off | Mon | 10/13/2003 |
| 2800 | FUV high local count rate | Sun | 10/12/03 |
| 2805 | FUV high local count rates G160M | Mon | 10/13/2003 |
| 2950 | NUV resolution, FUV offsets | Wed | 9/24/2003 |
| 3000 | FUV Cal SS flats, S/N = 100 | Mon | 10/13/2003 |
| 3300 | FUV BOA throughput & resolution | Sun | 10/12/03 |
| 3310 | NUV BOA transmission & resolution | Wed | 9/24/2003 |
| 3310 | NUV BOA with D2 lamp | Tue | 9/30/2003 |
| 3400 | Side 2 Mechanism Verification | Sat | 10/18/2003 |
| 3500 | FUV OSM1 position checks | Sat | 10/11/03 |
| 3550 | NUV OSM2 Position Checks | Sat | 9/20/2003 |
| 3600 | FUV Accum Check | Fri | 10/10/03 |
| 3650 | NUV Accum Check | Sat | 9/20/2003 |
| 3700 | NUV Efficiency Supplement | Sat | 10/18/2003 |
|  | End of FUV Appendix B calibration tests raising shroud temperature for post-test contamination certification |  |  |

## 2006 Calibration planning

| Test # | Test Name | Date Executed |
| --- | --- | --- |
| 850 | Repeatability monitor | 12/07/06 |
| 1111 | FUV external wavecals group 1 settings | 12/02/06 |
| 1121 | FUV group 2 settings | 12/05/06 |
| 1161 | G185M external wavecals | 11/28/06 |
| 1171 | G225M wavecals | 11/28/06 |
| 1181 | G285M wavecals | 11/28/06 |
| 1191 | G230L wavecals | 11/28/06 |
| 1210 | G130M sensitivity | 12/01/06 |
| 1220 | G160M sensitivity | 11/30/06 |
| 1230 | G140L sensitivity | 12/01/06 |
| 1250 | G185M sensitivity | 11/29/06 |
| 1255 | G185M/G225M crossover | 11/29/06 |
| 1260 | G225M sensitivity | 11/29/06 |
| 1260 | G185M sensitivity #2 | 12/07/06 |
| 1270 | G285M sensitivity | 11/30/06 |
| 1270 | G225M sensitivity #2 | 12/07/06 |
| 1280 | G230L sensitivity | 12/01/06 |
| 1290 | TA1 sensitivity | 11/30/06 |
| 1290 | TA1 sensitivity #2 | 12/07/06 |
| 1295 | TA1-BRT sensitivity | 12/02/06 |
| 1300 | FUV external flat-field S/N=30 | 12/06/06 |
| 1301 | FUV CDS lamp brightness | 12/05/06 |
| 1399 | FUV faint source | 12/06/06 |
| 2250 | NUV spatial resolution | 11/29/06 |
| 2740 | FUV Dark | 12/01/06 |
| 2740 | FUV Dark #2 | 12/05/06 |
| 2745 | NUV Dark | 11/30/06 |
| 3300 | FUV BOA transmission & resolution | 12/02/06 |
| 3310 | NUV BOA transmission & resolution | 12/03/06 |
| 3500 | FUV OSM1 position checks | 11/29/06 |
| 3550 | NUV OSM2 position checks | 11/28/06 |
| 3600 | FUV ACCUM check | 12/02/06 |
| 3650 | NUV ACCUM test | 11/29/06 |
| 5000 | FUV tag-flash demonstration | 12/04/06 |
| 5500 | NUV tag-flash demonstration | 12/04/06 |
| 6000 | Grating efficiency test | 11/29/06 |
| 7000 | NUV Internal Wavecals | 12/07/06 |
| 8000 | NCM1 flat verification | 12/06/06 |
| 9000 | Side Two operations | 12/06/06 |

## Target Acquisition Data

The following parameters and test data were generated by Robert Gillet to support the TA testing during Appendix B.  It is included as part of this document for posterity and because it is not documented anywhere else.

This document describes what target acq flight software parameters (patchable constants) need to be updated as a result of thermal vac testing, and suggests ways for deriving the new values.

| Patchable constant | New Value | Method |
| --- | --- | --- |
| Pcta_XDispIntercept Coeff--for linear map of X-disp coordinates from B seg to A seg. | -3376990 (i.e. -33.76990) but may change ----->>> | Steve Penton looked at the following G130M and G160M images: CSIL03286021646.SDI (G130M PtNe #1 internal) CSIL03286022659.SDI (G130M external) CSIL03268033938.SDI ACTUALLY WE SHOULD USE DATA DAY 284 AND LATER, AFTER THE CSIL03268034546.SDI FUV WALK/TIMING/NOMAB patches and did a least-squares fit of the 4 points (B seg Xdisp center, A seg Xdisp center) to come up with this linear model (where "center" is a Gauss fit). |
| Pcta_XDispSlope Coeff | 97912 (i.e. 0.97912) but may change |  |
| pcta_XImCalTarget Offset--distance from cal image to sci image in NUV TA1 mode. |  | In between Appendix A and Appendix B (July/August...his 8/20/03 email), Steve discovered the 4-pixel dispersion difference between the cal-to-sci offset for TA1 and that for RVMM. Tom wasn't surprised by this (talked to him 8/22/03) and I think we do need to have a different offset for RVMM than we do for TA1 (i.e. make these two constants into arrays and change the software to be smart enough to know which one to use). I may be thinking about this wrong, but an error of 4 pixels on the NUV is about 0.1 arcseconds, since the plate scale is about 25 milli-arcseconds/pixel. I believe the tightest target acq CEI spec is 0.1 arcseconds, which would mean this difference eats up all the error budget--not good. And isn't the dispersion direction the one that really matters for target acq? I think our plan was to look at the cal-to-sci offsets from the 1430 test and determine the offsets for each mode that way. We ran an LTAIMCAL followed by an LTAIMAGE in each of the 4 modes (TA1, RVMM, TA1BOA, RVMMBOA) and the IMCALs tell where it found the internal lamp and the IMAGEs tell where the science was. (Maybe the BOA ones are unnecessary, if there is no chance of a BOA target acq on orbit.) The "flood" images (1435) come into play for these offsets too, but I think their only usefulness will be to verify the accuracy of Tom's centering by determining the center of the PSA from a flood image for that mode and then comparing it to where LTAIMAGE found the external light...not sure what to do with any difference though...it may be the error in determining the center with the flood images will be greater than the difference. Then there was test 1437, which interleaved images of the internal cal lamp with flooded apertures, for the express purpose of measuring the offset. Hmm...is that the data to use? Ok, I'm officially confused. One final thought on these constants: since, in RVMM, there are double images of both the internal lamp and the external science, and we use a median to find the lamp but a moving-box-flux-weighted-centroid to find the science, there is an inherent problem: the cal lamp measured location will be pulled down (a pixel or two?) by the double image, but the science measured location will not be affected by the double image, hence the distance between them will be wrong. However, maybe this is ok, if we use the target acq testing from thermal vac to determine the distance--because that testing would have had that bias built into it. OK, one more final thought: Tom said, at some point during thermal vac, that determining the vector from the cal image to the sci image could be done theoretically by doing a ray-trace model or something, since all we're really doing is imaging the back of the aperture plate, and we know the parameters of the optics and we know the physical distance between the apertures. I don't know if doing this and comparing it to the offsets derived by the above methods makes sense or not. Maybe we would go with the empirical data anyway. |
| pcta_YImCalTarget Offset |  |  |
| pcta_CalTarget Offset[ ][ ]--the distance from the cal stripe to the science stripe, in 10ths of pixels, for each grating, and for PSA vs. BOA. |  | Steve and I started this...he identified some NUV data that would give the X-disp cal-to-sci distance: G230L: BOA: 267 21 26 08 (CSIL03......SDI) PSA: 267 21 38 04 WCA: (there were wavecals with both the above images) G225M: PSA: 266 08 52 44 WCA: ditto above G185M: 271 01 54 30 & 271 02 01 01 (was this second one a BOA?) were there wavecals with these? G285M: PSA I assume: 266 16 56 03, with wavecal FUV gratings: there are tons of these. Suggest using data after day 284 (FUV patches). Of course Steve already did this with Appendix A data so maybe doing it again is redundant. However it hasn't been done on a grating-by-grating basis or PSA/BOA, and maybe it needs to be. Note that we were requesting slews in the 1450 test when we should have been perfectly centered, and if we were perfectly centered, the only other thing I can think of that would cause a slew request is an incorrect offset. |
| pcta_*MilliArcsecsPerPixel*--plate scales |  | I know we have to measure these on orbit but could we do an empirical estimation of the NUV plate scales by taking our flood images (1435 or maybe 1437) and saying that the diameter of the circle is 2.5 arcseconds on the sky, and dividing to get the answer? Probably wouldn't be at all accurate. |

This report describes my verifications of the results of the target acq tests that were run in COS thermal vac / calibration (September & October 2003).

The table shows the dump file and what I verified in the header to ensure that the test was successful.  (I did not go into details about why the data values prove success, but it'll be clear to anyone knowlegdable of target acq who thinks about it.)  Obviously the CCL proc and the test procedures (Appendix A and Appendix B) will be necessary to make complete sense of the testing.

| Test | CCL | Dump file CSIL03...SDI | Verification |
| --- | --- | --- | --- |
| 1420 | TL1420TA12X2FWC | 269145449 | 1st point saw light. LQTAXPOS = -881, i.e. about half of stepsize 1767. LQTADPOS = -880; ditto. LQTADSLW = 3, LQTAXSLW = -1765 LQTAFX01 = 5328; FX02-FX04 < 10. |
| " | " | 269151020 | 2nd point saw light. LQTAXPOS = -881 LQTADPOS = 882 LQTAXSLW = -1765, LQTADSLW = 1766 LQTAFX02 = 5185; others < 10 |
| " | " | 269152449 | 3rd point saw light. LQTAXPOS = 882 LQTADPOS = 882 LQTAXSLW = -1 LQTADSLW = 1765 LQTAFX03 = 5255; others < 10 |
| " | " | 269153449 | 4th point saw light. LQTAXPOS = 883 LQTADPOS = -881 LQTAXSLW = -1 LQTADSLW = 2 LQTAFX04 = 5312; others < 10 |
| " | TL1420TA1RTB | 269154819 | 1st point saw light. LQTAXPOS = -884 LQTADPOS = -884 LQTAXSLW = -1767 LQTADSLW = 0 LQTAFX01 = 5465; others < 25 |
| " | TL1420TA13X3 | 269160250 | 2nd point saw light. LQTAXPOS = 0 LQTADPOS = 1767 LQTAXSLW = 1767 LQTADSLW = 0 LQTAFX02 = 5474; others < 32 |
| " | " | 269161919 | 4th point saw light. LQTAXPOS = 1767 LQTADPOS = 0 LQTAXSLW = 3534 LQTADSLW = -1767 LQTAFX04 = 5465; others <25 |
| " | " | 269163449 | 5th and 7th points saw light. LQTAXPOS = -221 LQTADPOS = -1767 LQTAXSLW = 1546 (+221 = 1767) LQTADSLW = -3534 LQTAFX05 = 4386; LQTAFX07 = 5639; others < 25 (1767*4386 + -1767*5639)/(4386 + 5639) = -220.85 (rounds to -221 and confirms LQTAXPOS) |
| " | " | 269164819 | 9th point saw light. LQTAXPOS = -1767 LQTADPOS = 1767 LQTAXSLW = 0 LQTADSLW = 0 LQTAFX09 = 5814; others < 28 LQTALOCL = 581 |
| 1430 | TL1430IMCAL | 269185520 | LQTAXCOR = 380 LQTAYCOR = 466 No previous images to compare to, but reasonable in that (380, 466) + SW offset (376, 42) = (756, 508) is near Tom's (754, 517) "TA1 center" value. (There is data later that confirms it. Gauss fits on 286153832.SDI, a TA1/LINE1 image, show the cal spot at (377, 463), which is very close to what this phase found.) LQTATOTL = 5402 |
| " | TL1430IMAGE | 269190619 | LQTAMXCR = 752.2 LQTAMYCR = 506 Looking at the image downlinked from this phase, this measured location is right on the center of the image. LQTADXCR = 756 LQTADYCR = 508, matching calculation in row above this one LQTAXSLW = -90 (= x plate scale of -23.5 * 3.8) LQTADSLW = -47 (= y plate scale of -23.55 * 2) |
| “ | TL1430IMCALRVMM | 269191719 | LQTAXCOR = 217 LQTAYCOR = 687 A picture of LINE1 in RVMM later, 286154520.SDI, shows (Gauss fit) the cal spot at (215, 691), which is very close to what this phase found. LQTATOTL = 1404 |
| “ | TL1430IMAGERVMM | 269193549 | LQTAMXCR = 589.8 LQTAMYCR = 726.9 Looking at the image downlinked from this phase, this measured location is right on the top (main) image (RVMM produces a double image). LQTADXCR = 593 LQTADYCR = 729 Reasonably close; will probably need to tweak cal-to-sci offsets a little bit. LQTAXSLW = -76 ( = x plate scale of –23.5 * 3.2) LQTADSLW = -50 ( = y plate scale of –23.55 * 2.1) |
| “ | TL1430IMCAL run before TL1430IMAGEBOA | 269200949 | LQTAXCOR = 380 LQTAYCOR = 461 (reasonably close to previous IMCAL 269185520) |
| “ | TL1430IMAGEBOA | 269201848 | LQTAMXCR = 743 LQTAMYCR = 502 Looking at the image downlinked from this phase, this measured location is right on the bright part of the image (which is a distorted shape due to the BOA). LQTADXCR = 756 LQTADYCR = 503 Reasonably close; may need new cal-to-sci offset for BOA. LQTAXSLW = -305 ( = x plate scale of –23.5 * 13) LQTADSLW = -23 ( = y plate scale of –23.55 * 1) |
| “ | TL1430IMCALRVMM run before TL1430IMAGEBOARVMM | 269202749 | LQTAXCOR = 216 LQTAYCOR = 686 (reasonably close to the previous IMCALRVMM 269191719) |
| “ | TL1430IMAGEBOARVMM | 269203750 | LQTAMXCR = 581 LQTAMYCR = 727.2 Looking at the image downlinked from this phase, this measured location is right on the brightest point of the top image (BOA + RVMM produces a distorted shape plus a double image of that distorted shape) LQTADXCR = 592 LQTADYCR = 728 Reasonably close; will probably have to tweak cal-to-sci offset, if there is any chance of target acq done with the BOA (may need a new, separate offset for this config). LQTAXSLW = -259 ( = x plate scale of –23.5 * 11) LQTADSLW = -18 ( = y plate scale of –23.55 * 0.8) |
| 1433 |  |  | The purpose of 1433 was to find out if mechanism motion was behind the 20 pixel difference I detected in later runs of 1430—therefore 1433 doesn’t need looking at. |
| 1435 |  |  | The purpose of 1435 was to locate the center of the aperture, so that we could confirm that our external source was centered. It was not a target acq test so it doesn’t need looking at here (but may be used for cal-to-offset calculations—although 1437 is probably much better). |
| 1437 |  |  | The purpose of 1437 was to get the cal-to-sci offsets, and does not need verifying here. |
| 1440 | TL1440IMCAL | 270100220 | This was run to show where the cal spot was before moving the aperture. It found: LQTAXCOR = 380 LQTAYCOR = 485 Then we moved the ap mech (+5, +5). The result is in the next row. |
| " | " | 270101719 | LQTAXCOR = 389 5 steps in X * 0.0478 arc-sec-per-step = 0.239 arc-sec 0.239 arc-sec / 0.0235 arc-secs-per-pixel = 10.17 pixels (measured 9 pixels—good) LQTAYCOR = 475 5 steps in Y * 0.0449 arc-sec-per-step = 0.2245 arc-sec 0.2245 arc-sec / 0.02355 arc-secs-per-pixel = 9.53 arc-sec (measured 10 pixels—good) LQTATOTL = 5627 |
| " | TL1440IMAGE | 270102650 | LQTAMXCR = 743.8 LQTAMYCR = 544.7 The sci spot is where it is; it’s not relevant to the success of this test. LQTADXCR = 765 (389 + offset of 376) LQTADYCR = 517 (485 + offset of 42) LQTAXSLW = -499 ( = x plate scale of –23.5 * 21.2) LQTADSLW = 651 ( = y plate scale of –23.55 * -27.7) |
| " | TL1440IMCAL | 270110020 | For this test, the ap mech was (-5, -5) from nominal. LQTAXCOR = 367 (vs. 380 nominal) Same as above: 5 ap X steps is 10.17 pixels (measured 13—reasonable) LQTAYCOR = 494 (vs. 485 nominal) Same as above: 5 ap Y steps is 9.53 pixels (measured 9—good) LQTATOTL = 5616 |
| " | TL1440IMAGE | 270110749 | LQTAMXCR = 743.2 LQTAMYCR = 544.2 Right where it was in the previous. LQTADXCR = 743 (367 + offset of 376) LQTADYCR = 536 (494 + offset of 42) LQTAXSLW = 4 ( = x plate scale of –23.5 * -0.2) LQTADSLW = 192 ( = y plate scale of –23.55 * -8.2) |
| " | TL1440IMCAL | 270111720 | For this test, the ap mech was (+15, 0) from nominal. LQTAXCOR = 409 (vs. 380 nominal) 15 steps is 3 times the 5 step amount, i.e. 30.51 pixels (measured 29—good) LQTAYCOR = 484 (vs. 485 nominal—good) LQTATOTL = 5506 |
| " | TL1440IMAGE | 270112220 | LQTAMXCR = 743.8 LQTAMYCR = 544.1 Right where it was in the previous. LQTADXCR = 785 (409 + offset of 376) LQTADYCR = 526 (484 + offset of 42) LQTAXSLW = -969 ( = x plate scale of –23.5 * 41.2) LQTADSLW = 427 ( = y plate scale of –23.55 * -18.1) |
| " | TL1440IMCAL | 270112819 | For this test, the ap mech was (0, -15) from nominal. LQTAXCOR = 377 (vs. 380 nominal--good) LQTAYCOR = 512 (vs. 485 nominal) 15 steps is 3 times the 5 step amount, i.e. 28.59 pixels (measured 27—good) LQTATOTL = 5426 |
| " | TL1440IMAGE | 270113321 | LQTAMXCR = 743.1 LQTAMYCR = 543.9 Still in the same place! LQTADXCR = 753 (377 + offset of 376) LQTADYCR = 554 (512 + offset of 42) LQTAXSLW = -232 ( = x plate scale of –23.5 * 9.9) LQTADSLW = -238 ( = y plate scale of –23.55 * 10.1) |
| " | TL1440IMCAL | 270113849 | For this test, the ap mech was (-10, +20) from nominal. LQTAXCOR = 358 (vs. 380 nominal) 10 steps is 2 times the 5 step amount, i.e. 20.34 pixels (measured 22—good) LQTAYCOR = 446 (vs. 485 nominal) 20 steps is 4 times the 5 step amount, i.e. 38.12 pixels (measured 39—good) LQTATOTL = 5443 |
| " | TL1440IMAGE | 270114350 | LQTAMXCR = 744.6 LQTAMYCR = 545.5 Science still nearly in the same place. LQTADXCR = 734 (358 + offset of 376) LQTADYCR = 488 (446 + offset of 42) LQTAXSLW = 250 ( = x plate scale of –23.5 * -10.6) LQTADSLW = 1355 ( = y plate scale of –23.55 * -57.5) |
| " | TL1440IMCAL | 270114849 | For this test, the ap mech was (+15, -26) from nominal. LQTAXCOR = 409 (vs. 380 nominal) 15 steps is 3 times the 5 step amount, i.e. 28.59 pixels (measured 29—good) LQTAYCOR = 533 (vs. 485 nominal) 26 steps in Y * 0.0449 arc-sec-per-step = 1.1674 arc-sec 1.1674 arc-sec / 0.02355 arc-secs-per-pixel = 49.57 arc-sec (measured 48—good) LQTATOTL = 5413 |
| " | TL1440IMAGE | 270115319 | LQTAMXCR = 743.2 LQTAMYCR = 543.3 Still in the same place. LQTADXCR = 785 (409 + offset of 376) LQTADYCR = 575 (533 + offset of 42) LQTAXSLW = -983 ( = x plate scale of –23.5 * 41.8) LQTADSLW = -746 ( = y plate scale of –23.55 * 31.7) |
| 1450 | TL1450G140LCALMEAN | 287142901 | LQTAXCOR = 568.1 (right about where Tom said it would be) LQTATOTL = 17014 |
| “ | TL1450G140LPKXDMEAN | 287143731 | LQTAMXCR = 479.5 (right about where Tom said it would be) LQTADXCR = 484.8 ( = 568.l + offset of –83.3) Apparently our cal-to-sci offset is off a bit (or we’re not all that well centered…but we assume Tom got us perfectly centered)—likely a new set of offsets will come out of this data. LQTAXSLW = 550 ( = x plate scale of 104.82 * 5.3…remember that the MXCR and DXCR values above are reported in tenths, but the software keeps all significant digits when it does calculations, so while 104.82 * 5.3 = 555, this is within acceptable error. . . .05 error in each of the subtraction terms makes 0.1 error; multiplied by 104.82 makes for a max error 10.482) |
| “ | TL1450G140LCALMED | 287145002 | LQTAXCOR = 567 (near where we found it with the mean, above) LQTATOTL = 16759 |
| “ | TL1450G140LPKXDMED | 287145731 | LQTAMXCR = 479 (near where we found it with the mean, above) LQTADXCR = 483.7 LQTAXSLW = 493 ( = x plate scale of 104.82 * 4.7) |
| “ | TL1450G130MCALMEAN | 287150702 | LQTAXCOR = 563.5 (right about where Tom said it would be) LQTATOTL = 11023 |
| “ | TL1450G130MPKXDMEAN | 287151902 | LQTAMXCR = 480.4 (near where Tom said it would be) LQTADXCR = 480.2 ( = 563.5 + offset of –83.3) Very nice—right on! LQTAXSLW = -21 ( = x plate scale of 104.82 * -0.2) |
| “ | TL1450G130MCALMED | 287152400 | LQTAXCOR = 564 (near where we found it with the mean, above) LQTATOTL = 10785 |
| “ | TL1450G130MPKXDMED | 287153102 | LQTAMXCR = 482 (near where we found it with the mean, above) LQTADXCR = 480.7 LQTAXSLW = -136 ( = x plate scale of 104.82 * -1.3) |
| 1455 | TL1455G285MCALMEAN | 270122551 | LQTAXCOR = 360.3 (near where Tom said it would be) LQTATOTL = 799 |
| “ | TL1455G285MPKXDMEAN | 270123351 | LQTAMXCR = 728 (within 9 pixels of where Tom said it would be) LQTADXCR = 731.5 ( = 360.3 + offset of 371.2) LQTAXSLW = -84 ( = x plate scale of –23.84 * 3.5) |
| “ | TL1455G285MCALMED | 270124451 | LQTAXCOR = 360 (near where we found it with the mean, above) LQTATOTL = 811 |
| “ | TL1455G285MPKXDMED | 270125251 | LQTAMXCR = 727 (near where we found it with the mean, above) LQTADXCR = 731.2 ( = 360 + offset of 371.2) LQTAXSLW = -100 ( = x plate scale of –23.84 * 4.2) |
| 1460 | TL1460G140LCAL | 287160203 | Ap mech was offset (+5, 0) steps for this test. Previous to this test, 287142901 found the cal stripe at 568.1. LQTAXCOR = 564.8 5 steps in X * 0.0478 arc-sec-per-step = 0.239 arc-sec 0.239 arc-sec / 0.10482 arc-secs-per-pixel = 2.28 pixels (measured 3.3 pixels—good) LQTATOTL = 15912 |
| “ | TL1460G140LPKXD | 287161002 | LQTAMXCR = 479.2 (right about where it was in test 1450, above) LQTADXCR = 481.5 ( = 564.8 + offset of –83.3) LQTAXSLW = 238 ( = x plate scale of –104.82 * 2.3, within 3 pixels—again, the error bars are larger than that) |
| “ | TL1460G140LCAL | 287162433 | Ap mech was offset (+9, 0) steps for this test. LQTAXCOR = 562.8 9 steps is 9/5 * 2.28 = 4.10 pixels (measured 5.3--okay) LQTATOTL = 15573 |
| “ | TL1460G140LPKXD | 287163332 | LQTAMXCR = 479.3 (still in the same place) LQTADXCR = 479.5 ( = 562.8 + offset of –83.3) Yes, we’re almost perfectly at the desired locations, even though we’re offset by 9…but as in 1450 (G140L) above, we are either not centered or the offset is wrong. LQTAXSLW = 14 ( = x plate scale of –104.82 * 0.2, within 7 pixels—within error bar) |
| “ | TL1460G140LCAL | 287164433 | Ap mech was offset (-7, 0) for this test. LQTAXCOR = 571.5 7 steps is 7/5 * 2.28 = 3.19 pixels (measured 3.4—good) LQTATOTL = 17411 |
| “ | TL1460G140LPKXD | 287165202 | LQTAMXCR = 479.4 (still in the same place) LQTADXCR = 488.2 ( = 562.8 + offset of –83.3) LQTAXSLW = 927 ( = x plate scale of –104.82 * 8.8 within error bar) |
| “ | TL1460G130MCAL | 287170301 | Ap mech was offset (+5, 0) for this test. Previous to this test, 287150702 found cal at 563.5. LQTAXCOR = 560.9 As above, 5 steps in X is 2.28 pixels (measured 2.6—good) LQTATOTL = 11217 |
| “ | TL1460G130MPKXD | 287170801 | LQTAMXCR = 480.6 (right about where it was in test 1450, above) LQTADXCR = 477.6 ( = 560.9 + offset of –83.3) LQTAXSLW = -321 ( = x plate scale of –104.82 * 3, within error bar) |
| “ | TL1460G130MCAL | 287171432 | Ap mech was offset (+9, 0) for this test. LQTAXCOR = 558.8 As above, 9 steps is 4.10 pixels (measured 4.7—good) LQTATOTL = 11473 |
| “ | TL1460G130MPKXD | 287172132 | LQTAMXCR = 480.4 (still in the same place) LQTADXCR = 475.5 LQTAXSLW = -515 ( = x plate scale of –104.82 * 4.9, within error bar) |
| “ | TL1460G130MCAL | 287172932 | Ap mech was offset (-7, 0) for this test. LQTAXCOR = 566.5 As above, 7 steps is 3.19 pixels (measured 3—good) LQTATOTL = 11188 |
| “ | TL1460G130MPKXD | 287173502 | LQTAMXCR = 480.7 (still in the same place) LQTADXCR = 483.2 LQTAXSLW = 267 ( = x plate scale of –104.82 * 2.5, within error bar) |
| 1465 | TL1465G285MCAL | 270133020 | Ap mech was offset (+5, 0) for this test. Previous to this test, 270122551 found cal at 360. LQTAXCOR = 370 5 steps in X * 0.0478 arc-sec-per-step = 0.239 arc-sec 0.239 arc-sec / 0.02384 arc-secs-per-pixel = 10.03 pixels (measured 10—good) LQTATOTL = 833 |
| “ | TL1465G285MPKXD | 270140951 | LQTAMXCR = 728 (same place it was found in test 1455 above) LQTADXCR = 741.2 ( = 370 + offset of 371.2) LQTAXSLW = -315 ( = x plate scale of –23.84 * 13.2) |
| “ | TL1465G285MCAL | 270141820 | Ap mech was offset (+9, 0) for this test. LQTAXCOR = 380 9 steps is 9/5 * 10.03 = 18.05 pixels (measured 20—good) LQTATOTL = 847 |
| “ | TL1465G285MPKXD | 270142550 | LQTAMXCR = 728 (still in the same place) LQTADXCR = 751.2 LQTAXSLW = -553 ( = x plate scale –23.84 * 23.2) |
| “ | TL1465G285MCAL | 270143620 | Ap mech was offset (-7, 0) for this test. LQTAXCOR = 349 7 steps is 7/5 * 10.03 = 14.04 pixels (measured 11—ok) LQTATOTL = 741 |
| “ | TL1465G285MPKXD | 270144250 | LQTAMXCR = 728 (still in the same place) LQTADXCR = 720.2 LQTAXSLW = 186 ( = x plate scale –23.84 * -7.8) |
| 1470 | TL1470G140LFWC3 | 287180303 | 3rd dwell point saw light. LQTADPOS = 600 LQTADSLW = 0 LQTAFX03 = 11100; others = 0. |
| “ | TL1470G140LFWC4 | 287181132 | 1st dwell point saw light. LQTADPOS = 0 LQTADSLW = -1200 LQTAFX01 = 11738; others < 3. |
| “ | TL1470G140LFWC5 | 287182032 | 3rd dwell point saw light. LQTADPOS = -599 (pulled a little by the noise at the other points) LQTADSLW = -1799 LQTAFX03 = 11918; others < 9 |
| “ | TL1470G140LFWC7 | 287183132 | 5th and 6th dwell points saw light. LQTADPOS = 900 LQTADSLW = -900 LQTAFX05 = 12070; LQTAFX06 = 12091; others < 23. (12070* 600 + 12091*1200) / (12070 + 12091) = 900.26 rounds to 900. LQTALOCL = 1209 |
| “ | TL1470G130MFWC3 | 287184202 | 3rd dwell point saw light. LQTADPOS = 600 LQTADSLW = 0 LQTAFX03 = 13751; others < 3 |
| “ | TL1470G130MFWC4 | 287185002 | 1st dwell point saw light. LQTADPOS = 0 LQTADSLW = -1200 LQTAFX01 = 13820; others > 6 |
| “ | TL1470G130MFWC5 | 287190303 | 3rd dwell point saw light. LQTADPOS = -599 (pulled a little by the noise at the other points) LQTADSLW = -1799 LQTAFX03 = 13587; others < 11 |
| “ | TL1470G130MFWC7 | 287191402 | 5th and 6th dwell points saw light. LQTADPOS = 899 LQTADSLW = -901 LQTAFX05 = 13389; LQTAFX06 = 13311; others < 47. (13389*600 + 13311*1200) / (13389 + 13311) = 899.12 LQTALOCL = 1338 |
| “ | TL1470G130MRTB | 287192602 | 3rd dwell point saw light. LQTADPOS = 600 LQTADSLW = 0 LQTAFX03 = 14410; others < 52. |
| “ | TL1470G130MRTB | 287193302 | 2nd dwell point saw light. LQTADPOS = -600 LQTADSLW = -1200 LQTAFX02 = 13711; others < 44. |
| 1475 | TL1475G285MFWC3 | 270145551 | 3rd dwell point saw light. LQTADPOS = 600 LQTADSLW = 0 LQTAFX03 = 2836; others = 0. |
| “ | TL1475G285MFWC4 | 270150650 | 1st dwell point saw light. LQTADPOS = 0 LQTADSLW = -1200 LQTAFX01 = 2643; others < 12. |
| “ | TL1475G285MFWC5 | 270152119 | 3rd dwell point saw light. LQTADPOS = -622 (based on the flux log, the shutter must have been open at dwell point #2 as well) LQTADSLW = -1822 LQTAFX02 = 110; LQTAFX03 = 2610; others < 5. (110*-1200 + 2610*-600) / (110 + 2610) = -624.26 (not exactly –622 because of noise at other dwell points) |
| “ | TL1475G285MFWC7 | 270153950 | 5th and 6th dwell points saw light. LQTADPOS = 893 LQTADSLW = -907 LQTAFX05 = 2561; LQTAFX06 = 2439; others < 28. (2561*600 + 2439*1200) / (2561 + 2439) = 892.68 rounds to 893. LQTALOCL = 256 |
| “ | TL1475G285MRTB | 270154751 | 3rd dwell point saw light. LQTADPOS = 600 LQTADSLW = 0 LQTAFX03 = 2447; others < 28 |
| “ | TL1475G285MRTB | 270155520 | 2nd dwell point saw light. LQTADPOS = -600 LQTADSLW = -1200 LQTAFX02 = 2401; others < 29 |

# Text boxes

Figure 2: Signal to noise per resolution element for the data.